## Slide 1: Trigger based uplink adapted transmission
Date: 2023-11-01
Authors:

## Slide 2: Background
A few key features are left out from 802.11be
  Multi-AP, A-PPDU, non-primary channel access, trigger based uplink adapted transmission, distributed RU and so on
  Some of them were proposed in UHR study group again, like multi-AP
  In this contribution, we reconsider the feature-trigger based uplink adapted transmission
  It is promising feature to boost spectrum usage, especially for large bandwidth uplink transmission
  The required change is relative minor

## Slide 3: Problem with trigger based uplink transmission
In [1] and [2], they both mentioned the following issue for trigger based uplink transmission
  The assigned RU/MRU will be wasted if only one portion of it is busy
  Take the following transmission for example, the whole 996+484 tone MRU at the STA 1 will be wasted just because 484 tone RU is busy.
Trigger
160 MHz
STA 1, 996-tone
STA 2, 484-tone
STA 1, 484-tone
Idle
busy
Idle

## Slide 4: Trigger based uplink transmission
For RU/MRU less than 242-tone, this issue can’t be addressed since current CCA is 20 MHz based.
However, for large RU/MRU, the issue mentioned in slide 2 could be addressed.
The suggested way is to allow that the STA respond with the TB PPDU on a few 20 MHz sub-channels of RU/MRU based on CCA results.

## Slide 5: Trigger based uplink transmission
For the following RU/MRU greater than 242-tone, there are many combinations for available RU/MRU that exclude busy 242-tone RU
  Recommend to consider limited combinations, such as when the CCA results for a few 20 MHz sub-channels within RU/MRU are idle.
  On the other hand, keeping the existing TB PPDU format, including same U-SIG for each 20 MHz in a 80 MHz, should be taken into account when the solution is developed.
RU/MRU greater than 242-tone
484+242-tone
996+484-tone
996+484+242-tone
2*996
2×996+484-tone
3×996-tone
3×996+484-tone
4×996-tone
Other RUs: 484-tone and 996 tone

## Slide 6: Summary
In this contribution, we promote the feature-trigger based uplink adapted transmission.
  It could make full use of the available RU within assigned RU/MRU for uplink transmission

## Slide 7: References
[1] 11-20-0413-01-00be-discussion-on-eht-trigger-based-ul-mu
[2] 11-20-1886-01-00be-ru-adaptation-in-tb-ul-mu-transmission

## Slide 8: SP
Do you agree to allow that the STA responds with the TB PPDU to its received Trigger frame on part of the assigned RU/MRU based on CCA results?