## Slide 1: Discussion on general direction of integrated mmWave
Date: 2023-11-01
Authors:

## Slide 2: Background
The following motion [1] was agreed in March 2023
  Form an 802.11 Integrated mmWave Study Group (IMW SG) to develop a Project Authorization Request (PAR) and a Criteria for Standards Development (CSD) for a new 802.11 MAC/PHY amendment which specifies carrier frequency operation between 42.5 and 71 GHz and leverages MAC/PHY specifications in the Sub 7 GHz bands
  The target start date of the Study Group is November 2023
Integrated mmWave [2-5] is pretty promising for the whole Wi-Fi industry
  Perfectly cater for the new use cases, such as fiber to the room (FTTR) [3], live steaming in the closed office cubicles.
  Good to frequency reuse with a large bandwidth in enterprise/dense deployments.
  Point out a long-term Wi-Fi evolutional roadmap given that there is no light house feature in UHR.
  Open path to commercialize new features/applications, such as ranging and sensing.
  In this contribution, we discuss the general direction of integrated mmWave

## Slide 3: Leverages MAC/PHY specifications in the Sub 7 GHz
Before we proposed to reuse sub 7GHz PHY in [3] together other contributions [5-9]
  Upclock current sub 7GHz PHY by X times such that to increase subcarriers space and keep single PHY mode-OFDM
  Configure the channel width by taking into current support channel width in sub 7GHz and its evolution tendency
  Reuse Sub 7 GHz PHY modules as much as possible, like FFT size, tone mapper/interleaver, coding, MCS and so on
  …
  Beside the items mentioned above, we should make sure that hardware/computing resource does not require great-leap-forward increment
  The supported bandwidth should be decreased, no longer starts with 2.16GHz since it involves filter, ADC/DAC, sampling rate and so on
  Non-contiguous channel bonding should not be allowed

## Slide 4: Leverages MAC/PHY specifications in the Sub 7 GHz
Given the maximum mandatory support bandwidth (80 MHz) in sub 7 GHz and its steady evolution.
  Recommend 80/160 MHz as minimum bandwidth in mmWave band.
  80 MHz is preferred at the client side given that lots of current clients still support 80 MHz at most, and 160 MHz is preferred at the AP side; Doubling their corresponding sizes is also ok
  MAC components in sub 7 GHz should also be reused as much as possible, those from 802.11ad/ay should not be inherited if they are covered by sub 7GHz MAC
  Discovery procedure
  BSS operation, including static puncture for radar coexistence
  Association/multi-link setup
  Acknowledgement procedure
  Power management
  Sounding operation
  …

## Slide 5: Integrated mmWave with MLO
There is no mmWave band only device.
Thanks to the key feature-MLO in 802.11be, this feature should be incorporated in integrated mmWave design
  Mitigate power consumption with only one awake sub 7GHz link in monitoring status
  Address the blockage issue of mmWave band with the help of a sub 7GHz link.
With MLO, control PHY should not be taken into account. Instead, most control/management frames are moved to Sub 7GHz.
  Control PHY decreases the data rate significantly, resulting in low spectrum usage.
  Additional mode of control PHY adds complexity to the implementation.
  With MLO, beam training procedure should also be tuning, e.g., reusing sounding procedure.

## Slide 6: Backward compatibility and coexistence
In 802.11ad/ay, the minimum bandwidth is 2.16 GHz, however, in 802.11aj, the minimum bandwidth is 540 MHz.
According to the passed motion shown in slide 2, integrated mmWave design should take both 45 GHz and 60GHz into account . Moreover, integrated mmWave design should also be unified for them, including channelization (if regulation allows)
Given current status of commercial products about 802.11ad/ay/aj, only energy detection is needed for coexistence with legacy IEEE 802.11 ad/ay/aj and backward compatibility should be waived in order to reduce the burden and complexity
  Channelization for integrated mmWave should also not take the configuration of channel in 802.11ad/ay/aj into account, and could be fully redesigned.

## Slide 7: Other thought
Agree to [6] and [7], SU only transmission is preferred, and MU transmission should be moved to next gen of this IMMW
  MU transmission includes both OFDMA and MU-MIMO.
  SU-MIMO should not be excluded given its high data rate, although it has some complexity to some extent.
  2 spatial streams is preferred from the aspect of practical scenarios. Other numbers could also be ready from the aspect of standard draft.

## Slide 8: Summary
In this contribution, we suggest the following guidelines for IMMW
  Reuse PHY and MAC in sub 7GHz as much as possible
  MLO architecture with at least one sub 7GHz link should be incorporated
  Backward compatibility in mmWave band should not be considered

## Slide 9: References
[1] 11-23-0481-02-0uhr-imw-sg-formation-motion-text
[2] 11-22-0030-01-0wng-look-ahead-to-next-generation
[3] 11-22-1083-01-0wng-next-generation-sg-formation
[4] 11-22-0046-01-0wng-next-generation-after-802-11be
[5] 11-22-0729-01-0wng-next-generation-after-802-11be-follow-up
[6] 11-22-1595-01-0uhr-some-questions-to-answer-in-the-sg
[7] 11-22-1872-00-0uhr-considerations-on-phy-designs-for-mmwave-band
[8] 11-22-1395-00-0uhr-thoughts-on-high-frequency-band
[9]11-23-0066-02-0uhr-thoughts-on-utiliizing-mmwave