## Slide 1: UHR Seamless Roaming for Multi-link Device
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Jian Zhang | Ruijie Networks Co., Ltd. |  |  | zhangjian3@ruijie.com.cn
Danyang Hong | Ruijie Networks Co., Ltd. |  |  | hongdanyang@ruijie.com.cn
Jianxiang Chen | Ruijie Networks Co., Ltd. |  |  | chenjianxiang@ruijie.com.cn
Date: 2023-10-25
Authors:

## Slide 2: Abstract
Introduction
Roaming Model
Access process
Seamless Roaming procedure
Roaming Frame Format Extension
Conclusion

## Slide 3: Introduction
It takes the non-AP STA a long time to do the 802.1X re-authentication and 4-way handshake for the traditional roaming scheme. This may lead to packet loss or even transmission interruption during roaming time for the single-link device.
The 802.11be (EHT) standard has introduced multi-link operation (MLO) [1], and a non-AP STA multi-link device (MLD) can communicate with AP MLD over a plurality of links. However, the non-AP STA MLD spends a lot of time on the re-authentication and re-association for the fast transition (FT) roaming, and it can’t ensure the continuity of data transmission.
We discuss the seamless roaming scheme for UHR non-collocated AP MLD. This scheme fully utilizes the advantages of MLO to saving time and ensuring the continuity of data transmission.

## Slide 4: Roaming Model
The UHR non-AP STA MLD associates with the collocated AP MLD with the wire or wireless backhaul. The UHR AP UMAC can use the backhaul links to manage LMAC and PHY of the collocated EHT AP MLD.
During the access process, PTK and GTK are generated using the UHR AP MLD UMAC address and EHT AP MLD LMAC Address, respectively. To achieve the seamless roaming, the PTK will be shared in non-collocated AP MLDs for the non-AP STA MLD, and the non-AP STA MLD stores the GTKs for all the AP MLDs.
Seamless roaming mechanism: the non-AP STA MLD selects one of the links (e.g. STA Link0) to disconnect from the original AP MLD(e.g. EHT AP MLD1 Link0) and then connects this link (STA Link0) to the new AP MLD (e.g. EHT AP MLD2 Link0). The other links of non-AP STA MLD remain connected to the original AP until the connection with the new AP MLD is finished.
Roaming Frame Format Extension: the roaming frame has been extended to advertise seamless roaming capability, invoke seamless roaming, grant seamless roaming, and confirm completion of roaming link handover.
Non-collocated AP MLD[2]
Non-AP STA MLD

## Slide 5: Access Process
The PTK is generated using the UHR AP MLD UMAC address and Non-AP STA MLD UMAC address through the EAPOL-Key frame (data type MAC address KDE). The UHR AP MLD UMAC stores the PTK for non-AP STA MLD, and PTK is shared in the AP MLDs belonging to the same UHR AP MLD UMAC to achieve the later seamless roaming.
GTK, IGTK and BIGTK are generated using the EHT AP MLD LMAC Address. The all EHT AP MLDs belonging to the same UHR AP MLD sends their GTK, IGTK, BIGTK to the non-AP STA MLD, and the non-AP STA MLD stores these keys.
In the access process, the non-AP MLD and UHR AP MLD negotiate the unicast and multicast keys for all links of MLDs. The unicast key is shared in the non-collocated AP MLDs which are connected to the same UHR AP MLD UMAC. The non-AP STA MLD stores the all multicast keys for the non-collocated AP MLDs. The non-AP STA MLD does not need the re-authentication, re-association, and 4-way handshake, and the non-AP STA MLD directly switches the target link to reduce the authentication delay caused by FT roaming.

## Slide 6: Access Process: Key Design
The multicast key (GTK, IGTK and BIGTK) are generated using the low MAC address of each link on the AP side. For 4-way handshake, we need to expand the content of EAPOL-Key KDE (GTK KDE, IGTK KDE, BIGTK KDE) and FTE Filed (MLO GTK, MLO IGTK, and MLO BIGTK) for the FT protocol.
EAPOL-Key KDE Field Extension
FTE Field Extension
Add AP MLD ID field to identify the different AP MLDs.

## Slide 7: Seamless Roaming Procedure (I)
① Suppose the following associations during the access process : non-AP STA MLD Link0– AP MLD1 Link0, non-AP STA MLD Link1– AP MLD1 Link1;
② The non-AP STA MLD decides to roam according to the current link state.
③ In the overlapping area of signal coverage, the non-AP STA using its all links one bye one send the probe request to the adjacent AP MLDs (e.g. AP MLD2) which are connected to the same UHR AP MLD UMAC. The AP MLD2 replies the probe response from the non-AP STA MLD (probe response).
④ The non-AP STA evaluates the signal quality of the probe response for each link, and decides the roaming target AP (e.g. AP MLD2). At this step, non-AP STA also determines the priority of the link connection to the target AP (e.g. non-AP STA MLD Link 0 – AP MLD2 Link0).

## Slide 8: Seamless Roaming Procedure (II)
⑤ The non-AP STA MLD selects an appropriate link from the associated links and sends the roaming request containing BSS transition management (BTM) roaming request frame to the original AP (e.g. AP MLD1). This frame uses the multi-link configure element to tell the original AP (e.g. MLD1) that the non-AP STA wants to switch from the original link (e.g. MLD1 Link0) to the target link (e.g.MLD2 Link0).
⑥ 1) The original AP (AP MLD1) reports the above roaming request to UHR UMAC, and then UHR UMAC approves or rejects this roaming requests based on the target link status of the target AP and informs the original AP of the results. 2)The original AP (MLD1) sends BTM roaming reconfigure frame to non-AP STA MLD over the corresponding received link. 3)This frame triggers the link reconfiguration of the non-AP STA MLD (e.g. Link0), i.e. STA MLD Link0 – AP MLD2 Link0 STA MLD Link0 - AP MLD1 Link0. 4)The non-AP STA MLD uses the new link to send the BTM roaming confirm frame to AP MLD2, and confirms that this link of the non-AP STA MLD has been successfully reconfigured.
⑦The UHR AP MLD UMAC updates Link0 configuration. The link between the non-AP STA MLD Link0 and AP MLD2 Link0 has the highest priority for the new STA data transmission. Note: non-AP STA MLD Link1 maintains connection and communication with AP MLD1 Link1 at the step ⑥ and ⑦.
⑧ 1) The UHR AP MLD UMAC determines the switching of leftover links. Assuming link reconfiguration: the reconfiguration of non-AP STA Link1 is triggered by BTM roaming reconfigure frame through the existing connection links (e.g. AP MLD1 Link1 or MLD2 Link0 ). 2) The non-AP STA reconfigures the link, i.e. STA MLD Link1 – AP MLD2 Link1 STA MLD Link1 - AP MLD1 Link1. 3) After reconfiguration, non-AP STA sends the BTM roaming confirmation frame to AP MLD2 over the Link1 to confirm the successful reconfiguration.
Finally, all links of non-AP STA MLD complete roaming switching, and non-AP STA only connects and communicates with AP MLD2.

## Slide 9: Roaming Frame Format Extension (I)
UHR Mobility domain element: declaring the seamless transition capability
The UHR mobility domain element is added to the beacon, probe response, association request, association response, and authentication frames to declare the seamless transition capability of the UHR MLD.
Element ID | Length | MDID | ST Capability
1 | 1 | 2 | 1
Octets
The Element ID and Length fields are defined in 9.4.2.1 [3].
The MDID (mobility domain ID) field is an identifier that names a UHR Roaming mobility domain.
The ST Capability field declares the capability of the seamless BSS transitions. The ST Capability field is defined as following,
Seamless BSS Transition Status | Reserved
1 (0/1) | 7
Bits
Seamless BSS Transition Status is set to 1 if the MLD has the capability and is set to 0 otherwise.

## Slide 10: Roaming Frame Format Extension (II)
UHR Mobility domain extension: declaring the seamless transition capability
The beacon frame (Table 9-32 [3]), probe response frame (Table 9-39 [3]), association request frame (Table 9-62 [3]) , Association Response (Table 9-63 [3]), and authentication frame (Table 9-68 [3]) are all modified as follows,
Order | Information | Notes
<Last assigned +1> | UHR Mobility domain | The Ultra High Reliable Mobility Domain element is present if dot11SeamlessBSSTransition Activated is true.

## Slide 11: Roaming Frame Format Extension (III)
BTM roaming frame extension
For seamless roaming, we extend the BTM Roaming frames to exchange the roaming messages including a roaming request (from STA MLD to UHR AP MLD), a roaming link-switch instruction (from UHR AP MLD to STA MLD), and a roaming link-switch confirmation (from STA MLD to UHR AP MLD).
The Category field is defined in table 9-51 in 9.4.1.11 [3], setting to 10 subjected to wireless network management (WNM).
The Dialog Token field is a nonzero value chosen by the STA sending the BTM roaming request frame to identify the request/response transaction.
The Action field is defined in table 9-425 in 9.6.13.1 [3], adding the types as follow,
Category | Action | Dialog Token | Common Info
1 | 1 | 2 | variable
Value | Description
28 | Roaming Request
29 | Roaming Reconfigure
30 | Roaming Confirm
31-255 | Reserved
Octets

## Slide 12: Roaming Frame Format Extension (III)
The Common Info carries the roaming information for the different action frames.
1) The Length field is the length of Common info except for Length field;
2) The MLD AP ID field is the requested ID of AP MLD ;
3) The Links Info field is the ID of the link that STA expects to disconnect from.
--The Links Num field indicates the requesting number of links.
--The Link ID Info field is the ID of Link requesting to disconnect.
4) The Status Code field is a value from the options listed in 9.4.1.9 [3].
5) For STA control field:
--The Link Del Mode field indicates the behavior of the deleting link. Immediately deleted when setting to 0. Waiting for the Link Del Count to delete when setting to 1.
--The Link Del Count field indicates the number of TUs (1024us) to delete the link after receiving the frame.
Length | MLD AP ID | Links Info | Status code | STA control
1 | 1 | variable | 1 | 2
Octets
Common Info
Link Num | Link ID Info | Link ID Info | ….
Link Del Mode | Link Del Count
9.4.1.9 [3]
Roaming Request (from STA MLD to UHR AP MLD)
Roaming Reconfigure (from UHR AP MLD to STA MLD)
Roaming Confirm (from STA MLD to UHR AP MLD)

## Slide 13: Conclusion
The PTK is generated using the UHR AP MLD UMAC address during the access process. The PTK will be shared in non-collocated AP MLDs during the seamless roaming process for the STA MLD. The sharing keys reduces the re-authentication and re-association delay caused by FT roaming.
Seamless roaming mechanism: the STA MLD selects one of the links to disconnect from the original AP MLD(e.g. EHT AP MLD1 Link0) and then connects this link to the new AP MLD. The other links of STA MLD remain connected to the original AP until the connection with the new AP MLD is completed. This seamless roaming method ensures the continuity of data transmission.
Roaming Frame Format Extension: the roaming frame has been extended to declare seamless roaming capability, invoke seamless roaming, grant seamless roaming, and confirm completion of roaming link handover according to MLD characteristics.

## Slide 14: References
[1] Po-Kai Huang, et al. Multi-link Operation Framework, DCN 11-23/0231r0.
[2] Guogang Huang , et al. Thoughts on Seamless Roaming Under Non-collocated AP MLD Architecture, DCN 11-22/1910r1
[3] IEEE Std 802.11™-2020. Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications.