## Slide 1: Multi-Link based Multi-AP Coordination for Low-Latency Traffic
Date: 2023-11-12
Authors:

## Slide 2: Abstract
Multi-link device (MLD) and multi-link operation (MLO) between two MLDs are key features supported in P802.11be Extremely High Throughput (EHT) [1].
In the Project Authorization Request (PAR) of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enhancement, reduce latency, and reduce power consumption for AP, compared to P802.11be EHT MAC/PHY operation [2].
Multi-AP operation (aka. Multi-AP coordination/transmission) has been discussed as one of the key candidate features to meet the requirement of UHR capability.
In this contribution, we propose multi-link-based multi-AP operation with low-latency traffic.

## Slide 3: Recap: Low-Latency Traffic in Multi-Link Devices [3-7]
During multi-link setup, AP MLD may classify traffic between AP MLD and non-AP MLD into one or more categories based on the latency requirements of the traffic.
  e.g., a low latency (LL) category for LL traffic, and a non-low latency (non-LL) category for non-LL traffic.
  In operation, LL traffic may be associated with one or more TIDs associated with one or more predetermined access categories (ACs) or traffic streams.
AP MLD may negotiate with non-AP MLD a traffic identifier (TID) to link mapping to assign traffic streams to available links.
AP MLD may prioritize different links based on the category of traffic.
  e.g., A traffic stream of LL category between AP MLD and non-AP MLD may be mapped to link 2.

## Slide 4: Low-Latency Traffic in Multi-AP Network
AP 2 may transmit a non-LL traffic frame (e.g., data frame conveying non-LL traffic to associated STA2), at the time T1.
Case 1: STA1 associated with AP1 may hear the non-LL traffic frame and may set its NAV at T2.
Problem 1:
  STA 1 may postpone the transmission of a LL traffic frame (e.g., data frame conveying LL traffic, as shown in the figure) at time T3.
  As a result, delay is introduced.

## Slide 5: Multi-AP Coordination based on Link Priority – Solution 1
AP MLD 1 may transmit to AP MLD 2 a management frame informing a priority of link 2 used for LL traffic.
  e.g., AP MLD 2 may have a non-LL frame for transmission.
AP MLD 2 may select between link 1 and link 2 for the transmission of the non-LL frame.
  e.g., based on the priority of link 1 and/or the priority of link 2 specified in the management frame.
AP MLD 2 may transmit a non-LL frame, via link 1, to non-AP MLD 2.
Non-AP MLD 1 may be enabled to transmit a LL traffic frame, via link 2, to AP MLD 1.

## Slide 6: Multi-AP Coordination based on Link Priority – Solution 2
AP MLD 2 may transmit to AP MLD 1 a request frame soliciting a response from AP MLD 1.
In response, AP MLD 1 may transmit to AP MLD 2 a response frame informing a priority of link 2 used for LL traffic. (e.g., AP MLD 2 may have a non-LL frame for transmission.)
AP MLD 2 may select between link 1 and link 2 for the transmission of the non-LL frame, e.g., based on the priority of link 1 and/or the priority of link 2 specified in the response frame.
AP MLD 2 may transmit a non-LL frame, via link 1, to non-AP MLD 2.
Non-AP MLD 1 may be enabled to transmit a LL traffic frame, via link 2, to AP MLD 1.

## Slide 7: Summary
In this contribution, we proposed the methods of multi-link based multi-AP coordination for low-latency traffic.

## Slide 8: References
[1] IEEE P802.11be Draft 4.1
[2] IEEE 802.11-23/0480r3, P802.11bn Project Authorization Request (Draft)
[3] IEEE 802.11-23/0069r1, Considerations on Latency Improvement, 2023-03-27
[4] IEEE 802.11-20/0418r4, QoS management framework in 802.11be, 2020-08-11
[5] IEEE 802.11-19/0163r1, Low latency enhancements for R1, 2020-07-28
[6] IEEE 802.11-20/0697r3, Supporting latency sensitive applications in 11be, 2020-05-28
[7] IEEE 802.11-20/0408r6, Prioritized EDCA channel access over latency sensitive link(s) in MLO, 2020-03-09