## Slide 1: Epoch start time setting
Date: 2023-11-08
Authors:

## Slide 2: Revisions
R0 – Initial Version –
R1 – Addition of slide 13 : Benefits of pseudo random variation (∆t) for Epoch Start Time, and SPs clarification.

## Slide 3: Abstract
In the scope of the RCM, determining the start time of a new Epoch is a key point of the MAC address change mechanism.
Current contribution describes a method to determine the starting time of an Epoch with reduced information exchange, and associated function to compute Privacy Enhancement Parameters.
This contribution covers both Individual Epoch initiated to a single non-AP MLD, and Group Epoch managed by the AP and used for the change of multiple stations at once (potentially all non-AP MLDs on a given BSS).

## Slide 4: MLD TSF counter in 11be (reminder):
TSF counter is sent in each beacon frame
This is a 64bit value indicating time in µs elapsed since the enablement of the Link.
TSF counter may be different between two links of a given MLD STA:
- TSF Offset between links (Toffset) may be sent in the TSF Offset subfield of STA info field of the Basic Multi-Link element, if the TSF Offset Present field of the STA control field is set to 1
- Clock drift between two APs on a given AP-MLD is limited to ±30 μs
Toffset between the TSF timer of the reported AP (TA) and the TSF timer of the reporting AP (TB)
is encoded as a 2s complement signed integer with units of 2 μs.
Toffset is calculated as Toffset= Floor((TA – TB)/2).
Note : for NSTR mobile AP, TSF Offset Present field is always set to 0, but drift between APs shall be limited to 25 µs.

## Slide 5: Variable Group Epoch start boundary computation:
t
GETn=Tn + ∆Tn + RefLink Offset
Tn=TSF counter value of the group Epoch Reference Time number n :
Tn=Tn-1+ GEI, or Tn=T0+(n x GEI)
With n = [(current TSF –T0 – RefLink Offset) / GEI]
∆Tn=PRF-128\64( GTK*, “ERCM”, Tn) mod (Time range)
CPE-Param = PRF-M\L(PTK*, “ERCM”, Tn) [2]
T0
T1
Tn
GET1
GETn
∆T1
∆Tn
Group Epoch start Time is based on a fixed frequency with a limited pseudo random variation.
GEI = Group Epoch Interval
GET= Group Epoch Start Times
Example values :
GEI = 10 minutes
Time Range = 2 minutes
GET0
∆T0
GTK* is derived from the GTK
PTK* is derived from the PTK (KDK)
GEI

## Slide 6: RefLink Offset:
RefLink Offset = offset of the TSF counter of the current link compared to the Reference Link (of id RefLink ID ) with a 2 µs resolution.
T0 is the value of the first reference time for the Epoch on the Reference Link.
Note : If no beacon is received on current link (Multi Link Power save mode), no direct reading of RefLink Offset is available.
In that case, RefLink Offset may be approximated using 2 TSF Offsets fields of the Basic MultiLink info element received on a reporting link :
- TSF Offset field for RefLink in received beacon : TSF OffsetRefLink = Floor((TSFRefLink – TSFReporting)/2).
RefLink Offset = 2 x TSF OffsetRefLink
= 2 x Floor ((TSFRefLink - TSFcurrent )/2)
≈ Floor((TSFRefLink - TSFreporting ) / 2) – Floor((TSFCurrent - TSFReporting )/2)
≈ 2x ( TSF OffsetRefLink – TSF Offsetcurrent )

## Slide 7: Group Epoch start Time
A non-AP MLD receives the Group Epoch parameters from its AP MLD (Epoch initiator) including: GEI = Group Epoch Interval, T0= initial Group Epoch reference Time, a Time Range, and a RefLink Id.
  Epoch parameters (GEI, T0, Time Range, and RefLink Id of the Reference Link used as a time reference), have same value for all links, and are used to determine Epoch start time and non-AP STA CPE parameters
  Epoch parameters can be sent in an encrypted IE, or encrypted frame.
After association,
  each non-AP MLD computes the value n corresponding to the number of Group Epoch elapsed since last TSF reset on its Master Link.
    n = [(current TSF –T0 – RefLink Offset) / GEI]
  Non-AP STA can then determine next Group Epoch reference Time
    Tn+1=T0+ (n+1) x GEI
Before next Group Epoch reference Time, non-AP STA and AP station compute the CPE parameters for the non-AP STA
    CPE_PARAMn+1 = PRF-M\L( PTK*, “ERCM”, Tn+1)
    ∆Tn+1 = PRF-128\64( GTK*, “ERCM”, Tn+1) mod (Time range)
    GETn+1 = Tn+1 + ∆Tn+1 + RefLink Offset

## Slide 8: Variable Individual Epoch boundary computation
t
ITn=TSF value of the Individual Epoch reference time number n :
ITn=ITn-1+ IEI , or ITn=IT0 + (n x IEI)
n = [(current TSF– IT0 - RefLink Offset) / IEI]
IETn=ITn + ∆ITn+ RefLink Offset
(CPE-Paramn, ∆ITn)=PRF-M\L( PTK*, “ERCM”, ITn)
IT0
IT1
ITn
IET1
IETn
∆IT1
∆ITn
IEI = Individual Epoch Interval
IET= Individual Epoch start Times
Example values :
IEI = 3 min
Time Range = 30 sec
IET0
∆IT0
Individual Epoch start Time is based on a fixed frequency with a limited pseudo random variation
IEI

## Slide 9: Individual Epoch start Time
If a non-AP STA (Epoch initiator), requests an individual Epoch management, the non-AP STA negotiates following Epoch parameters with the AP :
  Individual Epoch Interval : IEI
  First Individual Epoch start Time : IET0 (precise time indicated by the STA, ∆T0=0), and associated RefLink ID
  Max duration of Epochs (expressed in iteration): N
    N=0 : Undetermined duration (association life time)
    N=1 : one shot @MAC change
    N>1 : determined duration.
  Note 1: Epoch parameters (EI, IET0 , N, and RefLink ID) are encrypted and not known by other STA
  Note 2: For individual Epoch, IET0=IT0
AP and non-AP STA can then compute future individual epoch reference times.
  n = [(current TSF – IET0) / IEI]
  ITn+1=IET0+ (n+1) x IEI
Before the next individual epoch reference time, the non-AP STA and AP compute at once both future Epoch start time, and associated CPE parameters for the non-AP STA.
    (CPE_PARAMn+1, ∆ITn+1) = PRF-M\L( PTK*, “ERCM”, ITn+1)
    IETn+1=ITn+1 + ∆ITn+1 + RefLink Offset

## Slide 10: Coexistence of Group and Individual RCM
By default, 11bi non-AP STA follows Group Epoch
If a non-AP STA negotiates an Individual Epoch to the AP, the non-AP STA may either:
  Opt1: Only follow Individual Epochs (ignore Group Epochs)
  Opt2: Follow both Individual and Group Epochs.
In case of opt2, additional rules are required to avoid selecting an Individual Epoch start time too close from the Group Epoch start Time.
  Priority should be given to Group Epoch:
    To ensure “mass” effect of group change
    Because it is easier to cancel Individual Epoch change (impact on 1 STA)
  If time between next Individual and Group epoch start time is lower than a TBD time (e,g. 1s), then Individual Epoch is ignore.
    |GETn-IETp| < 1s => IETp is ignored by both AP and non-AP STA and non-AP STA only change its CPE parameters at GETn.
t
T0
T1
Tn
GET1
GETn
GET0
IET0
IET1
IETp
IETp+1

## Slide 11: ERCM regarding Client Privacy Enhancements Requirements [4]
Req ID | Client OTA MAC Address randomization Requirement | Status
6 | 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP | Not addressed at the current stage but compatible
7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection. | Addressed
8 | 11bi shall define a mechanism for a CPE AP to initiate changing the OTA MAC Addresses of a set of associated CPE Client’s in the BSS (those CPE Clients in Associate STA State 4) without any loss of connection | Addressed

## Slide 12: Benefits of Using a Time Reference for CPE parameters generation
The proposed mechanism, to determine the starting of an Epoch and associated CPE parameters based on TSF, is simple and requires no additional mechanism for synchronization (TSF mechanism is enough).
Both AP and non AP STA can compute at any time, CPE parameters. This include CPE parameters currently in use, previous CPE parameters or even future CPE parameters and associated usage time.
Information required for CPE parameters and Epoch boundaries computation requires low overhead since data are sent only once to initiate a series of Epochs.
Proposed mechanism also allows a coexistence of both Individual and Group Epoch

## Slide 13: Benefits of pseudo random variation (∆t) for Epoch Start Time
Individual Epoch:
Simple regular instant of change of CPE parameters is an easily detectable fingerprint of a given non-AP STA.
Adding a pseudo random variation (especially in a large time range), makes the instant of change not precisely predictable and avoids fingerprinting using this mean.
Group Epoch:
With mass rotation, the distribution of the first frame transmission using new MAC address is grouped around the Epoch starting time.
A large number of new MAC addresses will then appear, shortly after the start of the Epoch, that makes it predictable after few iterations.
Obfuscation of this instant of change is necessary to avoid differentiating between a new association and a change of MAC address.

## Slide 14
Straw Poll #1
SP#1 : Do you support that Epoch’s start time of all non-AP STA affiliated to a single non-AP MLD are aligned in time ?
Yes
No
Abstain

## Slide 15
Straw Poll #2
SP#2 : Do you support using a time reference as input for the generation of the CPE parameters of this Epoch ?
Yes
No
Abstain

## Slide 16
Straw Poll #3
SP#3 : Do you support that Group Epoch start Time (GET) is based on a fixed frequency (GEI) with a limited pseudo random variation.
GETn+1=Tn+1 + ∆Tn+1+ RefLink Offset
with :
Tn+1=T0+ ((n+1) x GEI)
∆Tn+1 = PRF-128\64( GTK*, “ERCM”, Tn+1) mod (Time range)
GTK* derived from GTK
RefLink Offset = offset of the TSF counter of the current link compared to the Reference Link.
Yes
No
Abstain

## Slide 17
Straw Poll #4
SP#4 Do you support that CPE Parametres are computed thanks to a unique PRF call using as input parameters: a key derived from the PTK, and the reference starting time of the Epoch, according to the formula:
CPE-Paramn+1=PRF-M\L(PTK*, “ERCM”, Tn+1)
With :
Tn+1=T0+ ((n+1) x EI)
PTK* is derived from the PTK
Yes
No
Abstain

## Slide 18
Straw Poll #5
SP#5 : Do you support that Individual Epoch start Time (IET) is based on a fixed frequency (IEI) with a limited pseudo random variation ∆T.
IETn+1=ITn+1 + ∆Tn+1 + RefLink Offset
with :
ITn+1=IET0+ ((n+1) x IEI)
    (CPE_PARAMn+1, ∆Tn+1) = PRF-M\L( PTK*, “ERCM”, ITn+1)
PTK* is derived from the PTK
RefLink Offset = offset of the TSF counter of the current link compared to the Reference Link .
Yes
No
Abstain

## Slide 19: References
[1] IEEE 802.11-21/1854r1 – Association MAC Address based on AID (A-AMAC)
[2] IEEE 802.11-23/1147r0 -Obfuscation Computation Procedure
[3] IEEE 802.11-21/1539r0 – Rotating MAC Addresses Over the Air
[4] IEEE 802.11-21/1848r7 – Requirements Document
[5] IEEE 802.11-22/0622r7 – EDP – TGbi -Agenda- April 2022