## Slide 1: TGbi – Proposal for coordinated MAC rotation
Date: 2023-11-101
Authors:
Name | Affiliations | Address | Phone | email
D. Ficara | Cisco |  |  | dficara@cisco.com
J. Henry | Cisco |  |  | jhenry@cisco.com
U. Campiglio | Cisco |  |  | ucampigl@cisco.com
J. Contreras | Cisco |  |  | Jacontre@cisco.com

## Slide 2: Background – Epochs and Coordination
Epochs were discussed in 11-23/0873, 11-23/1246 and 11-23/1675. Epochs define time periods at the edge of which a CPE client rotates its otaMAC address
11-23/1675 discusses about individual and mass rotations
Mass rotation – Large Anonymity Set but explicit event
Individual rotation – Anonymity via confusion with STA disconnecting/reconnecting

## Slide 3: A simple definition for anonymity
Simple metric for privacy [1]:
Anonymity Set Size. The anonymity set for an individual u, denoted ASu is the set of users that the adversary cannot distinguish from u. It can be seen as the size of the crowd into which the target u can blend.
In other words, if you hide in the crowd, the bigger the crowd, the better you hide.

## Slide 4: Individual vs Mass rotation
There is interest in proposals where STAs have a specific negotiation (each its own) for epoch.
On the other hand, this reduces the anonymity set size (single element in the crowd) -> may force additional obfuscation mechanisms (e.g., 'pretend auth/assoc')
If N stations rotate their otaMAC at the same time, Anonymity Set Size is N.
If STAs coordinate, the better for everyone (large anonymity set). A STA can decide of a threshold for N beyond which anonymity is good enough, crowd size is large enough.

## Slide 5: Epoch hopping in – Proposal
Define a number of global Epochs, for all STAs in a BSS.
Each of them is a Rotation opportunity Wagon. STAs can choose to hop in or not.
AP declares next Wagon at T=Tx seconds/TUs in protected multicast frame, stating min threshold of #STAs according to AP (NAP )
Before Tx – Dmargin, each STA i declares to AP on its own time if it intends to hop onto next wagon and min threshold Nsta(i)
At Tx – Dmargin, the AP computes subset of STAs whose threshold is satisfied and report set size to all STAs. If |subset| == 0, AP declares next Wagon invalid and won't be executed
  AP can "goto (1)" : declare a new Wagon at T=Ty
Otherwise, all STAs that declared positive intention at (2) and whose threshold is satisfied by the subset size, will perform mass rotation at T=Tx

## Slide 6: Epoch hopping in - example
AP
STA1
STA2
STA3
STA4
STA5
Tx
Tx – Dmargin
Mass rotation
STA1,3,4,5
Epoch with threshold 3, at T=Tx
Hop in, N=4
Anonymity Set Size = 4
Hop in, N=7
Hop in, N=3
Hop in, N=3
Hop in, N=4

## Slide 7: Open Points
Will this be a capability for STAs to be declared?
How to define the threshold?
  Does AP choose it as % of joined #STAs with capability?

## Slide 8: Summary
Discussion on Anonymity Set Size related to Epoch structure
  Pros/Cons of Individual vs Mass rotation
Coordinated rotation proposal
Open points

## Slide 9: References
Technical Privacy Metrics: a Systematic Survey - https://arxiv.org/abs/1512.00327
11-23/0873 Client Frame Tracking Countermeasures
11-23/1246 Proposal for sliding window MAC address rotation
11-23/1675 Epoch structure proposal