## Slide 1: TGbi – Proposal for coordinated MAC rotation
Date: 2024-03-08
Authors:
Name | Affiliations | Address | Phone | email
D. Ficara | Cisco |  |  | dficara@cisco.com
J. Henry | Cisco |  |  | jhenry@cisco.com
U. Campiglio | Cisco |  |  | ucampigl@cisco.com
J. Contreras | Cisco |  |  | Jacontre@cisco.com

## Slide 2: Background – EDP Epochs and Coordination
(EDP) Epochs were discussed in 11-23/0873, 11-23/1246 and 11-23/1675.
11-23/1675 discusses about individual and mass rotations
Mass rotation – Large Anonymity Set
Individual rotation – Anonymity via confusion with STA disconnecting/reconnecting
11-24/222r2: support for group and individual epochs, one-time and periodic

## Slide 3: A simple definition for anonymity
Simple metric for privacy [1]:
Anonymity Set Size. The anonymity set for an individual u, denoted ASu is the set of users that the adversary cannot distinguish from u. It can be seen as the size of the crowd into which the target u can blend.
In other words, if you hide in the crowd, the bigger the crowd, the better you hide.

## Slide 4: Hiding in the Crowd Example (Group Epochs)
time
MAC 1
MAC n
MAC 2
…
MAC 3
MAC n+1
time
MAC 1
…
MAC n
MAC n+1
Mmm… MAC 3 stopped and a new MAC started sending right after, without any new association, it is OBVIOUSLY MAC 3
Mmm… 20 MACs stopped and 20 new MACs started sending right after, without any new association, it is obviously a rotation, but which one is which?
MAC n+n
…
Anonimity Set Size = 1
Anonimity Set Size = 20

## Slide 5: Coordination for Group Epochs
11-24/222r2:
A Group EDP Epoch sequence is initiated by an AP MLD by advertising the EDP Epoch parameters to a set of non-AP MLDs as defined in subclause 10.y.2.2 Group EDP Epoch advertisement.
Each non-AP MLD of the set of non-AP MLDs applies the advertised EDP Epoch parameters of the Group EDP Epoch to determine the same EDP Epoch sequence of one or more EDP Epoch start times.

## Slide 6: One-Time Group Proposal
AP declares group EDP epoch parameters, stating:
  "all STAs must join" or
  min threshold of #STAs according to AP (NAP ).
If (B): Each STA i declares to AP on its own time if it intends to hop onto this group EDP epoch.
If (B): Before EDP epoch start, if NAP is not reached, AP declares (unicast protected action frames to each STA i) next group EDP epoch invalid and won't be executed
  AP can "goto (1)" : declare a new group EDP epoch
If (B): Otherwise, all STAs that declared positive intention at (2) will participate to the group EDP Epoch (i.e.: perform group frame anonymization operations, etc...)

## Slide 7: Periodic Group Proposal
AP declares EDP epoch sequence and group EDP epoch parameters, stating:
  "All STAs must join" or
  min threshold of #STAs according to AP (NAP ).
If (B): Each STA i declares to AP on its own time if it intends to hop onto this group EDP epoch sequence.
If (B): Before first EDP epoch start, if NAP not reached, AP declares (unicast protected action frames to each STA i) group EDP epoch invalid and won't be executed
  AP can "goto (1)" : declare a new group EDP epoch + new epoch sequence
If (B): Otherwise, all STAs that declared positive intention at (2) will participate to the group EDP Epoch (i.e.: perform group frame anonymization operations, etc...) for this epoch sequence
  This means no additional messaging for all the EDP epoch sequence
(at any point in the sequence) STA j decides to withdraw from group EDP epoch sequence by sending protected action frame to AP. AP re-evaluates group EDP Epoch.

## Slide 8: Summary
Discussion on Anonymity Set Size related to Epoch structure
Coordinated group proposal in light of new 11-24/222r2
  One-time
  Periodic

## Slide 9: Straw Poll 1
Do you support a mechanism to coordinate group EDP epochs with thresholds on Anonymity Set Size (# of non-AP MLD STAs)?
Yes
No
Abstain

## Slide 10: Straw Poll 2
Do you support integrating the proposal for coordinated group EDP epoch, including Anonymity Set Size threshold, in the current draft?
Yes
No
Abstain

## Slide 11: References
Technical Privacy Metrics: a Systematic Survey - https://arxiv.org/abs/1512.00327
11-23/0873 Client Frame Tracking Countermeasures
11-23/1246 Proposal for sliding window MAC address rotation
11-23/1675 Epoch structure proposal
11-23/2098r3 Frame Anonymization Normative Text
11-24/222r2 Frame Anonymization and EDP Epoch Operation