## Slide 1: Longer Block-Length LDPC Codes
Date: 2024-07-12
Authors:
Name | Affiliations | Address | Phone | Email
Rethna Pulikkoonattu | Broadcom Inc | 16340 W Bernardo Dr, San Diego, CA, 92127 |  | rethna@broadcom.com
Andrew Blanksby |  |  |  | blanksby@broadcom.com
Tom Richardson | Qualcomm Inc |  |  | tomr@qti.qualcomm.com
Sameer Vermani |  |  |  | svverman@qti.qualcomm.com

## Slide 2: Introduction
This submission proposes Low-Density-Parity-Check (LDPC) codes with a block length of 3888 bits (2x1944) for UHR
  Support all the 4 code rates defined in 802.11be
Outline of the presentation
  High level reasoning for proposing 2x longer LDPC codes
  Birds eye view of the proposal
  Performance comparisons between the longer codes and existing codes
    Considerable performance improvements in various communication scenarios
    Even better performance gains in the presence of RF impairments for high data rate transmissions
  Code construction based on lifting
    Basic idea of lifting
    Details of code definition
      Exponent matrix and parity check matrix details
    Show how the approach allows reuse of existing encoding/decoding architectures
  Conclusions

## Slide 3: Why a 2x longer LDPC code?
LDPC codes has been the backbone error correction coding scheme for WiFi for over 15 years
  Longest LDPC code specified so far has block length=1944 bits
  Performance wise, about 2.7dB away from the optimum random codes (e.g., BICM,AWGN,4096-QAM, R=5/6 limits).
  Since the TGn amendment, data rates have surged significantly due to expansions in MIMO dimensions, modulation size (from 64-QAM to 4096-QAM), and bandwidth (from 40MHz to 320MHz), along with higher aggregations, all necessitating enhanced coding performance.
Pitch for longer block-length codes
  Long block length random codes lead to enhanced coding gains, in accordance with the finite-length scaling laws [1,2]
  Deterministic codes, which are suboptimal, exhibit scaling gains that are significantly larger than those of optimal random codes, (In AWGN a doubling effect is known to be true [1], see figure 12 in [1]).
The performance vs complexity trade off suggests that block-length of 2x1944 bits is a sweet spot

## Slide 4: Proposal for 2x longer codes: Birds eye view
Maintain the base structure of the 802.11be code, quasi-cyclic-LDPC (QC-LDPC) specifically, unchanged
  Facilitate the reutilization of existing hardware blocks in implementations
  Empower parallel encoding and decoding functionalities
Demonstrable gains across the board (channels, PHY bandwidth, MIMO, MCS, Transmit Beamforming)
  Provides 0.5-1.0dB gains over the present 802.11 LDPC codes, depending on the channel conditions
  Larger gains for high data rates with Tx/Rx impairments
Encoding and decoding
  The code's design allows for the potential parallelism in both encoding and decoding, using existing hardware blocks of 1944 bits

## Slide 5: Simulation Performance (1x1)
Conditions
  1x1: AWGN, D-NLOS, BLOS
  Linear Demapper
  No RF-impairments
  5000 channel realizations
  SNR ref @ PER=1%
  Near ideal channel estimation
  Decoder
    Layered BP,max 20 iterations
    Packet Length is varied to budget adequate number of codewords and symbols

## Slide 6: Simulation Performance (MIMO 2x2)
Conditions
  2x2x2 MIMO
  TxBF=OFF
  ~ML demapper
  No RF-impairments
  5000 channel realizations
  SNR ref @ PER=1%
  Near ideal channel estimation
  Channels
    D-NLOS,B-LOS
  Decoder
    Layered BP
    max 20 iterations

## Slide 7: Simulation Performance (MIMO 4x2 TxBF)
Conditions
  4x2x2 MIMO
  TxBF=SVD
  Linear demapper
  No RF-impairments
  5000 chan realizations
  SNR ref @ PER=1%
  Near ideal Chan.Est
  Channels
    D-NLOS, B-LOS
  Decoder
    Layered BP
    max 20 iterations

## Slide 8: Results with Impairments for High Data Rates
Now, we show performance gains of 2x LDPC with impairments
  Focus on high data rates
Simulation assumptions
  Full fledged implementation (realistic Tx/Rx impairments, tracking loops, channel estimation)
  RF Impairments modeled
    PLL Phase Noise, IQ imbalance, DC offset, CFO, Non-Linearity
  Detector
    4x2 has SVD precoding and at the receiver a linear de-mapper is used
    2x2 and 4x4 results (in Appendix) are with a lower complexity ML detector
  LDPC Decoder
    Max Iterations = 20
    Layered min-sum variant
  Other assumptions
    Packet size is varied to budget adequate number of codewords and symbols
    1000 independent channel realizations
    GI=1.6uS

## Slide 9: 320 MHz MIMO 4x2 D-NLOS: MCS 10-13
RF Impairments
  Phase Noise, IQ imbalance, CFO, DC offset, PA Non-Linearity
  Tx and Rx have identical impairment profiles

## Slide 10: Remarks on the gains in the presence of impairments
Greater gains are realized in a practical scenario characterized by limitations imposed by RF impairments
  Improvement in decoding SNR translate to a huge overall gain in an impairment limited scenario and can in some cases even lead to removal of error floor.
The 2x1944 code offers effective pathways to ensure full functionality of MCS10-13 across a broad spectrum of scenarios
  Improved reliability of higher MCSs.

## Slide 11: Outline of the Code Design: Protograph Lifting
Start with a graph corresponding to blocklength=1944 Code
Base graph is lifted by 2. Edges are then permuted using graph optimization techniques, specifically avoiding problematic short cycles (design goal is girth ≥ 6) and trapping sets. Further fine tuning is achieved by modifying graphs to improve decoding threshold and error floor [3], while retaining the lifting framework.
Illustration of the proto-lifting with a toy example

## Slide 12: 2x1944 LDPC Code Definition
Define the exponent matrix E(H) of size 48(1-R) x 48, where R is the code rate. The parity check matrix H is obtained by simply following the cyclic shifting procedure on identity matrix of size Z=81.
Keep the matrix interpretation consistent with the existing codes (i.e., cyclic shifted structure) in the IEEE specification

## Slide 13: Parallelism in Decoding
Two decoders working on 1944 block runs concurrently
  The cross-layer message passing will go through the connected edges (represented by the diagonal cross; corresponding to circulant matrix)
  This is possible due to the sub-matrix structure (2x2 circulant matrices)
Note: The general idea here is that, in the process of message passing based decoding on graphs, two graphs can be run in parallel. At certain fixed node positions (e.g., when the connection is off-diagonal), the exchange of information can be switched in a fixed manner.

## Slide 14: Parallelism in Decoding(ctd..)
Message Passing [4] and check node computation procedures unchanged, except for the appropriate swapping of the edges in the graph.
individual code graphs
connected code graph

## Slide 15: Parallelism in Decoding(ctd..)
Message passing is performed on these factor graphs [4] simultaneously.
individual code graphs
connected code graph

## Slide 16: Conclusions
LDPC codes with longer block lengths consistently yield enhanced performance gains
  2x1944 LDPC codes offers gains in the range 0.5-1.0dB in low-medium MCS
  Much larger gains in high MCS situations which are often limited by RF impairment limits
    These codes offers effective pathways to ensure full functionality of higher order QAM cases such as MCS10-13 across a broad spectrum of channel/BW scenarios
Proposed code structure facilitates parallelism in both encoding and decoding
  Manageable implementation cost of 2x1944 LDPC codes in both STA and AP devices
We believe this can be a differentiating feature for UHR, strengthening the high reliability aspect of the link

## Slide 17: Straw-Poll 1
Do you support adopting 2x1944 length LDPC codes for UHR?
  The parity matrix representation of the 2x1944 LDPC codes are as described in the slides 21-30

## Slide 18: References
Polyanskiy, Y., Poor, H.V. and Verdú, S., 2010. Channel coding rate in the finite blocklength regime. IEEE Transactions on Information Theory, 56(5), pp.2307-2359.
Yang, W., Durisi, G., Koch, T. and Polyanskiy, Y., 2014. Quasi-static multiple-antenna fading channels at finite blocklength. IEEE Transactions on Information Theory, 60(7), pp.4232-4265.
Richardson, T., 2003, October. Error floors of LDPC codes. In Proceedings of the annual Allerton conference on communication control and computing (Vol. 41, No. 3, pp. 1426-1435).
Richardson, T. and Urbanke, R., 2008. Modern coding theory. Cambridge university press.

## Slide 19: Appendix

## Slide 20: Random Coding vs LDPC: Finite Length Bounds
Finite Length scaling gain (Random codes versus LDPC codes). Suboptimal Codes exhibit larger scaling gains than random codes [2])
  Gain ~ 0.5-0.8dB vs RCU bounds (0.2-0.3)dB AWGN.
  Higher gain and bigger gap on D-NLOS channels
    Suboptimality of the code
    Frequency diversity (interleaving)
    Finite blocklength scaling

## Slide 21: 3888-LDPC E(H): R=5/6
[13,-1,-1,48,-1,80,-1,66,-1,4,74,-1,7,-1,-1,30,76,-1,-1,52,37,-1,-1,60,-1,-1,-1,49,73,-1,31,-1,-1,74,73,-1,-1,23,-1,-1,1,-1,0,-1,-1,-1,-1,-1
-1,13,48,-1,80,-1,66,-1,4,-1,-1,74,-1,7,30,-1,-1,76,52,-1,-1,37,60,-1,-1,-1,49,-1,-1,73,-1,31,74,-1,-1,73,23,-1,-1,-1,-1,1,-1,0,-1,-1,-1,-1
-1,69,-1,63,-1,74,56,-1,64,-1,-1,77,57,-1,-1,65,6,-1,-1,16,-1,51,-1,-1,64,-1,-1,-1,68,-1,-1,9,48,-1,-1,62,54,-1,27,-1,-1,-1,0,-1,0,-1,-1,-1
69,-1,63,-1,74,-1,-1,56,-1,64,77,-1,-1,57,65,-1,-1,6,16,-1,51,-1,-1,-1,-1,64,-1,-1,-1,68,9,-1,-1,48,62,-1,-1,54,-1,27,-1,-1,-1,0,-1,0,-1,-1
51,-1,15,-1,-1,0,-1,80,-1,24,-1,25,-1,42,54,-1,-1,44,71,-1,71,-1,-1,9,67,-1,-1,35,-1,-1,-1,58,-1,-1,-1,29,-1,-1,53,-1,0,-1,-1,-1,0,-1,0,-1
-1,51,-1,15,0,-1,80,-1,24,-1,25,-1,42,-1,-1,54,44,-1,-1,71,-1,71,9,-1,-1,67,35,-1,-1,-1,58,-1,-1,-1,29,-1,-1,-1,-1,53,-1,0,-1,-1,-1,0,-1,0
-1,16,29,-1,36,-1,-1,41,-1,44,56,-1,-1,59,-1,37,-1,50,24,-1,-1,-1,-1,65,4,-1,65,-1,52,-1,-1,-1,4,-1,-1,-1,-1,73,-1,52,1,-1,-1,-1,-1,-1,0,-1
16,-1,-1,29,-1,36,41,-1,44,-1,-1,56,59,-1,37,-1,50,-1,-1,24,-1,-1,65,-1,-1,4,-1,65,-1,52,-1,-1,-1,4,-1,-1,73,-1,52,-1,-1,1,-1,-1,-1,-1,-1,0]

## Slide 22: 3888-LDPC E(H): R=3/4
[48,-1,-1,29,28,-1,39,-1,9,-1,61,-1,-1,-1,-1,-1,-1,-1,63,-1,45,-1,-1,80,-1,-1,-1,-1,-1,-1,37,-1,-1,32,-1,22,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,48,29,-1,-1,28,-1,39,-1,9,-1,61,-1,-1,-1,-1,-1,-1,-1,63,-1,45,80,-1,-1,-1,-1,-1,-1,-1,-1,37,32,-1,22,-1,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1
4,-1,49,-1,-1,42,-1,48,11,-1,-1,30,-1,-1,-1,-1,-1,-1,49,-1,-1,17,41,-1,37,-1,-1,15,-1,-1,54,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1
-1,4,-1,49,42,-1,48,-1,-1,11,30,-1,-1,-1,-1,-1,-1,-1,-1,49,17,-1,-1,41,-1,37,15,-1,-1,-1,-1,54,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1
-1,35,-1,76,78,-1,51,-1,37,-1,35,-1,21,-1,-1,-1,-1,17,64,-1,-1,-1,-1,-1,-1,-1,59,-1,7,-1,-1,-1,-1,-1,-1,32,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1
35,-1,76,-1,-1,78,-1,51,-1,37,-1,35,-1,21,-1,-1,17,-1,-1,64,-1,-1,-1,-1,-1,-1,-1,59,-1,7,-1,-1,-1,-1,32,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1
9,-1,-1,65,44,-1,9,-1,-1,54,-1,56,73,-1,-1,34,42,-1,-1,-1,-1,-1,-1,-1,-1,35,-1,-1,-1,-1,-1,-1,46,-1,-1,39,0,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1
-1,9,65,-1,-1,44,-1,9,54,-1,56,-1,-1,73,34,-1,-1,42,-1,-1,-1,-1,-1,-1,35,-1,-1,-1,-1,-1,-1,-1,-1,46,39,-1,-1,0,-1,-1,-1,-1,-1,0,-1,0,-1,-1
-1,3,62,-1,-1,7,-1,80,-1,68,-1,26,-1,-1,-1,80,55,-1,-1,-1,36,-1,-1,-1,-1,26,-1,-1,9,-1,-1,-1,-1,72,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1
3,-1,-1,62,7,-1,80,-1,68,-1,26,-1,-1,-1,80,-1,-1,55,-1,-1,-1,36,-1,-1,26,-1,-1,-1,-1,9,-1,-1,72,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0
-1,26,-1,75,33,-1,21,-1,69,-1,59,-1,3,-1,-1,38,-1,-1,-1,-1,-1,-1,35,-1,-1,-1,-1,62,36,-1,-1,26,-1,-1,-1,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1
26,-1,75,-1,-1,33,-1,21,-1,69,-1,59,-1,3,38,-1,-1,-1,-1,-1,-1,-1,-1,35,-1,-1,62,-1,-1,36,26,-1,-1,-1,-1,-1,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0]

## Slide 23: 3888-LDPC E(H): R=2/3
[61,-1,75,-1,4,-1,63,-1,-1,56,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,8,-1,-1,-1,-1,2,-1,17,25,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,61,-1,75,-1,4,-1,63,56,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,8,-1,-1,2,-1,17,-1,-1,25,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,56,-1,74,77,-1,20,-1,-1,-1,-1,-1,-1,-1,64,-1,24,-1,-1,4,-1,67,-1,-1,-1,7,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
56,-1,74,-1,-1,77,-1,20,-1,-1,-1,-1,-1,-1,-1,64,-1,24,4,-1,67,-1,-1,-1,7,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
28,-1,21,-1,68,-1,-1,10,7,-1,14,-1,65,-1,-1,-1,-1,-1,-1,-1,23,-1,-1,-1,-1,-1,-1,-1,-1,75,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,28,-1,21,-1,68,10,-1,-1,7,-1,14,-1,65,-1,-1,-1,-1,-1,-1,-1,23,-1,-1,-1,-1,-1,-1,75,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1
-1,48,38,-1,43,-1,78,-1,76,-1,-1,-1,-1,-1,-1,-1,-1,-1,5,-1,36,-1,-1,-1,15,-1,72,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1
48,-1,-1,38,-1,43,-1,78,-1,76,-1,-1,-1,-1,-1,-1,-1,-1,-1,5,-1,36,-1,-1,-1,15,-1,72,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1
40,-1,2,-1,-1,53,-1,25,-1,-1,-1,52,62,-1,-1,-1,20,-1,-1,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1
-1,40,-1,2,53,-1,25,-1,-1,-1,52,-1,-1,62,-1,-1,-1,20,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1
69,-1,-1,23,64,-1,10,-1,22,-1,-1,-1,21,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,68,-1,23,-1,29,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1
-1,69,23,-1,-1,64,-1,10,-1,22,-1,-1,-1,21,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,68,-1,23,-1,29,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1
12,-1,-1,0,-1,68,-1,20,55,-1,61,-1,-1,-1,40,-1,-1,-1,-1,-1,-1,-1,-1,52,-1,-1,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1
-1,12,0,-1,68,-1,20,-1,-1,55,-1,61,-1,-1,-1,40,-1,-1,-1,-1,-1,-1,52,-1,-1,-1,-1,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0
-1,58,-1,8,-1,34,-1,64,-1,78,-1,-1,-1,-1,11,-1,-1,78,24,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,58,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1
58,-1,8,-1,34,-1,64,-1,78,-1,-1,-1,-1,-1,-1,11,78,-1,-1,24,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,58,-1,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0]

## Slide 24: 3888-LDPC E(H): R=2/3
[61,-1,75,-1,4,-1,63,-1,-1,56,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,8,-1,-1,-1,-1,2,-1,17,25,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,61,-1,75,-1,4,-1,63,56,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,8,-1,-1,2,-1,17,-1,-1,25,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,56,-1,74,77,-1,20,-1,-1,-1,-1,-1,-1,-1,64,-1,24,-1,-1,4,-1,67,-1,-1,-1,7,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
56,-1,74,-1,-1,77,-1,20,-1,-1,-1,-1,-1,-1,-1,64,-1,24,4,-1,67,-1,-1,-1,7,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
28,-1,21,-1,68,-1,-1,10,7,-1,14,-1,65,-1,-1,-1,-1,-1,-1,-1,23,-1,-1,-1,-1,-1,-1,-1,-1,75,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,28,-1,21,-1,68,10,-1,-1,7,-1,14,-1,65,-1,-1,-1,-1,-1,-1,-1,23,-1,-1,-1,-1,-1,-1,75,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1
-1,48,38,-1,43,-1,78,-1,76,-1,-1,-1,-1,-1,-1,-1,-1,-1,5,-1,36,-1,-1,-1,15,-1,72,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1
48,-1,-1,38,-1,43,-1,78,-1,76,-1,-1,-1,-1,-1,-1,-1,-1,-1,5,-1,36,-1,-1,-1,15,-1,72,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1
40,-1,2,-1,-1,53,-1,25,-1,-1,-1,52,62,-1,-1,-1,20,-1,-1,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1
-1,40,-1,2,53,-1,25,-1,-1,-1,52,-1,-1,62,-1,-1,-1,20,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1
69,-1,-1,23,64,-1,10,-1,22,-1,-1,-1,21,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,68,-1,23,-1,29,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1
-1,69,23,-1,-1,64,-1,10,-1,22,-1,-1,-1,21,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,68,-1,23,-1,29,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1
12,-1,-1,0,-1,68,-1,20,55,-1,61,-1,-1,-1,40,-1,-1,-1,-1,-1,-1,-1,-1,52,-1,-1,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1
-1,12,0,-1,68,-1,20,-1,-1,55,-1,61,-1,-1,-1,40,-1,-1,-1,-1,-1,-1,52,-1,-1,-1,-1,-1,-1,-1,-1,44,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0
-1,58,-1,8,-1,34,-1,64,-1,78,-1,-1,-1,-1,11,-1,-1,78,24,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,58,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1
58,-1,8,-1,34,-1,64,-1,78,-1,-1,-1,-1,-1,-1,11,78,-1,-1,24,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,58,-1,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0]
E(H) in text/CSV format

## Slide 25: 3888-LDPC E(H): R=1/2

## Slide 26: 3888-LDPC E(H): R=1/2
[-1,57,-1,-1,-1,-1,-1,-1,-1,50,-1,-1,11,-1,-1,-1,50,-1,-1,-1,-1,79,-1,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
57,-1,-1,-1,-1,-1,-1,-1,50,-1,-1,-1,-1,11,-1,-1,-1,50,-1,-1,79,-1,-1,-1,-1,1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,3,-1,-1,-1,28,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,55,-1,-1,7,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
3,-1,-1,-1,28,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,55,7,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
30,-1,-1,-1,-1,-1,-1,-1,-1,24,37,-1,-1,-1,-1,-1,56,-1,-1,14,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,30,-1,-1,-1,-1,-1,-1,24,-1,-1,37,-1,-1,-1,-1,-1,56,14,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
62,-1,53,-1,-1,-1,-1,-1,-1,53,-1,-1,-1,-1,3,-1,35,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,62,-1,53,-1,-1,-1,-1,53,-1,-1,-1,-1,-1,-1,3,-1,35,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,40,-1,-1,-1,-1,20,-1,66,-1,-1,-1,-1,-1,-1,22,-1,28,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
40,-1,-1,-1,-1,-1,-1,20,-1,66,-1,-1,-1,-1,22,-1,28,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
0,-1,-1,-1,-1,-1,-1,-1,8,-1,-1,-1,42,-1,-1,-1,-1,50,-1,-1,-1,-1,8,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,0,-1,-1,-1,-1,-1,-1,-1,8,-1,-1,-1,42,-1,-1,50,-1,-1,-1,-1,-1,-1,8,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1
69,-1,79,-1,79,-1,-1,-1,-1,-1,-1,-1,-1,56,-1,-1,52,-1,-1,-1,-1,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1
-1,69,-1,79,-1,79,-1,-1,-1,-1,-1,-1,56,-1,-1,-1,-1,52,-1,-1,-1,-1,-1,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1,-1
65,-1,-1,-1,-1,-1,-1,-1,38,-1,57,-1,-1,-1,-1,-1,72,-1,-1,-1,27,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1,-1
-1,65,-1,-1,-1,-1,-1,-1,-1,38,-1,57,-1,-1,-1,-1,-1,72,-1,-1,-1,27,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1,-1
-1,64,-1,-1,-1,-1,-1,-1,14,-1,52,-1,-1,-1,-1,-1,-1,30,-1,-1,-1,-1,-1,32,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1,-1
64,-1,-1,-1,-1,-1,-1,-1,-1,14,-1,52,-1,-1,-1,-1,30,-1,-1,-1,-1,-1,32,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1,-1
-1,-1,-1,45,-1,-1,-1,70,0,-1,-1,-1,-1,-1,-1,-1,77,-1,9,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1,-1
-1,-1,45,-1,-1,-1,70,-1,-1,0,-1,-1,-1,-1,-1,-1,-1,77,-1,9,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1,-1
2,-1,56,-1,-1,-1,-1,57,35,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,12,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0,-1
-1,2,-1,56,-1,-1,57,-1,-1,35,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,12,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1,0
-1,24,-1,-1,-1,61,-1,-1,-1,60,-1,-1,-1,-1,-1,27,51,-1,-1,-1,-1,-1,16,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0,-1
24,-1,-1,-1,61,-1,-1,-1,60,-1,-1,-1,-1,-1,27,-1,-1,51,-1,-1,-1,-1,-1,16,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,-1,0]
E(H) in text/CSV format

## Slide 27: Parity Check Matrix -3888-LDPC & E(H): R=5/6
parity check matrix

## Slide 28: Parity Check Matrix -3888-LDPC & E(H): R=3/4
parity check matrix

## Slide 29: Parity Check Matrix -3888-LDPC: R=2/3
parity check matrix

## Slide 30: Parity Check Matrix -3888-LDPC: R=1/2
parity check matrix

## Slide 31: 160MHz MIMO 2x2 D-LOS: MCS 10-13
RF Impairments (Typical)
  Phase Noise, IQ imbalance, CFO, DC offset
  Tx and Rx have identical impairment profiles

## Slide 32: 160MHz MIMO 2x2 D-LOS: 4096-QAM
RF Impairments (Typical and Minimal)
  Typical: Phase Noise, IQ imbalance, CFO, DC offset
  Minimal: Very low noise Phase Noise profile (dominant noise)

## Slide 33: 320 MHz MIMO 2x2 D-LOS: MCS 10-13
RF Impairments (Typical)
  PLL Phase Noise, IQ imbalance, CFO, DC offset
  Tx and Rx have identical impairment profiles

## Slide 34: 160MHz MIMO 4x4 D-NLOS
Long Packets Length (10+ symbols)
RF Impairments (Aggressive)
  Phase Noise, IQ imbalance, CFO, DC offset, NL
  Tx and Rx have identical impairment profiles