## Slide 1: Multi AP Transmissions: On the Link Quality Metric
Date: 2023-09-10
Authors:

## Slide 2: Introduction
We introduced the concept of Virtual BSS (V-BSS) in 11-19/1019r0, (Virtual BSS For Multi AP Coordination)
In 1394r1 (Nov 2022), we proposed a method for collection and management of relevant metrics from the Wi-Fi network that will help to configure the V-BSS network for multi-AP Transmissions – with a view to optimize, in general, any objective function of interest - such as maximize area throughput or minimize packet delay etc.
We introduced Link Quality Metric (LQM) and Queue Size Metric (Recap in next page)
  Assumes a central controller.
In this contribution, we further develop on LQM

## Slide 3: V-BSS concept and definitions
A-AP12
A-AP11
A-AP13
A-AP21
A-AP22
A-AP23
A-AP31
A-AP32
A-AP33
S01
S02
S03
S04
S05
S06
S07
S08
S09
S10
S20
S24
S25
S11
S12
S13
S14
S15
S16
S17
S18
S19
S21
S22
S23
S26
S27
S28
V-BSSID
C-AP
Stations (S01, … S28) are wirelessly connected to one or more Anchor APs (A-AP) in the multi BSS
A-APs are connected to Multi AP Coordinator (coordinator AP or C-AP)
  C-AP controls the control path
  typically a wired connectivity
Link Quality Metric (LQM)
  Path loss between 2 entities.

## Slide 4: LQM
Two types of LQM Tables.
  LQM Table (A-AP to A-AP)
    Upon boot up (time zero) - each A-AP listens to beacons from the neighboring A-APs and creates a path-loss list.
    A-APs periodically updates their list and sends to C-AP
    C-AP reviews and modifies this list
  LQM Table (A-AP to STA)
    Each STA listens to beacons from the neighboring A-APs and creates a path-loss list
    STAs periodically updates its list and sends it to the A-AP that it is associated with.
    A-APs sends this to C-AP.
    C-AP reviews and modifies this list
If O(V)BSS is detected, interference table(s) can also be created

## Slide 5: LQM table (AP to STA)
Upon boot up (time zero) - each STA listens to beacons from the neighboring APs for a duration of TBD seconds and creates a RSSI/path-loss table.
Note that
  Each STA maintains a list of ordered pairs of {AP, path_loss} (LQM list) for all the APs it can receive beacons from
  Each STA periodically updates the above
  Each STA periodically sends the above list to the A-AP it is associated with.
  A-AP sends this to C-AP periodically.
  C-AP constructs and reviews the LQM table
Next 3 slides explains this concept with an example

## Slide 6: LQM Table from A-AP to C-AP (for C-AP review)
 | A-AP11 | A-AP12 | A-AP13 | A-AP14 | A-APxx | A-AP31 | A-AP32 | A-AP33 | 
S01 | x11 | x12 |  |  |  |  |  |  | 
S02 | x21 | x22 |  |  |  |  |  |  | 
S03 | x31 | x32 | x33 |  |  |  |  |  | 
S04 |  | x42 | x43 | x44 | x4x |  |  |  | 
S05 |  | x52 | x53 | x54 | x5x |  |  |  | 
S06 |  |  | x63 | x64 | x6x |  |  |  | 
S07 |  |  |  | x74 | x7x |  |  |  | 
S08 |  |  |  |  | x8x |  |  |  | 
S09 |  |  |  |  | x9x | x91 | x92 |  | 
S27 |  |  |  |  | x27x | x271 | x272 | x273 | 
S28 |  |  |  |  |  | x281 | x282 | x283 | 
S29 |  |  |  |  |  | x291 | x292 | x293 | 
x11..x293 are the computed LQM
  Computed by each station by listening to A-AP beacons
Each station passes the LQM list to the A-AP it is associated with.
  e.g: S01 sends {x11, A_AP11}, {x12, A_AP12} … tuples to A_AP11.
Each A_AP sends these lists in turn, to the C-AP.
C-AP collates these in to a table as shown below

## Slide 7: LQM Table review by C-AP
Table in the previous slide does not have all the entries filled in. This is because all APs cannot hear all STAs.
During the time of network installation of an infra-structure network, the relative AP position/geolocation etc. would be looked into. This information can be made available to C-AP (pre-configuration information).
C-AP can come out with a set of coarse LQM values {say y1,y2, y3, y4} which are sufficiently far apart, based on the location of the A-APs. These values can be used to fill up the table as shown in the next figure.

## Slide 8
 | A-AP11 | A-AP12 | A-AP13 | A-AP14 | A-APxx | A-AP31 | A-AP32 | A-AP33 | 
S01 | x11 | x12 | y1 | y2 | y1 | y3 | y4 | y4 | 
S02 | x21 | x22 | y1 | y1 | y2 | y3 | y4 | y4 | 
S03 | x31 | x32 | x33 | y2 | y2 | y3 | y4 | y4 | 
S04 | y1 | x42 | x43 | x44 | x4x | y2 | y3 | y4 | 
S05 | y1 | x52 | x53 | x54 | x5x | y2 | y3 | y3 | 
S06 | y1 | y1 | x63 | x64 | x6x | y1 | y3 | y3 | 
S07 | y2 | y1 | y1 | x74 | x7x | y1 | y3 | y2 | 
S08 | y2 | y3 | y2 | y1 | x8x | y1 | y2 | y2 | 
S09 | y3 | y3 | y2 | y1 | x9x | x91 | x92 | y1 | 
S27 | y3 | y4 | y3 | y1 | x | x271 | x272 | x273 | 
S28 | y4 | y4 | y4 | y2 | y1 | x281 | x282 | x283 | 
S29 | y4 | y4 | y4 | y2 | y1 | x291 | x292 | x293 | 
LQM Table from C-AP to A-AP (after C-AP review)
C-AP reviews the LQM table and inserts the missing entries from the pre-configuration info.
  y1, y2 etc. denote a LQM value that best represents a distance range(d2-d1).
  (for free space (in dB)) 20log10(d1 + (d2-d1)/2) + 20log10(f) + constant
  y1, y2 etc. are obtained by C-AP at the time of network installation – possibly by geo-locationing the A-APs.

## Slide 9: LQM table (AP to AP)
As described earlier (LQM table AP to STA), another table can be constructed that involve only A-APs in a similar fashion.
Upon boot up (time zero) - each A-AP listens to beacons from the neighboring A-APs for a duration of TBD seconds and creates a path-loss/RSSI list as below. These values will be periodically updated.
  A-AP11’s table is given below as an example
Each A-AP sends this list to C-AP

## Slide 10: LQM Table A-AP to A-AP at C-AP (for C-AP review)
 | A-AP11 | A-AP12 | A-AP13 | A-AP14 | A-APxx | A-AP31 | A-AP32 | A-AP33
A-AP11 | 0 | X11_12 | X11_13 | X11_14 |  |  |  | 
A-AP12 | X12_11 | 0 | X12_13 | X12_14 |  |  |  | 
A-AP13 |  | X13_12 | 0 | X13_14 | X13_xx |  |  | 
A-AP14 |  | X14_12 | X14_13 | 0 | X14_xx |  |  | 
A-APxx |  |  | Xxx_13 | Xxx_14 | 0 | Xxx_31 |  | 
A-AP31 |  |  |  | X31_14 | X31_xx | 0 | X31_32 | 
A-AP32 |  |  |  |  | X32_xx | X32_31 | 0 | X32_33
A-AP33 |  |  |  |  | X33_xx | X33_31 | X33_32 | 0
X11_12 … are the computed LQM (path loss values)
  Computed by each A-AP by listening to other A-AP beacons

## Slide 11: Review of AP-to-AP Table by C-AP
Similar procedure as in slides 7 & 8.
  C-AP updates and collates the AP-to-AP table it obtained from A-APs using V-BSS configuration information

## Slide 12: How to use these tables?
The A-AP to A-AP table together with the A-AP to STA table can help C-AP to determine what coordination mode for transmission (joint processing, coordinated OFDMA, coordinated Spatial Reuse, coordinated beamforming) is optimal
Note that C-AP manages the network. Data may or may not be routed through C-AP

## Slide 13: Managing Coordinated Transmissions
From AP-to-AP LQM Table, coordinator-AP learns the power profile (spatial configuration – loosely speaking) of APs (Implementation Specific)
From AP-to-STA LQM table, coordinator-AP maps out the most suited multi-AP transmission modes for each STA (and the corresponding Anchor AP(s) ) in the network (Implementation Specific)
C-AP informs
  sub-set of the LQM-table to each Anchor-AP (for periodic update & for A-AP’s reference).
  The dynamic groups that can participate in a coordinated transmission (chosen by C-AP)
  What Coordinated transmission mode is the most suitable for the given dynamic groups
    and the necessary parameters to enable the same, such as TX power (for C-SR), channel details (for C-OFDMA) etc.
    Which all dynamic groups can work independently.

## Slide 14: Reference
[1] 11-22/1394r1, “Virtual BSS And Multi AP Transmissions”
[2] 11-18/1926r2, “Terminology for AP Coordination”
[3] 11-19/1019r0, “Virtual BSS For Multi AP Coordination”
[4] 11-19/1972r1, “Operation of Virtual BSS for Multi-AP Coordination”
[5] 11-23/0668r2, “Coordinated Measurement”
[6] 11-23/908r0, “Efficient Coordinated Spatial Reuse”