## Slide 1: Trigger, BA, and BAR protection
Date: 2023-11-09
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Ido Ouzieli |  |  |  | 
Danny Alexander |  |  |  | 
Daniel F Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Robert Stacey |  |  |  | 
Ehud Reshef |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
There have been presentations talking about protection for various control frames. [1-5]
We provide follow up for the development of this topic.

## Slide 3: Which Control frame to protect?
3 Control frames stand out due to potential security attack
  Trigger frame
    Due to potential power attack since SMPS and eMLSR use Trigger frame to tell client to exit low power mode
    Due to potential fake request for long response
    BA protocol attack
  BAR frame and BA frame
    Due to BA protocol attack
There are existing PBAC protocols to deal with BA protocol attack
  Only focus on BAR and disallow important moving window functionality for BAR frame and MU-BAR
  Directly protect BA and BAR is therefore better

## Slide 4: Which variants to protect?
Trigger frame
  Flexibility of Trigger frame format implies feasibility to insert PN and MIC and be backward compatibility
  One solution will likely work for all variants
  Protecting all variants also address the fake request for long response
BA
  Formats depending on the variants
  Should consider compressed BA and Multi-STA BA
BAR
  Formats depending on the variants
  Should consider compressed BAR and Multi-TID BAR

## Slide 5: Mode of Protection
Authentication of the frame is definitely required
For group addressed frame, encryption of the body will directly create issues for backward compatibility
  Legacy will still parse encrypted User Info field to search for relevant User Info field and may parse wrong and respond TB to kill other TB transmission
It is clear that we should consider Authentication only for group addressed control frame that are defined to be protected
  Examples of target group addressed control frame: Trigger frame and Multi-STA BA

## Slide 6: Cipher Usage
11be mandates support of GCMP-256, which implies that support of GMAC-256 is already there
Propose to simply use GMAC-256 for Authentication only protection
  Already supported by all 11bn since 11bn will support 11be
  The best we can use anyway
  No need for further negotiation

## Slide 7: Discussion on Key
For group addressed control frame that are defined to be protected, should use additional key per BSS to do the protection
  Similar to what we have done for GTK/IGTK/BIGTK
For individually addressed control frame that are defined to be protected, would make more sense to have separate key (different from the key used for group addressed) for individual client
  Align with the direction in the existing spec to separate group key and individual key

## Slide 8: Conclusion
We provide follow up on protection for Trigger frame, BA frame, and BAR frame
  Important control frame to protect due to security attack
We discuss the following aspects for the development on this topic
  Which variants to protect
  Define authentication only for group addressed control frame that are defined to be protected
  Use GMAC-256 for group addressed control frame that are defined to be protected
  Have additional group key per BSS to protect group addressed control frame that are defined to be protected

## Slide 9: SP #1
Do you support to define Trigger frame protection in 802.11bn?

## Slide 10: SP #2
Do you support to define BAR frame protection in 802.11bn?
  Which variants to be protected is TBD

## Slide 11: SP #3
Do you support to define BA frame protection in 802.11bn?
  Which variants to be protected is TBD

## Slide 12: SP #4
Do you support to use GMAC-256 to protect group addressed control frame that are defined to be protected

## Slide 13: SP #5
Do you support to have one additional group key per BSS to protect the group addressed control frames that are defined to be protected?

## Slide 14: Reference
[1] 11-23-0286 Trigger Frame Protection
[2] 11-23-0312 Thoughts on Secure Control frames
[3] 11-23-0352 Enhanced Security Discussion
[4] 11-23-1102 security enhancement follow up
[5] 11-23-1914 Enhanced Security Consideration in UHR