## Slide 1: MAC Header Protection
Date: 2023-11-09
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Daniel F Bravo |  |  |  | 
Ido Ouzieli |  |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Danny Alexander |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Protection of MAC header has been discussed [1]
We provide our thoughts in this presentation

## Slide 3: Need for MAC Header Protection
Several fields in the MAC header today are masked out and not protected by the frame body protection
  Due to possibility of value change during retransmission and the need to reuse a PN
However, those masked out fields do introduce security concern
  PM bit as discussed in [2]
  SN field due to BA protocol attack to complete the protection of BA protocol attack
  HT control due to various information that maybe piggybacked
Hence, it is indeed useful to protect MAC header

## Slide 4: Scope of MAC Header Protection
The problem we have in hand (ex, PM, SN, HT Control) are in the MAC header of data and management.
Further, those problems (PM, BA protocol, HT Control) are specific to individually addressed data and management frame.
  Introduce MAC header protection for group addressed data and management frame likely have backward compatibility issues or blow out the group addressed transmission over the air
It then makes sense for 11bn to focus the design of MAC Header protection on individually addressed data and management frame

## Slide 5: Direction of Protection
To accommodate the possibility of MAC header change during retransmission, MAC header protection and Frame body protection needs to be MIC separately
  Imply separate key different from frame body protection
  Imply separate PN field different from frame body protection
  Imply separate MIC computation different from frame body protection

## Slide 6: Requirement on Response
Today acknowledgement is sent to individually addressed data/management frame after FCS check
With MAC header protection, acknowledge then needs to be sent only after FCS check and MIC check of MAC header
  If Acknowledgement is sent without MIC check of MAC header, then we still have attack on transmitter side
SN 1 in MAC header
Data frame 1
Ack without checking MIC
SN 2 in MAC header
Data frame 1
modify

## Slide 7: Fields to be Protected
Fields like PM, SN, HT Control should naturally be protected
Fields like Duration need separate discussion
  Recall Duration from any 3rd party CTS is not protected, and is difficult to be protect if feasible at all
Security header of frame body protection needs to be considered to have some coupling between MAC header protection and Frame body protection
  Otherwise, possibility of swap attack
SN 1 MAC header 1
SN 2 MAC header 2
Data frame 1
Data frame 2
Swap
SN 2 MAC header 2
SN 1 MAC header 1
Data frame 1
Data frame 2
Receiver uses SN2 for data frame 1

## Slide 8: Conclusion
We think MAC header protection is an important feature for 11bn
  Focus on individually addressed data and management frame
  Have separate key, PN field, MIC calculation different from frame body protection
  Require to send response after checking FCS and MIC of MAC header protection
  Protect security header (if present) to have some coupling of MAC header protection and frame body protection

## Slide 9: SP #1
Do you support to define MAC header protection for individually addressed data and management in 11bn?

## Slide 10: SP #2
Do you support that the checking the MIC of MAC header protection is required before sending response to individually addressed data and management with MAC header protection?

## Slide 11: SP #3
Do you support that MAC header protection for individually addressed data and management will at least protect the following fields?
  PM bit
  Sequence Control
  HT Control (if present)
  security header of frame body protection (if present)

## Slide 12: Reference
[1] 11-23-1888 MAC Header Protection follow up
[2] Framing Frames: Bypassing Wi-Fi Encryption by Manipulating Transmit Queues