## Slide 1: AMP Communication Channel Usage Estimation Part 3: Low Latency Traffic
Date: 2023-11-??
Authors:

## Slide 2: Abstract
This is a follow-up to doc. IEEE 802.11-23/1601r1, considering the effect low latency traffic

## Slide 3: IEEE 802.11 Access Categories
t
SIFS +
2 ×SLOT
[0 .. 7]×SLOT
t
SIFS + 2 ×SLOT
[0 .. 3]× SLOT
t
SIFS + 7 ×SLOT
[0 .. 15]×SLOT
t
SIFS +
3 ×SLOT
[0 .. 15]×SLOT
t
BK
BE
VI
VO

## Slide 4: Interference Analysis: System-Level Simulation
3000 AMP-STAs
Query all AMP-STAs every 60s
1ms per query
Access Category Background
VoIP Traffic: 100B @ 20ms
Access Category Voice
KPI: VoIP packet delay

## Slide 5: Results n = 3000, Query every 60s
In the following 5 slides we explain each aspect of the CDF

## Slide 6: Results n = 3000, Query every 60s
VoIP Packet transmission duration + AIFS[AC_VO]

## Slide 7: Results n = 3000, Query every 60s
Backoff, 0...3 slots

## Slide 8: Results n = 3000, Query every 60s
Probability that AMP query is active: 3000×1ms / 60s = 0.05

## Slide 9: Results n = 3000, Query every 60s
Additional latency if AMP query is active: [0 ... 1ms]
(uniformly distributed as transmissions are not synchronized)

## Slide 10: Results n = 3000, Query every 60s
Bounded latency:
Packet transmission duration +
AIFS[AC_VO] +
3×slot +
1ms

## Slide 11: Effect of AMP Parameters
Duty Cycle
TXOP Duration
Adaptation of AMP parameters:
Duty cycle changes the length of the vertical arrow.
TXOP duration changes the length of the horizontal arrow.

## Slide 12: Conclusion
Evaluated the effect of AMP query traffic on the delay distribution of VoIP packets
  Due to the selected access categories, any VoIP transmission is blocked by at most one AMP query  bounded latency
  Linear relation between AMP TXOP duration and maximum delay
  Linear relation between AMP duty cycle and probability of blockage
Base for further discussion on duty cycle or TXOP duration limits.