## Slide 1: In-device Coexistence and P2P – follow-up
Date: 2023-11-10
Authors:

## Slide 2: Summary of proposals
UHR is the opportunity to improve reliability in presence of interference or other device activities
We propose several solutions, for predictable or unpredictable interferences/activities
  Long term indication of periodic service periods during which a STA shall be considered in doze (unavailable)
  Long term indication of interference in frequency domain
  Long term expected behaviors
  Short term signaling in BA in case of unexpected interference to ensure no double punishment (unfavorable rate adaptation)
  Short term shortening/truncation of a TxOP due to upcoming interference, as a TxOP responder or TxOP holder in CTS or BA…

## Slide 3: Classification of long term indications for in-device coex
Long term indication can be split into 3 different parts:
1) Identification of periods of time during which the STA is completely unavailable
2) Identification of interference levels on specific 20 MHz subchannels (all the time or possibly only during specific SPs)
3) Description of expected behaviors in possible presence of interference (all the time or possibly only during specific SPs)

## Slide 4: Classification of long term indications for in-device coex
Long term indication can be split into 3 different parts:
1) Identification of periods of time during which the STA is completely unavailable
  On AP side, such information is similar to long term AP power save schedule, so we can use this mechanism
    We can use Broadcast TWT with TWT ID=0 (for all STAs) and Responder PM=1 to indicate the time during which the AP is available (and therefore unavailable outside)
    Unavailability field in TWT element can be set to 1 to clarify that unavailability takes precedence (even if there’s an iTWT SP that happens to exist within the unavailability period)

## Slide 5: Classification of long term indications for in-device coex
Long term indication can be split into 3 different parts:
1) Identification of periods of time during which the STA is completely unavailable
  On STA side, there is the P2P TWT mechanism defined in 802.11
    STA informs the AP of its unavailability period(s) with a Channel Usage Request frame containing a TWT element
    Following AP’s successful response, P2P TWT is created during which the AP shall consider the STA as unavailable or in doze
    Not a TWT agreement: TWT element just used as container to define service period, this is really an announcement
  Proposal can be as simple as mandating support for P2P TWT on AP side
  Alternatively: use Colocated Interference Report and add normative behaviors

## Slide 6: Classification of long term indications for in-device coex
Example of usage of P2P TWT notification (unavailability notification)
AP 1
P2P AP
P2P Client
WLAN- STA
WLAN BSS
P2P
WLAN- STA
AP 2
WLAN BSS
P2P TWT Notification
P2P TWT Notification

## Slide 7: Classification of long term indications for in-device coex
Long term indication can be split into 3 different parts:
2) Identification of interference levels on specific 20 MHz subchannels (all the time or possibly only during specific SPs)
  If a 20 MHz subchannel is identified as being at a level of interference that is so high that no communication is possible, this subchannel shall not be used between the STA and the AP
    This can become a sort of per-STA static puncturing negotiation for SU PPDUs between AP and STA
    For MU transmissions, the STA shall not be scheduled on RUs overlapping with the interfered subchannel
  Otherwise, rate selection would need to be adjusted to account for the interference
  We can use Colocated interference report or define signaling

## Slide 8: Classification of long term indications for in-device coex
Long term indication can be split into 3 different parts:
3) Description of expected behaviors in possible presence of interference (all the time or possibly only during specific SPs)
  Sometimes difficult to react fast enough in presence of interference and long term preventive behaviors can be a good tool to have
  Behaviors that can be requested: Maximum PHY rate, Max NSS, TxOP or PPDU duration limits
    This is useful if applying these constraints help ensure some level of detections when the interference is present, while not harm too much performance when interference is not present
  Similarly, these constraints can be applied all the time or within a specific service period and signaling has to be defined accordingly

## Slide 9: Proposals for 2) unpredictable interference
a) Shortening/truncation of a TxOP due to upcoming interference, as a TxOP responder or TxOP holder, and information about an upcoming unavailability period
b) Add signaling in BA in case of unexpected interference to ensure no double punishment (explained before)

## Slide 10: 2) a) TxOP shortening/truncation and short term indication of an upcoming unavailability period
Define a mechanism so that a non-AP STA recipient of a PPDU transmission can indicate, at the beginning of the TxOP that it will be available only until a specific point in time, and not after because it knows an interferer will be present at that time
  That would be in a CTS response or any initial control frame response
  Similar feedback can be provided in a BA frame during a TxOP for completeness
  If the STA is aware of the duration of the unavailability period, that can also be included
We also propose to allow a non-AP STA to send such information in an unsolicited manner (so as a TxOP holder possibly)

## Slide 11: 2) b) Rate selection in case of interference
We propose to add a signaling indication in a BlockAck frame that is sent (by a responder) as immediate response to a PPDU transmission (sent by an initiator) in order to indicate to the initiator of the PPDU that the PPDU reception suffered from an unusual interference, which was the main cause of packet losses.
  Could be a simple 1-bit field to indicate that the PPDU reception suffered from interference or not or it could be more advanced to locate more accurately the interference impact if needed
Expected behavior: Initiator will not take into account statistics of this PPDU for updating its rate selection algorithm
  Note that this could fit in the more general Link adaptation mechanism (rate selection based on feedbacks in the BA) if we define one in UHR

## Slide 12: 2) b) Rate selection in case of interference
Continued..
If the transmitter already dropped the rate, it would also be good to have a way to bring the rate back up
  This can be a complementary signaling to specifically ask to go back to immediately preceding rate
  As mentioned in previous slide, this can fit in a more general link adaptation mechanism in BA, such as a simple tool to ask to go up one rate, go down one rate, or keep current rate…

## Slide 13: SP1
Do you agree to define a mechanism to allow a STA to optionally indicate or update a periodic unavailability in time to its peer STA?
  Expectation is to use existing protocols

## Slide 14: SP2
Do you agree do define a mechanism so that a non AP STA that is a TXOP responder can indicate in a response frame for how long it will be available, if known and/or whether it will be unavailable after a specific point in time and, if known, for how long?

## Slide 15: SP3
Do you agree do define a mechanism so that a non-AP STA as a TXOP holder can indicate in a frame for how long it will be available, if known and/or whether it will be unavailable after a specific point in time and, if known, for how long?

## Slide 16: SP4
Do you agree do define a long term signaling to allow a STA to request its peer associated STA to limit the range of transmit parameters (e.g. Max MCS, Max NSS, Max PPDU size) used by the peer STA for PPDUs addressed to the STA
  goal is to be more resilient to possible interference on STA Rx side

## Slide 17: Annex 1

## Slide 18: P2P TWT as defined in current spec
STA informs the infrastructure AP of its unavailability period(s) with a Peer-to-Peer TWT agreement
  This is not a regular TWT agreement, TWT procedure is ignored and TWT element is just used here just to define the timing parameters of the service period
  Mode where the AP shall accept the Peer-to-peer TWT agreement (this is an advertisement from the STA)
  The only rule that applies is as follows
    The AP shall consider the STA in doze state during the Peer-to-peer TWT Service Period(s), and therefore not transmit to the STA during that time, unless if it receives an explicit indication that the STA is awake and available
This way:
  The client device can easily multiplex the time used for operating with the BSS and for operating with P2P Group
  The infra AP is aware of the time during which the STA is unavailable and schedules it outside of these period(s)

## Slide 19: P2P TWT as defined in current spec
STA sends a Channel Usage Request frame to its associated infrastructure AP, which includes
  a TWT element describing the service period(s) during which the STA will be unavailable, and with
  The Usage Mode field in the Channel Usage element set to 3 for “Peer-to-Peer link”
  No Channel Entry field included in the Channel Usage element
Infra AP shall respond with a Channel Usage Response frame with “Accept TWT” to provide a TWT Flow ID for the corresponding P2P TWT agreement
Following this exchange, the Peer-to-peer TWT agreement is active and the only following rule applies:
  The AP shall consider the non-AP STA to be in power save mode and doze state at the start of the peer-to-peer TWT SP and back to its original power management mode at the end of the peer-to-peer TWT SP unless the AP receives a frame addressed to it from the non-AP STA within the time that overlaps with the peer-to-peer TWT SP.

## Slide 20: P2P TWT as defined in current spec

## Slide 21: Annex 2

## Slide 22: In-device coexistence issue
In device coexistence with Bluetooth (BT) has always been an issue.
  So far, this was contained in the 2.4 GHz band only.
  BT will now be able to operate at both 5 and 6 GHz, which makes the problem bigger than it was before.
  EU Regulatory is already in process of enabling Bluetooth, ZigBee and BLE operation in 5 and 6 GHz band.
There are other sources of interference
  other wireless technologies
  with multi-link operation, we have other sorts of interference that can arise, and that may be sometimes difficult to predict.
    Multilink NSTR operation is a good example where a transmission on one link by a STA of a non-AP MLD may impact the reception of a collocated STA of the same non-AP MLD by generating some cross-link interference, …
  In-device coexistence (spurs, modulation between components, …)

## Slide 23: Other activities
A STA can be associated to an infrastructure AP and have P2P or mobile AP operation at the same time, …
Such STA typically needs to multiplex in time its operation for infrastructure AP and for P2P
  A STA currently uses power mode changes with infra AP in order to signal unavailabilities (very inefficient)
  Negotiation of TWT SP operation could help, but difficult to describe properly the client constraints, which makes negotiation difficult or impossible
Lack of a clear mechanism for a STA to inform an infrastructure AP of its constraints for P2P operation, especially a clear indication of a Service Period or Period of Time during which the STA shall be considered as in doze state and unavailable

## Slide 24: Predictable/unpredictable interference
1 Some interference may be predictable
  For such interference, tools are needed in order to define properly the period during which the interference occurs, and possibly characterize the interference
    Some BT can be scheduled in some cases
2 Other interference are difficult to predict long in advance
  This is often the case for BT interference
  We therefore need solutions in order to react properly when interference occurs, and not have reactions that impact even more a Wi-Fi connection.
3 Other possible interference situation
  Some interference are in the middle
    For instance, periodicity for interference period is known, but interference may not always occur during such period

## Slide 25: Interference impact
Obviously, when interference occurs, it impacts ongoing transmissions/receptions
  Reducing SINR if interference occurs during reception, often leading to packet losses
  Or forcing unavailability of the STA with very short notice
    Stopping ongoing transmission if priority is given within the device for another wireless technology, …
Double punishment:
  When interference occurs to a received PPDU and causes packet losses, not only can some packets be lost, but the rate selection mechanisms on the transmitter side may get adjusted to lower the rate of subsequent transmissions, as the transmitter does not know that the packet losses was not due to the channel conditions but was due to unexpected and infrequent interference.