## Slide 1: HT Control field expansion
Date: 2023-11-10
Authors:

## Slide 2: Background
HT Control field and A-Control subfield are useful.
  Only 5 A-Control IDs are reserved for future usage.
  Expansion with the reserved A-Control ID ONES leads to overhead and complexity.
  Overhead: A new field will be added.
  Complexity: HW parses HT Control field. If the HT Control field is HE Variant, then HW extracts A-Control subfield. If the A-Control ID ONES is detected, HW extracts the new added field and the Data field after the new added field. There is only Data field otherwise.

## Slide 3: Another way for A-Control field expansion
Most of exchanged frames between UHR STAs are frames that are not non-A-MPDUs and under a block ack agreement
  Retry subfield is reserved in these frames.
For other frames between UHR STAs, it is possible to always check whether they are retransmissions or not.
  Retry subfield is possible to be reserved in frames between UHR STAs.
Retry subfield can be leveraged for A-Control field expansion in UHR.
  If Retry subfield is equal to 0, it is HT Control field.
  If Retry subfield is equal to 1, it is A-Control Expansion field.
PV | Type | … | Retry=1 | … | +HTC=1
Duration | … | A-Control Expansion
Frame Control
PV | Type | … | Retry=0 | … | +HTC=1
Duration | … | HT Control
Frame Control

## Slide 4: Conclusion
A-Control Expansion field indicated by Retry subfield is proposed.
  It is easier and no overhead, comparing to use A-Control ID ONES.
  New MPDU is as following.
2 | 2 | 6 | 0 or 6 | 0 or 6 | 0 or 2 | 0 or 6 | 0 or 2 | 0 or 4 | variable | 4
Frame Control | Duration/ID | Address 1 | Address 2 | Address 3 | Sequence Control | Address 4 | QoS Control | HT Control/ A-Control Expansion | Frame Body | FCS
B0 B1 | B2 B3 | B4 B7 | B8 | B9 | B10 | B11 | B12 | B13 | B14 | B15
Protocol Version | Type | Subtype | To DS | From DS | More Fragments | Retry/ A-Control Expansion Indicator | Power Management | More Data | Protected Frame | +HTC

## Slide 5: SP
Do you agree to define the following MPDU for transmission between 11bn STAs?
  B11 of Frame Control field is defined as A-Control Expansion Indicator subfield.
  If +HTC subfield is equal to 1 and A-Control Expansion Indicator subfield is equal to 1, A-Control Expansion field overrides HT Control field.
2 | 2 | 6 | 0 or 6 | 0 or 6 | 0 or 2 | 0 or 6 | 0 or 2 | 0 or 4 | variable | 4
Frame Control | Duration/ID | Address 1 | Address 2 | Address 3 | Sequence Control | Address 4 | QoS Control | HT Control/ A-Control Expansion | Frame Body | FCS
B0 B1 | B2 B3 | B4 B7 | B8 | B9 | B10 | B11 | B12 | B13 | B14 | B15
Protocol Version | Type | Subtype | To DS | From DS | More Fragments | A-Control Expansion Indicator | Power Management | More Data | Protected Frame | +HTC