## Slide 1: Parallel coordinated DMG monostatic sensing over multiple channels
Date: 2023-11-14
Authors:
Name | Affiliation | Address | Phone | Email
Yan Xin | Huawei Technologies | Ottawa, ON, Canada |  | yan.xin@huawei.com

## Slide 2: Background
Parallel coordinated monostatic DMG sensing measurement exchange has been specified in Subclause 11.55.3.6.2.3 in P802.11bf D2.1, in which in the sounding phase, as shown in Figure 11-75o (below), multiple sensing responders shall transmit DMG monostatic sensing PPDUs in parallel after the last DMG Sensing Request frame.
For parallel coordinated monostatic DMG sensing, the sensing initiator should assign the transmit beams to different sensing responders (e.g. to avoid interference across multiple sensing responders) (subclause 11.55.3.4)

## Slide 3: Improvement of existing solution
Comments in CID#3331, 3332 and 3333 outline some potential issues for existing solutions for parallel coordinated DMG monostatic sensing in 11bf D2.0
- “Transmissions of sounding PPDUs by multiple sensing responders simultaneously over a single channel in the parallel mode in coordinated monostatic sensing may impact on the synchronization of the PPDUs and/or TRN field, and the subsequent measurement results in the measurement phase.”
- “using the transmit beams assigned by the sensing initiator by setting the TX Beam List subelement in the DMG Sensing Measurement Session element in the DMG Sensing Measurement Request frame … cannot guarantee to fully avoid interference across multiple sensing responders for all scenarios.” The reason is that the environment-based reflected signals are ransom.
To achieve more accurate measurement by using parallel coordinated DMG monostatic sensing, in this contribution an improved solution is considered by transmitting monostatic PPDUs in the sounding phase over multiple DMG channels.

## Slide 4: Parallel coordinated DMG monostatic sensing over multiple channels
In parallel coordinated DMG monostatic sensing over multiple channels, in the sounding phase the monostatic PPDUs are transmitted by respective Responders over different channels, which are specified in the BSS Operating Channels field and Primary Channel field within the EDMG Operation element transmitted by an EDMG AP or an EDMG PCP in subclause 10.23.2.14 (EDCA channel access in an EDMG BSS(11ay)). The procedure in the initial phase and the reporting phase remains unchanged.
An example is shown as below where the Responder STA A transmits a Monostatic PPDU over the secondary channel and the Responder STA B transmits a Monostatic PPDU over the primary channel.

## Slide 5: Sounding channel indication in DMG Sensing Request frame
TDD Beamforming Information field of a DMG Sensing Request frame
In 802.11bf D2.1, BW field (an 8-bit map) is reserved if the Sensing Type is set to Coordinated Monostatic.
For parallel coordinated DMG monostatic sensing over multiple channels, the Initiator can set the BW field to a non-zero value (e.g., all ‘zeros’ except one bit set to ‘one’) to indicate the operating channel to be used by the sensing Responder, which is one of the primary, secondary, secondary1 or secondary2 as specified in the BSS Operating Channels field and Primary Channel field within the EDMG Operation element with the identified STA ID to perform sounding in the sounding phase. The BW fields carried in different DMG Sensing Request frames shall be set to different non-zero values for different sensing Responders with the respective STA IDs.
For parallel coordinated DMG monostatic sensing over single channel, the Initiator shall set the BW field DMG Sensing Request frame to all ‘zeros’.

## Slide 6: DMG Sensing Response frame
The TDD Beamforming Information field of a DMG Sensing Response frame if the Sensing Type in the DMG Sensing Request frame is set to Coordinated Monostatic (9.3.1.25.6 DMG Sensing Response frame)
In some cases, a Responder may not be able to follow the Initiator’s indication carried within the DMG sensing request frame to perform the parallel coordinated monostatic DMG sensing over multiple channels, it is proposed to set both values in the Sounding Duration field and the Report Duration field to be 0..
- The Sounding Duration field indicates the duration of sounding in the next DMG sensing measurement exchange. A value of 0 indicates that the sensing responder does not
transmit any sounding PPDUs.
- The Report Duration field indicates the duration of the report frame transmitted by the sensing responder in the next DMG sensing measurement exchange. A value of 0 indicates
that the sensing responder does not transmit any report frames.

## Slide 7: Revisit of (E)DMG channel access
DMG channel access and EDMG channel access
- BTI, A-BTF, ATI and DTI (including SP and CBAP)
- BTI and ATI shall be transmitted on only the primary channel
- In EDMG, transmissions within a CBAP or an SP may span the primary
channel and the secondary channel(s).
- The schedule of the DTI of a beacon interval shall be communicated through the Extended Schedule element and, in an EDMG BSS, also through the EDMG Extended Schedule element.
- An EDMG AP or EDMG PCP may use the EDMG Extended Schedule element to allocate an SP or a CBAP over channels with different bandwidths and the allocations may be overlapped.

## Slide 8: Indications of parallel SP allocations and sounding channel in (EDMG) Extended Schedule element
During the parallel coordinated DMG monostatic sounding phase, different SP allocations with different Allocation IDs, which overlap in time but operate over multiple channels, are specified in the Extended Schedule element and/or EDMG Extended Schedule element to respective Responders for transmissions of respective monostatic PPDUs in parallel.
In the parallel coordinated DMG monostatic sounding phase, both the Source AID and the Destination AID in the Extended Schedule element and/or in the EDMG Extended Schedule element for each SP with a unique Allocation ID are set to be the corresponding Responder AID.
For each SP allocation, the BW subfield in the Channel Allocation subfield in the EDMG Extended Schedule element is set to different values to specify that different Responders perform sounding/measurement using different channels during the parallel coordinated monostatic sounding phase.
In the sounding phase, the responder that receives the last Request frame in order transmits monostatic sensing PPDU over the primary channel no later than a SIFS after transmitting the Response frame without performing CCA. This responder can be polled first by the Initiator (no channel switching is needed) to allow more time for other responders to switch the channel.

## Slide 9: CCA in secondary channels in EDMG (subclause 10.3.2)
An EDMG STA shall maintain physical and virtual CS on a primary channel. To perform EDCA channel access in an EDMG BSS, an EDMG STA shall support performing energy detection on each of its supported channels.
An EDCA TXOP is obtained and the slot boundaries are determined based solely on activity of the primary channel. Once an EDCA TXOP has been obtained, channel access over other secondary channels are determined based on whether or not the CCA for those channels is idle during an interval of PIFS immediately proceeding the start of the TXOP.

## Slide 10: Parallel coordinated DMG monostatic sensing over multiple channel in CBAP with a TXOP
In the sounding phase, the responder that receives the last Request frame in order transmits monostatic sensing PPDU over the primary channel no later than a SIFS after transmitting the Response frame without performing CCA. This responder can be polled first by the Initiator (no channel switching is needed) to allow more time for other responders to switch the channel.
The Responder that receives a DMG Sensing Request frame with an assigned STA ID that is not the highest one, may perform CCA on one of the secondary channels, which is indicated in the BW field in the correspondent DMG Sensing Request frame, during an interval of PIFS immediately proceeding the start of the monostatic sounding PPDU transmission.
DMG sensing report
DMG sensing report

## Slide 11: Summary
Parallel coordinated DMG monostatic sensing over multiple channels was proposed.
Sounding channel indication by specifying the BW field in DMG Sensing Request frame was considered.
Channel access methods for SP allocation and TXOP operation in CBAP allocation for parallel coordinated DMG monostatic sensing over multiple channels were discussed.

## Slide 12: SP
Do you support the parallel coordinated DMG monostatic sensing over multiple channels mechanism proposed in 802.11-23/2025r2?
- Yes
- No
- Abstain

## Slide 13
Backup

## Slide 14: Extended Schedule element (9.4.2.130, 802.11REVme D4.0)
Extended Schedule element carried in DMG Beacon frame in BTI or Announce frame in ATI
Allocation type:

## Slide 15: EDMG Extended Schedule element (9.4.2.267, 802.11REVme D4.0)
EDMG Extended Schedule element carried in DMG Beacon frame or Announce frame. An EDMG AP or EDMG PCP may use the EDMG Extended Schedule element to allocate an SP or a CBAP over channels with different bandwidths. For partially or fully overlapping allocations, both the source AID and the destination AID of each allocation shall be different from both the source AID and destination AID of other overlapping allocation.