## Slide 1: Further Discussion on AMP PAR
Date: 2023-11-17
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
HaoWang |  |  |  | 
Doc.: IEEE 802.11-23/2042r2
November 2023

## Slide 2: Abstract
  In this submission, whether and how to define the restrictions on agreed PAR are discussed.
Doc.: IEEE 802.11-23/2042r2

## Slide 3: Restrictions on the Agreed PAR
Agreed PAR text
Restriction 1: restrictions on data communication of AMP devices operating in 2.4 GHz band in order to minimize the impacts on the legacy devices
Restriction 2: restrictions on the frequency band where there can be dedicated wireless power transfer for AMP devices

## Slide 4: Restriction 1 on Data Communication
  Even though AMP devices need to compete for the channel with other legacy devices operating on 2.4 GHz, the unique features of AMP traffic, such as extremely long transmission interval, small payload, naturally minimize the co-existence impact on the legacy devices.
  The transmission power of AMP devices is essentially bounded by the limited harvested energy. Thus the interference generated by AMP devices, especially when the required communication distance is short in some use cases, is expected to be small.

## Slide 5: Restriction 1 on Data Communication
  To address the concern that there may be impact on legacy traffic, low priority channel access class can be configured for Ambient IoT traffic
    Negligible impact on legacy devices on 2.4 GHz, especially for those with higher channel access priority ([1]-[3])
    Longer latency for AMP devices but acceptable for AMP use cases.
    No impacts on AMP traffic when no other higher priority traffic exists thus there is flexibility.
  If such restriction is needed, low priority to access the channel can be given to AMP traffic by setting the channel access category as AC_BK.
  .

## Slide 6: Restriction 2 on Wireless Power Transfer
  Power link design and specification are only needed for proactive wireless power transfer where the wireless power transfer is proactively performed /controlled by the AP/energizer, e.g., periodicity, on/off in an on-demand manner, etc.
  Passive energy harvesting without specification can be applied up to implementation, e.g., AMP devices placed near an existing AP can detect the signal from the AP once the signal strength is above certain threshold.
  Wireless power transfer is from transmitter perspective and energy harvesting is from receiver perspective.
  If the restriction is needed, wireless power transfer can be specified for Sub-1 GHz frequency band.

## Slide 7: Proposal for PAR
  This amendment defines:
    at least one mode of data communication in sub-1 GHz band
    at least one mode of data communication in 2.4 GHz band with the AMP access category (AC) being set to AC_BK (background)
    at least one mode of wireless power transfer RF energy harvesting in sub-1 GHz band, to support RF energy harvesting.

## Slide 8: Group PAR Discussion
  PAR proposed in [4], no conclusion
  This amendment defines:
    at least one mode of ultra-low power data communication link sub-1GHz or 2.4 GHz
    at least one mode for certain type of AMP IOT devices to connect with legacy WLAN network in 2.4GHz band
    at least one mode of wireless RF power transfer in sub-1GHz or 2.4GHz
    at least one mode to support positioning function

## Slide 9: Group PAR Discussion
  Agreed AMP PAR baseline in [5]
  This amendment defines:
    at least one mode of data communication in sub-1 GHz band
    at least one mode of data communication in 2.4 GHz band with [TBD restriction]
    at least one mode of RF energy harvesting [in TBD band].

## Slide 10: Proposal for AMP PAR Update
  This amendment defines:
    at least one mode of data communication in sub-1 GHz band
    at least one mode of data communication in 2.4 GHz band with the AMP access category (AC) being set to AC_BK (background)
    at least one mode wireless power transfer RF energy harvesting in sub-1 GHz band, to support RF energy harvesting.

## Slide 11: Motion 1
Approve the following modification to the AMP PAR document (11-23/1006r3):
  This amendment defines:
    at least one mode of data communication in sub-1 GHz band
    at least one mode of data communication in 2.4 GHz band with the AMP access category (AC) being set to AC_BK (background)
    at least one mode of wireless power transfer RF energy harvesting in sub-1 GHz band, to support RF energy harvesting.
  •Moved:
  •Seconded:
  •Result:

## Slide 12: Reference
IEEE 802.11-23/1601r1, AMP Communication Channel Usage Estimation
IEEE 802.11-22/1627r6, AMP Communication Channel Usage Estimation Part 2: AC_BK
IEEE 802.11-23/1994r0, Simulation on coexistence of AMP traffic and existing traffic
IEEE 802.11-23/1190r0, Further discussion on AMP PAR
IEEE 802.11-23/1006r3, ieee-802-11-amp-sg-proposed-par
Doc.: IEEE 802.11-23/2042r2
November 2023