## Slide 1: Initial Control / Response Control frame transmission rules
Date: 2023-11-13
Authors:

## Slide 2: Introduction
Initial Control frames (e.g., RTS or MU-RTS) serve to poll for a STA’s presence before the actual data frame transmission.
Roughly, a STA responds with a CTS if NAV is not set and it receives the RTS or MU-RTS.
However, absence of CTS does not prevent the ICF transmitter to attempt initiating more TXOPs.
  Increases BO count at the initiator STA with repeated failures => increased latency, more power etc.
  Creates unnecessary interference to medium for other STAs.
Clearly, having some rules for ICF transmitter to regulate its transmissions would improve network efficiency.

## Slide 3: Proposal
After experiences an ICF failure to STA-2, a STA-1 limits the number of future ICF transmissions to STA-2 for a certain timer duration (e.g., max PPDU length or max PPDU length/2).
  If STA-1 is AP, then it may still transmit to other non-AP STAs during this time following baseline channel access rules.
STA-1 resumes regular channel access rules after receiving any valid PPDU from STA-2 since that indicates STA-2 is available.
  Since UL transmissions are typically less frequent, may consider different timer duration rules for UL and DL.
Note: the rules then are similar to medsync rules defined for EMLSR and NSTR in 11be and we may also consider just reusing/updating those rules.

## Slide 4: Proposal (contd.)
For the case when the STA-2 successfully receives the ICF but is unable to respond in baseline because NAV is set, we can allow the STA-2 to send a short Control frame in response that signals the remaining NAV duration.
  Note: similar exceptions to short frames are there for 11ax TF transmissions.
  This is then similar to DTS frame transmission in DMG and the short Control frame may have a similar design.
Any third-party STA that receives the short Ctrl frame would not set its NAV from this frame (e.g., set any Duration field to zero).
The design can be well aligned with other proposals about STAs unavailability due to any types of coex issues
STA-1
STA-2
NAV set at STA-2
ICF
RCF
(busy, be back in X ms)
ICF
X ms
ICF
ICF
ICF
Will not be sent
Notes: CF-end cases maybe rare but could be handled by having STA-2 send some frame to STA-1..

## Slide 5: Evaluation of RTS retransmission events
We plot of ratio of CTS misses per transmitted RTS as function of traffic load in network corresponding to events where NAV will be set at intended destination.
STA-1 generates a packet for STA-2 on average every 2ms and attempts to initiate a TXOP with an RTS.
A third party STA-3, hidden to STA-1, is receiving some traffic which causes STA-3 to often set NAV around STA-2.
It shows that as the traffic load at STA-3 increases, there is significant number of occurrences where a single event of NAV being set at STA-2 would cause repeated RTS failures at STA-1.
STA 2
STA 3
STA 1
STA 3 source of data
Data frame every 2 ms