## Slide 1: DL Sounding Options
Date: 2023-11-02
Authors:
Name | Affiliation | Address | Phone | Email
Ravi Gidvani | Samsung |  |  | ravi.gidvani@samsung.com
Eunsung Jeon | Samsung |  |  | eunsung.jeon@samsung.com
Chulho Chung | Samsung |  |  | ch29.chung@samsung.com
Jung Woon Lee | Samsung |  |  | jw815.lee@samsung.com
Myeongjin Kim | Samsung |  |  | mj1108.kim@samsung.com
Hunmin Shin | Samsung |  |  | hunmin.shin@samsung.com
Mark Rison | Samsung |  |  | m.rison@samsung.com
Michail Koundourakis | Samsung |  |  | m.koundou@partner.samsung.com

## Slide 2: Background
Concept of DL Beamforming was first introduced in 802.11 n.
DL Beamforming consists of two parts
  Sounding :- This stage Beamformer exchanges frame sequence with Beamformee to collect CBR from the station
  Beamforming:- Once the channel info is available, AP uses this info to direct beam formed PPDUs towards stations.
Sounding sequence introduces overhead. This overhead is compensated by improved MCS.
Standards do not mandate / recommend periodicity of sounding sequence. Beamformer can initiate sounding sequence at different intervals depending on its implementation.

## Slide 3: Issues Observed
It is observed that certain Beamformer implementations will initiate sounding sequences very frequently. This can be a result of unintentional algorithmic behavior, corner conditions or interoperability issue. Such condition can lead to degradation of RX performance.
There are also conditions wherein after successful sounding, Beamformee is unable to receive beamformed PPDUs successfully.
When such conditions detected Beamformer has option of excluding station from beamforming sequence completely. It depends on implementation of Beamformer. However a Beamformee has no such option to temporarily disable sounding.
There are other conditions such as internal state of Beamformee where in for power saving or memory reasons Beamformee may temporarily want to opt out of beamforming in exchange for lower throughput.

## Slide 4: Proposal
Proposal is provide mechanism for Beamformee to disable beamforming/sounding temporarily.
Three possible ways this can be done :
  Introducing a single bit to indicate DISABLE_BEAMFORMING. This is will tell beamformer to completely opt in / opt out of beam beamforming completely (i.e. both sounding and beamforming)
  Introducing two bits to indicate DISABLE BEAMFORMING (completely disable/enable beamforming) and DISABLE SOUNDING (using implicit or stale CSI Beamforming when set) to peer. This may also need corresponding Capability bits to be added in MAC or PHY capability.
  Introducing three bits to indicate DISABLE SU_BEAMFORMING (completely disable/enable beamforming for SU beamforming), DISABLE MU_BEAMFORMING (completely disable/enable beamforming for MU beamforming) and DISABLE SOUNDING (using implicit or stale CSI Beamforming when set) to peer. This may also need corresponding Capability bits to be added in MAC or PHY capability.
Similar concept exists for Disabling trigger where a station can opt out of triggered access under conditions when station finds it more beneficial to stay in OFDM mode instead of OFDMA.

## Slide 5: Changes To Standard
Options to introduce bits to disable beamforming/sounding temporarily are as follows
  OMN fields
  OMN Action frame
  OM indication
  Define NEW Action frame and/or new operating indications
Capability bits can be one bit per capability depending on which option group decides.

## Slide 6: References
IEEE Std 802.11™-2020
IEEE P802.11be™/D4.0