## Slide 1: TGbi Epoch proposal
Date: 2023-10-28
Authors:

## Slide 2: Abstract
Define an epoch for when a client should change the Over The Air (OTA) MAC address that is being used.

## Slide 3: Epoch Partitioning Idea
Partition time into epochs based on network trust*:​
Fully Untrusted – Open/OWE – Rotate every 5 mins ​maximum
Semi Untrusted – PSK – Rotate every 10 mins maximum
Trusted - 802.1X - Rotate every 10 mins maximum – optional​ (enabled if using IRM)
  Passpoint treated as Fully Untrusted
By defining epochs based on association duration, both the AP STA and non-AP STA will know when they should rotate to the new IRM​, calculation could happen anytime during the current epoch
This allows for a dynamic approach as not all non-AP STA will rotate at the same time, making it more difficult for an eavesdropper to know a rotation happened vs STA joining/leaving
*non-AP STA can override the default network type in the supplicant configuration, and can delay rotation due to traffic type

## Slide 4: Update/Sunset
Announce time – Tell AP-STA when non-AP STA will start to use new OTA mac – sent in a protected frame​
e.g. in 1 minute non-AP STA will use new OTA mac​
Once announce time has elapsed, Sunset timer starts.​
Sunset timer – DTIM period * 5​
This should allow frames already queued to be transmitted
Old mac shall not respond and AP shall not forward packets for old OTA mac once Sunset timer has elapsed.

## Slide 5: Straw Poll
Would you support using AKM based/network trust level, for Epoch definition?