## Slide 1: [Collision Evaluation]
Date: 2023-11-13
Authors:
Name | Affiliations | Address | Phone | email
Jerome Henry | Cisco |  |  | jerhenry@cisco.com
Domenico Ficara | Cisco |  |  | dficara@cisco.com
Javier Contreras | Cisco |  |  | jacontre@cisco.com
Stephen Orr | Cisco |  |  | sorr@cisco.com

## Slide 2: Abstract
This document provides evaluation on IRM collision over large scale scenarios
Rev.0 – initial version

## Slide 3: Single IRM Collision
Collision of Random Mac selection is a special case of “Birthday Problem”
  On set of N random people, at least 2 may share a birthday
  Birthday paradox shows that only 23persons are needed for a 50% probability of matching birthday
  In general, this is probability calculation for k number of devices having a pair collision over a large address space N
  Address space here is 70368744177664, (246)
Formula: p(n) = 1 - [(n-k)!/n!]
Probability for just 2 devices to have a collision = 1 - (2^46-1)/(2^46) = 1/2^46
This is roughly 1 - 0.999999999999986 = 1 in almost 1 thousand billion
Yes, this is clearly not an issue

## Slide 4: IRM Collision – Medium Size Scenario
The probability grows exponentially, not linear
Scenario for 20,000 devices, assuming one IRM selection per device, no storage
(middle size University scenario)
Total pairs: (20,000 *19999/2) = 199,990,000
Chance per pair 0.00000284203
Chance different 99.99971579752
Chance of match 0.00028420248
Odds are 1 in 4999

## Slide 5: IRM Collision – Day Activity
Same 20K clients
  335,000 EAP-4way per day
  600,000 Roam attempts, 40% are FT
Total pairs: (335,000 *334,999/2) = 56112332500.00
Chance per pair: 0.0007974042
Chance different: 99.92029136374
Chance of match: 0.07970863626
Odds are 29.5 : 340.85 (1 : 11.55) Possibly several daily per year

## Slide 6: IRM Collision – Large Scale
Large University:
  80.000 devices
  IRM stored for 7 days, one IRM per day (very conservative)
  Population of 560,000 “selection” events for collision
Total pairs: (560,000 *559999/2) = 156799720000
Chance per pair 0.00222825804
Chance different 99.77742226837
Chance of match 0.22257773163
Odds are 89 : 311 (= 1 : 3.49) Several events per day

## Slide 7: Defining a Collision
IRM Device has been authenticated
Non-AP STA sends IRM IE, this address is not the current TA, showing intention to use it
Scenario 1:
  Address present in the IE matches IRM in use by another STA
  In use: STA has an active valid association within the ESS (beyond AP scope)
  This covers random collision of two active clients
Scenario 2:
  Address present in IE matches stored IRM over X time
  IRM is not currently in use by active STA
  IRM storage may be beyond this standard, as it implies usage scenarios (i.e. policies, debugging long term, DHCP, etc.)

## Slide 8: Take Aways
For small number of devices, the probability is almost null
For large scale with retention, a collision will happen several times per year/day
It is advisable to define collision handling procedures in 802.11bh
“Random” selection implementation will have bias: devices may not use full address space, or poor RNG operations: In practice odds will be higher

## Slide 9: Proposals
AP STA must compare IRM only for authenticated devices
Define collision detection flag on EAPoL M3
  Avoid collision handling during Association response to avoid DoS
  Upon collision detection warning, STA generates a new IRM
Collision may have upper layer implications: e.g., linking user ID to devices in use
In case of collision on M2, AP STA will reply with Status = 2 (from in Okan's 1262/r0), and STA has to repropose IRM through protected Action frame exchange had proposal for IRM
Failure to obtain a non-collision IRM will lead to next 4WAY to fail

## Slide 10: References
Birthday problem: https://en.wikipedia.org/wiki/Birthday_problem
Understanding Birthday Paradox: https://betterexplained.com/articles/understanding-the-birthday-paradox/
Probability to Odds conversion: https://goodcalculators.com/probability-odds-conversion-calculator/