## Slide 1: Enhanced Acknowledgement for Low Latency Communication Follow-Up
Date: 2024-01-08
Authors:

## Slide 2: Abstract
In this presentation we present a follow-up to the enhanced acknowledgement method to reduce delay of a lower latency traffic transmission presentation [1].

## Slide 3: Early Acknowledgement of Low Latency Packets
Increased reliability and support of lower latency are two of the main improvement areas of the 802.11bn project.
An important part of the low latency communication is verifying that the packets arrive correctly.
With multi link communication and simultaneous transmit and receive (STR) capability, we need to allow to acknowledge MSDUs or A-MSDUs with low latency requirement before the end of the PPDU transmission.

## Slide 4: Early Acknowledgement of MPDUs
We assume that transmitter and receiver are multi-link and simultaneous transmit and receive capable. The payload is transmitted from the first link.
After the reception of the low latency MPDU, receiver sends a feedback frame to indicate reception status from the second link.

## Slide 5: Retransmission Option 1
If the feedback frame indicates the low latency MPDU is received in error. The second link could be used to transmit the MPDU received in Error.

## Slide 6: Retransmission Option 2
Another option is adding the MPDU received in error at the end of the PPDU, with dynamic PPDU modification.

## Slide 7: Early Indication of SIG Field Errors
Feedback frame could be utilized to indicate if there is an error in the PHY Header.
Notes: Mention RTS CTS or TXOP, indicate ppdu in all slides…

## Slide 8: Discussion
    C: Sending the feedback in another link, you are using STR. Have to make the 2nd link always available?
    A: Both devices should have STR capability. The device can transmit the feedback using the baseline procedure ( e.g. using EDCA) .

## Slide 9: Conclusion
In this contribution, we provide a feedback scheme to early indication of error for low latency transmissions.

## Slide 10: References
[1] 11-23/1201r0 “Enhanced Acknowledgement for Low Latency Communication”

## Slide 11: Straw Poll
Do you support the following text?
An MLD may transmit, on one link, the acknowledgement(s) of MPDU(s) of a PPDU received on another link, while receiving the remaining MPDU(s) of the PPDU.
Yes
No
Abstain