## Slide 1: Coex Enhancement for XR Use Cases
Date: 2024-04-08
Authors:
Name | Affiliations | Address | Phone | email
Guoqing Li Kumail Haider Carlos Aldana Claudio De Silva Davide Magrin Connor Kennedy Dong Zheng | Meta |  |  | guoqingli@meta.com

## Slide 2: Problem Statement
XR devices may use multiple radios such as Wi-Fi and Bluetooth and need to coex well
Device constraint issue
  Due to size and cost, these radios may share RF components and have to time share the RF resources
  Due to possible low isolation, one radio’s Tx may destroy another radio’s Rx
  In addition, Tx+Tx or Rx+Rx may not be possible depending on device’s architecture design and cannot be assumed as default
AP rate adaptation issue
  BT traffic interval may be at a few ms (<10ms) and Wi-Fi may not have sufficient time to notify AP its unavailability using power save signaling (e.g., PM) when switching to BT activity
  As a result, downlink throughput/latency may be greatly degraded from AP’s fast rate scaling down due to lack of response from STA
Wi-Fi packet duration issue
  BT typically has periodic traffic and need to Tx/Rx at predicted time slot
  However, AP/STA may continue Tx into BT’s Tx/RX slot, leading to either Wi-Fi packet loss or BT packet loss

## Slide 3: Coex Enhancement
A client (STA) device may be aware of its co-located traffic profile from other technologies (e.g., BT) and traffic interval and may shape its Wi-Fi Tx/Rx traffic to fit into non-overlapping intervals
STA may be able to control its uplink Tx activity, but has not mechanism to control AP’s DL activity
Proposal
  Define a mechanism that allows STA to indicate to AP periods of potential unavailability due to coex issues
  Define a mechanism that allows STA to request AP to control the following
    Max DL packet duration
    Min Tx interval
    Modified/slow DL rate control upon missing UL BA
  BT (or other tech.) activity usually will last a few seconds to minutes, thus these parameters can be negotiated through management frames

## Slide 4: STA Indication of coex activity
STA devices typically have good estimation of traffic profile of coex technologies
  These traffic profiles tend to have periodic, predictable intervals and data rates (channel usage duration requirements)
  E.g., a BT use case may be invoked such as audio streaming, leading to Xms BT usage every CI (e.g., 10 ms)
A STA may proactively share this coex schedule with the AP
  At the minimum, coex activity duration and interval (and possibly future end time) may be shared (existing methods may be discussed, or new methods may be devised)
  STA may also indicate frequency/spatial resources if coex operation partially impacts Wi-Fi availability/operation
  AP may modify its operation for the STA based on coex info (e.g., always use RTS/CTS before DL TX, modify rate adaptation, modify freq. resource allocations etc. during periods of coex activity)

## Slide 5: BA agreement modification to control DL duration
A client (STA) device may use DL BA agreement to influence the DL packet duration
  For example, tear down BA agreement/disable A-MPDU for DL transmission to reduce DL PPDU duration
However, there is lack of mechanisms (or limitations) for STA to trigger the re-setup of DL BA
Propose to define a mechanism for STA to prompt AP to set up DL BA agreement or to modify DL BA agreement in an unsolicited manner

## Slide 6: Proposed Spec Changes
Define management frame(s) to
  Indicate that STA allows STA to indicate to AP periods of potential unavailability/constrained operation due to coex issues
  Indicate STA’s coex requirements for DL transmission
    Modified rate adaptation during coex periods
    Max PPDU duration
    Min Tx interval
    Allows STA to prompt AP to modify/setup DL BA