## Slide 1: TGbi – Analysis simultaneous MAC address change
Date: 2023-11-14
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
J. Levy | Interdigital |  |  | 

## Slide 2: Device profiling
Device profiling can be done based on following flow characteristics
  Time series:
    Packet lengths
    Inter packet arrival
    Direction of the flow
  Summarized data across a time window
    The number of packets sent from the device to AP.
    The number of packets received by the device from AP.
    The variance of inter-arrival time.
    The average number of consecutively sent packets before seeing a received packet.
    The average number of consecutively received packets before seeing a sent packet.
    Total number of bytes in sent packets.
    Total number of bytes in received packets.
    Number of different sizes in sent packets.
    Number of different sizes in received packets.
    Maximum packet size.
    Mode of sent packet lengths (i.e., the packet size that appeared most in the monitoring window).
    Mode of received packet lengths.
    The variance of sent packet size distribution.
    The variance of received packet size distribution.
  Macro metrics
    Bandwidth profile of the device

## Slide 3: Device profiling
Based on the metrics shown in previous slide, a device can be profiled in short periods of time

## Slide 4: Considerations
Changing MAC addresses simultaneously in cases of device profiling based on traffic characteristics may actually be a bad idea
  You will signal the attacker when it needs to look for changes
It may be better to go for mechanisms where STAs may or may not change the MAC address
Simultaneous use of multiple MAC addresses where the packets of a flow are spread will improve the privacy characteristics

## Slide 5: References
M. Alyami, I. Alharbi, C. Zou, Y. Solihin and K. Ackerman, "WiFi-based IoT Devices Profiling Attack based on Eavesdropping of Encrypted WiFi Traffic," 2022 IEEE 19th Annual Consumer Communications & Networking Conference (CCNC), Las Vegas, NV, USA, 2022, pp. 385-392, doi: 10.1109/CCNC49033.2022.9700674.
Tadayoshi Kohno, Andre Broido and Kimberly C Claffy, "Remote physical device fingerprinting", IEEE Transactions on Dependable and Secure Computing, vol. 2, no. 2, pp. 93-108, 2005.
BR Chandavarkar et al., "Detecting rogue access points using kismet", 2015 International Conference on Communications and Signal Processing (ICCSP), pp. 0172-0175, 2015.