## Slide 1: An Approach to Enhance the Reliability for Wi-Fi Networks
Date: 2023-11-16
Authors:

## Slide 2: Introduction (1/2)
  The UHR study group (current IEEE 802.11 bn) was founded to look into the solutions that could enhance throughput, enhance reliability, reduce latency, and improve power consumption [1].
  Several technologies have been proposed for consideration in UHR, including
  Multi-AP [2-5]
  Preemption [6]
  mm-Wave MLO [7-8]
  MIMO enhancements [9]
  Power efficiency [10-11]
  Redundant transmission [12]

## Slide 3: Introduction (2/2)
Multi-user MIMO (MU-MIMO) and Orthogonal Frequency Division Multiple Access (OFDMA) are pivotal for enhancing overall network performance. UHR study group aims at improving reliability and reducing latency in such systems.
One effective method for improving reliability and reducing latency is through redundant transmission [12]. However, challenges still exist concerning the type of data to be transmitted redundantly and the appropriate transmission method.
In this presentation, a mechanism is introduced that leverages the capabilities of MU-MIMO and OFDMA to enhance reliability and reduce latency based on intelligently design redundant version of data.

## Slide 4: Proposed Method
Enhancing Reliability in MU-MIMO Systems:
  Supplementing conventional downlink data stream with an intelligently designed data stream that is broadcasted to users.
Transmission Facilitation:
  The intelligently designed data stream optimizes the transmission of users' data stream segments, particularly those prone to encountering deep-faded sub-channels.
Simultaneous Improvement:
  Intuitively the proposed approach enhances reliability and reduces the latency in MU-MIMO systems.

## Slide 5: Transmitter Side
The construction of the intelligently designed data stream follows these steps:
For any user, the data corresponding to indices of subcarriers that will face deep-faded sub-channels is selected and incorporated into the intelligently designed data stream.
The data from different users is arranged in a concatenated form within the intelligently designed data stream.
Afterwards, the intelligently designed data stream is broadcasted in conjunction with conventional transmission, utilizing different power levels.

## Slide 6: Receiver Side (case 1)
The power of intelligent stream is lower than other streams. The following are the steps:
Users can decode their data from the received signal, employing conventional MU-MIMO reception techniques.
If a user aims to enhance reliability, it will undertake the following steps:
Extraction of Deep-Faded Sub-channel Data: The user extracts data from the received signal based on the indices of subcarriers corresponding to deep-faded sub-channels.
Intelligent Broadcasted Data Stream Retrieval: Subsequently, the user retrieves its corresponding segment from the intelligently designed data stream using successive interference cancellation (SIC).
Maximum Ratio Combining: Finally, the user combines the data extracted in steps (a) and (b) using Maximum Ratio Combining.

## Slide 7: Receiver Side (case 2)
The power of intelligent stream is higher than other streams. The following are the steps:
Users begin by detecting the intelligent data stream.
After detection, they extract their conventional data stream using successive interference cancellation (SIC).
Users then choose data symbols from the conventional stream that correspond to deep-faded sub-channels.
Finally, the data from step (3) is combined with the corresponding segment from the intelligently designed data using Maximum Ratio Combining.

## Slide 8: Conclusions
This presentation presents a novel method for increasing reliability by supplementing the conventional downlink data stream with an intelligently designed data stream that is broadcast to users.
In MU-MIMO systems, the proposed technique improves reliability while decreasing latency.
This method is especially effective in mitigating reliability degradation caused by data transmitted over deep-faded sub-channels because the transmission of such data in the intelligently designed data stream, combined with combining at the receiver, serves to improve overall reliability.

## Slide 9: Straw Poll
Are you in favor of supporting the new concept of transmission for MU MIMO networks in TGbn?
Yes:
No:
Abstain:

## Slide 10: References
[1] 11-22/708 “Beyond be - Next Step”.
[2] 11-22/1516 “Considerations on Multi-AP Coordination”
[3] 11-22/1530 “Multi AP coordination for next-generation Wi-Fi”
[4] 11-22/1567 “C-OFDMA throughput analysis in various mesh backhaul scenarios”
[5] 11-22/1556 “Multi-AP Coordination for Low Latency Traffic Delivery”
[6] 11-22/1393 “Latency Reduction Scheme for UHR”
[7] 11-22/1395 “Thoughts on high frequency band”
[8] 11-22/1595 “Some questions to answer in the SG”
[9] 11-22/1649 “MIMO interference suppression for enhanced reliability”
[10] 11-22/1790 “Green AP and resilience requirements for home networks”
[11] 11-22/1414 “Low Power Listening Mode”
[12] 11-21/1205r0 “Redundant Transmission for Enhanced Reliability and Reduced Latency”