## Slide 1: Power Save for UHR
Date: 2024-01-12
Authors:

## Slide 2: Introduction
According to 11bn PAR [1] , more power saving of non-AP STA is one of key features for TGbn
In this contribution, we propose operation for reducing power consumption of a non-AP STA in Triggered TXOP Sharing procedure

## Slide 3: Recap: Triggered TXOP Sharing in EHT
An AP can allocate a portion of an obtained TXOP to one associated non-AP EHT STA for transmitting one or more non-TB PPDUs.
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
Non-TB PPDU
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
TXS Mode 1
TXS Mode 2

## Slide 4: Recap: Triggered TXOP Sharing in EHT
During TXS allocated time, non-AP STAs that don’t participate in the procedure are still in awake state although they want to save more power and they don’t intend to communicate with AP
In TXS mode 2, the non-AP STA allocated by the AP may return the remaining time of the allocated time if the STA finished the transmission earlier
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
BA
Non-TB PPDU
QoS Null
ACK
NAV
TXOP
DL frame
BA
DL frame
BA

## Slide 5: TXS Power Save (PS) Operation – Mode 1
When a STA receive an MU-RTS TXS Trigger frame, if the STA is not scheduled and supports the TXS PS Mode 1, the STA enters the doze state
During the TXS allocated time, the AP does not transmit a frame to the STA and the AP can transmit a frame to another STA
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
BA
Non-TB PPDU
QoS Null
ACK
Doze state
DL frame
BA
DL frame
BA

## Slide 6: TXS Power Save (PS) Operation – Mode 1
The STA can enable or disable the TXS PS Mode 1 before the TXS procedure
STA may enter the doze state only in case of enabling the TXS PS Mode 1
  Ex1) if the STA has lower battery power, the STA can enable the TXS PS Mode 1
  Ex2) if the STA has higher battery power or wants to receive DL frame as soon as possible (e.g., latency sensitive (or urgent) traffic), the STA may disable the TXS PS Mode 1
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
QoS Null
ACK
Doze state
DL frame
BA
Enabling TXS PS 1
ACK

## Slide 7: TXS Power Save (PS) Operation – Mode 2
If the TXS assigned STA returns the remaining duration, the STA enters the doze state
AP does not transmit a frame to the STA that enters the doze state during the remaining duration
The detailed procedures are TBD (e.g., additional signalling, remaining duration)
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
BA
Non-TB PPDU
QoS Null
ACK
Doze state
DL frame
BA
DL frame
BA

## Slide 8: Conclusion
11bn need to enhance the power saving operation for non-AP STA further
We proposed the methods for reducing the power consumptions of non-AP STAs in TXS procedure
  Unassigned STAs may enter the doze state during the TXS allocation duration
  Assigned STAs may enter the doze state if the STAs return the remaining duration to the AP
  AP should not transmit a frame to those STAs during the duration

## Slide 9: References
[1] 11bn PAR 23/0078