## Slide 1: Further discussion on Dynamic Subband Operation
Date: 2023-11-14
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Srinath Puducheri |  |  |  | srinath.puducheri@broadcom.com
Shubhodeep Adhikari |  |  |  | shubhodeep.adhikari@broadcom.com
Matthew Fischer |  |  |  | matthew.fischer@broadcom.com
Vinko Erceg |  |  |  | vinko.erceg@broadcom.com
Notes: November 2012

## Slide 2: Overview
Background
Dynamic Subband Operation
Protocol details
Capability details
Straw Polls

## Slide 3: Background
802.11be supports 320MHz as the maximum bandwidth of operation on any one link. 802.11bn may support even higher
State of the art 802.11bn APs are expected to support at least 320MHz bandwidth of operation
However, many 802.11bn non-APs may support only a smaller bandwidth (160MHz or lower) as the maximum bandwidth of operation.
Such mismatch in the capabilities between the AP and the non-AP would result in wastage of bandwidth capabilities of the AP whenever the AP interacts with smaller bandwidth non-APs.
In [2], a scheme Dynamic Subband Operation was proposed to overcome this limitation by allowing the 320MHz AP to dynamically indicate to a lower bandwidth non-AP, Tx/Rx opportunity outside of its operating bandwidth

## Slide 4: Dynamic Subband Operation
The scheme is applicable to any AP/non-AP bandwidth combinations where the bandwidth supported by the AP is higher than the non-AP.
Dynamic Subband Operation can enable the AP to utilize its additional bandwidth in a dynamic manner on a per-TXOP basis whenever it wins channel access on it.
  The AP can dynamically decide to allocate non-APs on different parts of its operating bandwidth and the non-APs to allocate in this manner depending on bandwidth availability, channel conditions and QoS requirements
  This results in much better resource utilization and system performance compared to HE SST.
The operation could be DL or trigger-based UL inside each dynamically allocated opportunity

## Slide 5: Protocol details
The AP sends to the DSO non-AP being scheduled, a "subband-switch control frame", which is a special initial control frame (could be a modified MU-RTS or BSRP or a newly defined frame) that indicates transition to the RU outside the operating bandwidth
The subband-switch control frame has sufficient padding to cover subband switch latency (i.e. latency required by the non-AP to switch from its operating bandwidth to the indicated RU
The subband switch latency depends on the non-AP implementation and is negotiated during the DSO capability signaling.
Depending on the negotiated capabilities of the DSO-capable non-AP, the following options are possible:
  Option 1: The subband-switch initial control frame is used only for subband switch by DSO non-APs and does not elicit any response. SIFS later, the AP sends a second control frame (which can be a regular MU-RTS/BSRP) that elicits a response in the new RU
  Option 2: The subband-switch initial control frame is used for subband switch by DSO non-APs and elicits a response in the new RU. This is especially possible if post-FCS MAC padding ([3]) is used
The subband-switch initial control frame may be in non-HT duplicate format, again depending on the negotiated capabilities.
Thereafter, the DSO TXOP can contain multiple SIFS-spaced DL/triggered UL exchanges with the DSO non-APs.
At the end of the TXOP (for example, detected through a gap of SIFS+delta time), the DSO non-AP switches back to operating on its operating bandwidth overlapping the primary 20MHz.

## Slide 6: Protocol details
The AP sends to the DSO non-AP being scheduled, a "subband-switch control frame", which is a special initial control frame (could be a modified MU-RTS or BSRP or a newly defined frame) that indicates transition to the RU outside the operating bandwidth
The subband-switch control frame has sufficient padding to cover subband switch latency (i.e. latency required by the non-AP to switch from its operating bandwidth to the indicated RU
The subband switch latency depends on the non-AP implementation and is negotiated during the DSO capability signaling.
Depending on the negotiated capabilities of the DSO-capable non-AP, the following options are possible:
  Option 1: The subband-switch initial control frame is used only for subband switch by DSO non-APs and does not elicit any response. SIFS later, the AP sends a second control frame (which can be a regular MU-RTS/BSRP) that elicits a response in the new RU
  Option 2: The subband-switch initial control frame is used for subband switch by DSO non-APs and elicits a response in the new RU. This is especially possible if post-FCS MAC padding ([3]) is used
The subband-switch initial control frame may be in non-HT duplicate format, again depending on the negotiated capabilities.
Thereafter, the DSO TXOP can contain multiple SIFS-spaced DL/triggered UL exchanges with the DSO non-APs.
At the end of the TXOP (for example, detected through a gap of SIFS+delta time), the DSO non-AP switches back to operating on its operating bandwidth overlapping the primary 20MHz.

## Slide 7: Schematic diagram for Dynamic Subband Operation (Option 1)
AP
DSO STA
160S
160P
160S
160P
SIFS
SIFS
SIFS
non DSO STA
160S
160P
SIFS + delta
Rx second control frame (on 160S)
Rx second control frame (on 160P)
Rx subband switch control frame (on 160P)
Rx subband switch (on 160P)
Tx Response (on 160S)
Tx Response (on 160P)
320 MHz DL/UL OFDMA
Switch back to 160P
“Subband switch” control frame (with padding for DSO)
Second control frame

## Slide 8: Capability details (1)
Whether the non-AP/AP support DSO
Operating bandwidth of the non-AP/AP
  A non-AP bandwidth of 20MHz, 40MHz, 80MHz, 160MHz can be supported within any larger operating bandwidth of the AP. The scheme should allow smaller bandwidth non-APs to accommodate any low power non-AP implementations
DSO switching positions of the non-AP
  Theoretically, number of new switching positions is (AP_bandwidth/non-AP_bandwidth)-1
  However, in practice, the non-AP or even the AP may prefer a subset of such positions.
  The non-AP and AP can negotiate the subset of switching positions in the following manner
    The non-AP provides a bitmap of the candidate switching positions and the AP echos the same or a subset
    The non-AP provides the number of switching positions and the AP decides the exact candidate switching positions and indicates it to the non-AP in a bitmap

## Slide 9: Capability details (2)
Switching delay requirement
  This is indicated by the non-AP to the AP which provides for it through the MAC padding in the subband switch control frame
  The non-AP may have different switching delay requirements when DSO is used with EMLSR enabled vs. when DSO is used with EMLSR disabled and both values would need to be indicated in case EMLSR is supported
Option 1 or Option 2 requirement
  In order to provide a response in the new switched part of the bandwidth, whether the non-AP requires 2 initial control frames (Option 1) or just 1 initial control frame (Option 2)

## Slide 10: Other Aspects
MU-MIMO
  DSO is realized by making OFDMA allocations to clients of varying operating bandwidths smaller than or equal to the operating bandwidth of the AP
  It is very likely that certain bandwidth segments can be supported by both legacy and DSO-compliant devices. Hence, the optimal efficiency is attained if both MU-MIMO and DSO can be used together.
  For that, we need MU-MIMO + OFDMA support either in a general manner or conditional upon DSO usage.

## Slide 11: Straw Poll 1
Do you agree to define a mechanism where narrower bandwidth non-APs can dynamically, on a per-TXOP basis, be allocated resources outside of their current operating bandwidth within the larger bandwidth of an AP?
Y/N/A

## Slide 12: Reference
[1] IEEE P802.11be™/D5.0
[2] 11-22/2204r0 Dynamic Subband Operation
[3] 11-23/1873r0 Post-FCS MAC padding