## Slide 1: Improved UHR Seamless Roaming for Multi-link Device
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Jian Zhang | Ruijie Networks Co., Ltd. |  |  | zhangjian3@ruijie.com.cn
Danyang Hong | Ruijie Networks Co., Ltd. |  |  | hongdanyang@ruijie.com.cn
Jianxiang Chen | Ruijie Networks Co., Ltd. |  |  | chenjianxiang@ruijie.com.cn
Date: 2023-11-28
Authors:

## Slide 2: Abstract
Introduction
Roaming Model
Seamless Roaming procedure
Main Difference from the previous contribution

## Slide 3: Introduction
The 802.11be (EHT) standard has introduced multi-link operation (MLO) [1], and a non-AP STA multi-link device (MLD) can communicate with AP MLD over a plurality of links. We have discussed the seamless roaming scheme for UHR non-collocated AP MLD. This scheme fully utilizes the advantages of MLO to saving time and ensuring the continuity of data transmission.
In the previous scheme [2], non-AP STA selected the optimal link based on the link signal quality, but did not consider the link load. In fact, STA can make a better choice based on both, i.e., combination of the link prioritizes and the probe response signal quality of the link.

## Slide 4: Roaming Model
The UHR non-AP STA MLD associates with the collocated AP MLD with the wire or wireless backhaul. The UHR AP UMAC can use the backhaul links to manage LMAC and PHY of the collocated EHT AP MLD.
During the access process, PTK and GTK are generated using the UHR AP MLD UMAC address and EHT AP MLD LMAC Address, respectively. To achieve the seamless roaming, the PTK will be shared in non-collocated AP MLDs for the non-AP STA MLD, and the non-AP STA MLD stores the GTKs for all the AP MLDs.
Seamless roaming mechanism: the non-AP STA MLD selects one of the links (e.g. STA Link0) to disconnect from the original AP MLD(e.g. EHT AP MLD1 Link0) and then connects this link (STA Link0) to the new AP MLD (e.g. EHT AP MLD2 Link0). The other links of non-AP STA MLD remain connected to the original AP until the connection with the new AP MLD is finished.
Non-collocated AP MLD[2]
Non-AP STA MLD

## Slide 5: Seamless Roaming Procedure (I)
① Suppose the following associations during the access process : non-AP STA MLD Link0– AP MLD1 Link0, non-AP STA MLD Link1– AP MLD1 Link1;
② (1) AP MLD1 decides to have the non-AP STA MLD prepare roaming based on the quality of the uplink signal. The AP informs UHR AP MLD UMAC of this message through the backhaul link. (2)And then, UHR AP MLD UMAC provides target link set and prioritizes them according to the link load of the neighboring APs of AP MLD1. The UHR AP MLD UMAC informs AP MLD1 of the target link set and link priority through the backhaul link.
③ (1)AP MLD1 informs the non-AP STA MLD of the target link set and their priority through BSS transition management (BTM) Request frame. (2) This frame and downlink quality jointly trigger the roaming process of STA.
④ (1) The non-AP STA using its all links one bye one send the probe request to the adjacent AP MLDs (e.g. AP MLD2) which are connected to the same UHR AP MLD UMAC. The AP MLD2 replies the probe response from the non-AP STA MLD (probe response). (2)The non-AP STA evaluates the signal quality of the probe response for the link in the target link set. (3) The non-AP STA decides the roaming target link (e.g. AP MLD2 Link0) according to the combination of the link prioritizes and the probe response signal quality of the link. At this step, non-AP STA also determines the target link(e.g. non-AP STA MLD Link 0 – AP MLD2 Link0).

## Slide 6: Seamless Roaming Procedure (II)
⑤ The non-AP STA MLD sends the roaming request containing BTM roaming request frame to the original AP (e.g. AP MLD1). This frame uses the multi-link configure element to tell the original AP (e.g. MLD1) that the non-AP STA wants to switch from the original link (e.g. MLD1 Link0) to the target link (e.g.MLD2 Link0).
⑥ 1)The original AP (MLD1) sends BTM roaming reconfigure frame to non-AP STA MLD over the corresponding received link. 2)This frame triggers the link reconfiguration of the non-AP STA MLD (e.g. Link0), i.e. STA MLD Link0 – AP MLD2 Link0 STA MLD Link0 - AP MLD1 Link0. 3)The non-AP STA MLD uses the new link to send the BTM roaming confirm frame to AP MLD2, and confirms that this link of the non-AP STA MLD has been successfully reconfigured.
⑦The UHR AP MLD UMAC updates non-AP STA Link0 configuration. The link between the non-AP STA MLD Link0 and AP MLD2 Link0 has the highest priority for the new STA data transmission. Note: non-AP STA MLD Link1 maintains connection and communication with AP MLD1 Link1 at the step ⑥ and ⑦.
⑧ 1) The UHR AP MLD UMAC determines the switching of leftover links. Assuming link reconfiguration: the reconfiguration of non-AP STA Link1 is triggered by BTM roaming reconfigure frame through the existing connection links (e.g. AP MLD1 Link1 or MLD2 Link0 ). 2) The non-AP STA reconfigures the link, i.e. STA MLD Link1 – AP MLD2 Link1 STA MLD Link1 - AP MLD1 Link1. 3) After reconfiguration, non-AP STA sends the BTM roaming confirmation frame to AP MLD2 over the Link1 to confirm the successful reconfiguration.
Finally, all links of non-AP STA MLD complete roaming switching, and non-AP STA only connects and communicates with AP MLD2.

## Slide 7: Main Difference from the previous contribution [2]
The triggering methods for roaming are different
In the previous contribution, non-AP STA initiated roaming based on the quality of the down-link signal;
In this contribution, the AP initiates roaming based on the quality of the up-link signal.
The target link determination method is different:
Previous contribution: Firstly, STA determines the link priorities based on the link quality of the probe response signals from neighboring APs. Then, the STA determines the target link according to the link priorities and reports the target link to UHR AP MLD UMAC. Finally, the UHR AP MLD UMAC approves or rejects the roaming request based on the target link load.
This contribution: Firstly, UHR AP MLD UMAC provides target link set and prioritizes them according to the link load of the neighboring APs of the original AP MLD. Then, UHR AP MLD UMAC informs the non-AP STA of the target link set and link priority by the link between the original AP MLD and non-AP MLD. Finally, the non-AP STA determines the target link based on the combination of the link prioritizes and the probe response signal quality of the link.

## Slide 8: References
[1] Po-Kai Huang, et al. Multi-link Operation Framework, DCN 802.11-23/0231r0.
[2] Hui Che et al. UHR Seamless Roaming for Multi-link Device. DCN 802.11-23/1976r0.