## Slide 1: Low STA Cost UHR Seamless Roaming for Multi-link Device
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Jian Zhang | Ruijie Networks Co., Ltd. |  |  | zhangjian3@ruijie.com.cn
Danyang Hong | Ruijie Networks Co., Ltd. |  |  | hongdanyang@ruijie.com.cn
Jianxiang Chen | Ruijie Networks Co., Ltd. |  |  | chenjianxiang@ruijie.com.cn
Date: 2023-12-01
Authors:

## Slide 2: Abstract
Introduction
Roaming Model
Seamless Roaming procedure
Roaming Frame Format Extension
Conclusion

## Slide 3: Introduction
The 802.11be (EHT) standard has introduced multi-link operation (MLO) [1], and a non-AP STA multi-link device (MLD) can communicate with AP MLD over a plurality of links. We have discussed the seamless roaming scheme for UHR non-collocated AP MLD. This scheme fully utilizes the advantages of MLO to saving time and ensuring the continuity of data transmission.
In the previous scheme [2], the optimal link was selected by STA, which resulted in a heavy burden on non-AP STA.

## Slide 4: Roaming Model
The UHR non-AP STA MLD associates with the collocated AP MLD with the wire or wireless backhaul. The UHR AP UMAC can use the backhaul links to manage LMAC and PHY of the collocated EHT AP MLD.
During the access process, PTK and GTK are generated using the UHR AP MLD UMAC address and EHT AP MLD LMAC Address, respectively. To achieve the seamless roaming, the PTK will be shared in non-collocated AP MLDs for the non-AP STA MLD, and the non-AP STA MLD stores the GTKs for all the AP MLDs.
Seamless roaming mechanism: the non-AP STA MLD selects one of the links (e.g. STA Link0) to disconnect from the original AP MLD(e.g. EHT AP MLD1 Link0) and then connects this link (STA Link0) to the new AP MLD (e.g. EHT AP MLD2 Link0). The other links of non-AP STA MLD remain connected to the original AP until the connection with the new AP MLD is finished.
Non-collocated AP MLD[2]
Non-AP STA MLD

## Slide 5: Seamless Roaming Procedure (I)
① Suppose the following associations during the access process : non-AP STA MLD Link0– AP MLD1 Link0, non-AP STA MLD Link1– AP MLD1 Link1;
② (1) The original AP MLD (AP MLD1) decides to have the non-AP STA MLD prepare roaming based on the quality of the uplink signal. (2) Roaming preparation message: original AP MLD UHR AP MLD UMAC neighbor AP MLDs of the original AP MLD. After receiving this message, the neighbor AP MLDs of the original AP MLD reserve time to measure the probe request signal from the non-AP STA. (3) The original AP MLD informs the non-AP STA MLD of the roaming preparation message through BSS transition management (BTM) Request frame.
③ This request frame triggers the roaming process of non-AP STA. The non-AP STA using its all links one bye one send the probe request to the adjacent AP MLDs (e.g. AP MLD2, AP MLD3, ….) which are connected to the same UHR AP MLD UMAC.
④ (1)The neighbor AP MLDs of the original AP MLD evaluates the signal quality of the probe response for each link. (2)The neighbor AP MLDs reports the link signal quality and link load to the UHR AP MLD UMAC. (3) The UHR AP MLD UMAC decides the roaming target link according to the combination of the link load status and the probe response signal quality of the link. (4) The UHR AP MLD UMAC informs the original AP MLD (AP MLD1) of this roaming target link (e.g. non-AP STA MLD Link 0 – AP MLD2 Link0) .

## Slide 6: Seamless Roaming Procedure (II)
⑤ (1)The original AP (MLD1) sends the roaming target link (in BTM roaming reconfigure frame) to non-AP STA MLD over the corresponding received link. (2)This message triggers the link reconfiguration of the non-AP STA MLD (e.g. Link0), i.e. STA MLD Link0 – AP MLD2 Link0 STA MLD Link0 - AP MLD1 Link0.
⑥ The non-AP STA MLD uses the new link (target link) to send the BTM roaming confirm frame to AP MLD2, and confirms that this link of the non-AP STA MLD has been successfully reconfigured.
⑦The AP MLD2 notifies UHR AP MLD UMAC to updates Link0 configuration. The link between the non-AP STA MLD Link0 and AP MLD2 Link0 has the highest priority for the new STA data transmission. Note: non-AP STA MLD Link1 maintains connection and communication with AP MLD1 Link1 at the step ⑥ and ⑦.
⑧ (1) The UHR AP MLD UMAC determines the switching of leftover links. Assuming link reconfiguration: the reconfiguration of non-AP STA Link1 is triggered by BTM roaming reconfigure frame through the existing connection links (e.g. AP MLD1 Link1 or MLD2 Link0 ). 2) The non-AP STA reconfigures the link, i.e. STA MLD Link1 – AP MLD2 Link1 STA MLD Link1 - AP MLD1 Link1. 3) After reconfiguration, non-AP STA sends the BTM roaming confirmation frame to AP MLD2 over the Link1 to confirm the successful reconfiguration.
Finally, all links of non-AP STA MLD complete roaming transition, and non-AP STA only connects and communicates with AP MLD2.

## Slide 7: Roaming Frame Format Extension (I)
UHR Mobility domain element: declaring the seamless transition capability
The UHR mobility domain element is added to the beacon, probe response, association request, association response, and authentication frames to declare the seamless transition capability of the UHR MLD.
Element ID | Length | MDID | ST Capability
1 | 1 | 2 | 1
Octet
The Element ID and Length fields are defined in 9.4.2.1 [3].
The MDID (mobility domain ID) field is an identifier that names a UHR Roaming mobility domain.
The ST Capability field declares the capability of the seamless BSS transitions. The ST Capability field is defined as following,
Seamless BSS Transition Mode | Reserved
2 | 6
Bits
Seamless BSS Transition Mode | Meaning
0 | MLD does not have the capability of seamless roaming.
1 | The seamless roaming is initiated by non-AP STA MLD.
2 | The seamless roaming is initiated by AP MLD and the roaming-target-link is determined by non-AP STA MLD.
3 | The seamless roaming is initiated by AP MLD and the roaming-target-link is determined by UHR AP MLD UMAC.

## Slide 8: Main Difference from the previous proposal
The triggering methods for roaming are different
In the previous proposal, non-AP STA initiated roaming based on the quality of the down-link signal;
In this proposal, the AP initiates roaming based on the quality of the up-link signal.
The target link determination method is different:
Previous proposal [2]: Firstly, STA determines the link priorities based on the link quality of the probe response (downlink) signals from neighboring APs. Then, the STA determines the target link according to the link priorities and reports the target link to UHR AP MLD UMAC. Finally, the UHR AP MLD UMAC approves or rejects the roaming request based on the target link load.
This proposal: Firstly, the neighbor AP MLD evaluate the signal quality of the probe request (uplink), and then reports the uplink signal quality and link load to the UHR AP MLD UMAC. Finally, the UHR AP MLD UMAC determines the target link based on the set of the link load status and the uplink signal quality.

## Slide 9: Conclusion
Low Cost Seamless roaming mechanism:
On the one hand, the cost of non-AP STA MLD is low. The detection signal quality is evaluated by AP MLD instead of non-AP STA MLD. The optimal link is determined by UHR AP MLD UMAC rather than non-AP STA.
On the other hand, there are fewer interactions between non-AP STA MLD and AP MLD. (1) Compared to [3], this scheme does not require non-AP STA MLD to inform the original AP MLD of the optimal link. Compared to [2][3], this scheme does not require the AP MLD to send a probe response to the AP MLD.
For compatibility, the sub-field Seamless BSS Transition Mode has been added to represent different roaming modes.

## Slide 10: References
[1] Po-Kai Huang, et al. Multi-link Operation Framework, DCN 802.11-23/0231r0.
[2] Hui Che et al. UHR Seamless Roaming for Multi-link Device. DCN 802.11-23/1976r0.
[3] Hui Che et al. Improved UHR Seamless Roaming for Multi-link Device. DCN 802.11-23/2147r0.