## Slide 1: Seamless Roaming within a Mobility Domain
Date: 2023-11-27
Authors:

## Slide 2: Introduction
UHR PAR requires improved support for roaming. More reliable roaming mechanisms have been discussed in UHR to achieve seamless roaming [3][4].
Multiple architecture options for seamless roaming data path handling were presented in [1].
In this presentation, we expand on [1] and propose further details on roaming architecture, signaling and data path operation for seamless roaming.

## Slide 3: Recap (1)
In [1] four architecture options were captured for seamless roaming:
Option A - Mandatory 11k/v/r:
  Mandate support for existing 11k/v/r features. This can achieve best case roaming time of 5-10 msec, but most clients don't achieve that, and there can be brief data loss. Goal is to achieve better roaming performance in 11bn.
Option B - Elongated Client Connectivity:
  AP MLD1 (source) and AP MLD2 (target) minimize the transferred context. Only control plane context is transferred without any data transfer. Client drains DL buffered data from the old AP MLD before it completely switches to the target AP MLD. The knife-switch is at the client.
Option C - Hot Standby:
  AP MLD1 (source) and AP MLD2 (target) exchange all context one time including both control plane context and data (one or more of MSDUs/A-MSDUs/MPDUs). Infrastructure switches the DS data path to target AP MLD after context transfer. The knife-switch is within the infrastructure.
Option D: Distributed MLO:
  UMAC MLO operation is distributed across lower UMACs on AP MLD1 (source) and AP MLD2 (target) and an Upper UMAC which provides single data path interface to DS across AP MLDs. The Upper UMAC provides Roaming MLD functionalities [4] [5] and could reside on one of the AP MLDs or on another network node (e.g. controller). Separate roaming of Upper UMAC would need to be supported as client roams, to minimize delays.

## Slide 4: Recap (2)
Summary of options:
 | Option A | Option B | Option C | Option D
Name | Mandatory 11k/v/r | Elongated client connectivity | Hot standby | Distributed MLO
Knife-switch | Within infrastructure | At client | Within infrastructure | None
Frame loss upon roaming | Typical but brief losses | Rare DL & infrequent UL losses | Rare losses | No losses
Infrastructure upper layer complexity | N/A | N/A | N/A | High
AP complexity | Very low | Low | Moderate | High
Client complexity | Very low | Low-Moderate | Low | Moderate
Association / Security | Client associates to the “Mobility Domain” (e.g. an ESS), with a single unicast key |  |  | 

## Slide 5: Challenges with Roaming MLD Architecture (1)
Distributed MLO architecture (Option D in [1]) using a Roaming MLD for seamless roaming is ill advised because it leads to additional delays and high complexity for infrastructure and chipset [2].
Splitting data path functionality across Upper UMAC and Lower UMAC residing on different nodes adds significant complexity for coordination across these nodes and adds delays.
Advertising Roaming MLD with many non-collocated affiliated APs would lead to beacon bloating
If Roaming MLD with Upper UMAC is hosted on one of the AP MLDs
  Leads to additional delays from Roaming MLD to non-collocated AP MLDs
  Requires a mechanism to roam the Roaming MLD itself closer to client’s location for scalability and to minimize delays. This adds further complexity.

## Slide 6: Challenges with Roaming MLD Architecture (2)
If Roaming MLD with Upper UMAC is hosted at a centralized node (e.g. controller)
  Leads to additional buffering of frames and adds delays from Roaming MLD to non-collocated AP MLDs.
  Typically, controller and AP MLDs sit far apart. Requires fast networking path between controller and all AP MLDs. Continuous data path coordination across controller and AP MLDs is challenging.
  Avoiding DL wireless duplication requires coordination between AP MLDs, adding additional delays.
  Implementing reorder buffers is challenging in terms of scalability. Requires massive throughput at controller with high client scale.
Due to these challenges, we strongly discourage adopting a Roaming MLD architecture for seamless roaming in 11bn

## Slide 7: Roaming within a Seamless Mobility Domain
Instead, we propose to adopt a roaming architecture which enables seamless roaming within a Seamless Mobility Domain (SMD) using Option B, Option C or hybrid of the two [1]
  Achieve seamless roaming without complexity of Roaming MLD
An SMD consists of multiple AP MLDs across which seamless roaming is supported. One SMD could cover all AP MLDs of an ESS or an ESS can have multiple SMDs.
Each AP MLD maintains its own data path to DS and complete UMAC functionality resides on the AP MLD as in 11be.
  UMAC is not split into Upper & Lower UMAC on different entities
Each SMD is uniquely identified in the network using a virtual MAC address (SMD MAC Address).
An AP MLD is configured with the SMD that it belongs to. Affiliated APs advertise SMD info in beacons & probe responses.
  For seamless roaming, a client associates with the SMD through an AP MLD and establishes setup links. Client then adds/deletes links with AP MLDs as it roams within that SMD.

## Slide 8: Association to a Seamless Mobility Domain
Association procedure is enhanced to indicate association to an SMD by including an SMD IE.
A single PTK is generated for association to an SMD. The SMD MAC Address is used in PTK generation to tie it to the SMD.
After client’s initial association with the SMD through an AP MLD, infrastructure facilitates PTK distribution on all AP MLDs of the SMD.
  PTK can be distributed right after association or fetched from a key storage by AP MLDs when roaming preparation is triggered.
  GTK for added links during roaming is provided to the STA as part of add link operation.
  AID space is per AP MLD. Target AP MLD assigns a new AID to the non-AP MLD during Add Link operation.

## Slide 9: Considerations for Seamless Roaming (1)
Support only MLD level roaming: Client roams all links to a neighbouring AP MLD
  In a non-roaming state, a non-AP MLD only has links setup with a single AP MLD and does not have links split across multiple AP MLDs, to avoid infra. complexity of multiple data paths to DS.
  Only during roaming transition, a non-AP MLD has link connectivity through multiple AP MLDs to achieve make-before-break roaming.
    Non-AP MLD has DL wireless connectivity through both source and target AP MLDs.
    Non-AP MLD always has UL wireless connectivity through a single AP MLD – first with source and then with target.

## Slide 10: Considerations for Seamless Roaming (2)
Roaming context transfer: context transfer can be done in two phases to achieve faster roaming time.
  Roaming preparation phase:
    Triggers the start of roaming procedure.
    Prepares one or more neighboring APs for roaming by transferring near static contexts (e.g. STA capabilities, BA agreements, SCS + QoS Char., TWT, negotiated TTLM).
    No resources are reserved on neighboring APs in this phase.
    If near static contexts change during this phase, then Source AP transfers updated contexts to neighboring APs.
    Context may timeout on neighboring APs after certain ‘roaming preparation period’ indicated to the client. AP keeps the context until the timeout and ages it out after.
    Roaming preparation can be initiated by the STA or the AP – e.g. AP may want to do load balancing based on BSS Load of neighboring APs.

## Slide 11: Considerations for Seamless Roaming (3)
Roaming execution phase:
  Started within the ‘roaming preparation period’ if specified by source AP in the preparation phase.
  Client indicates the target AP MLD (should consider any AP recommendation if received) using Add Link from the candidate target AP MLDs list.
  Source AP attempts to reserve resources on the target AP MLD (client includes RSSI for target APs in Add Link).
    Client may indicate roaming is acceptable even if some or all resources can’t be reserved
  Source AP transfers dynamic context (e.g. SN, PN) to target AP MLD and sends Add Link Response (with group keys and AID).
  Link with source AP is deleted after draining buffered DL data.
  Roaming execution can also be initiated by the AP by sending an Add Link Notification that recommends a target AP MLD.
ML Reconfiguration framework can be used/extended to define signalling for roaming phases.

## Slide 12: Considerations for Seamless Roaming (4)
Data path switching:
  DS data path is switched from source to target AP MLD right after the dynamic context (e.g. SN, PN) is transferred to the target AP MLD and Add Link response is sent to the client.
  After Add Link response - client can exchange UL & DL data with the target AP MLD and UL switches to the target AP MLD.
  To avoid data loss, source AP MLD continues to try to drain DL buffered data (Option B in [1]) and client can remain connected to source AP MLD even after add link response. There are two DL wireless data path to the client from source and target AP MLDs during roaming transiiton.
Data forwarding:
  Option C in [1] described support for data forwarding to target AP during roaming. However, transferring all buffered data (e.g. MSDUs/A-MSDUs/MDPUs) may be complex to implement - it is harder to take out and transfer MPDUs buffered deep in the hardware than transfer buffered MSDUs/A-MSDUs.
  AP may support the option of selected data forwarding (e.g. MSDUs/A-MSDUs/MPDUs for high-QoS TIDs) for fast roaming and to minimize data losses
  Data forwarding done during roaming (e.g. MSDUs/A-MSDUs/MPDUs for specific TIDs/ACs or SCS streams) can be negotiated between source AP MLD and the non-AP MLD.
  Source AP MLD tries to drain rest of the DL buffered data to the non-AP MLD (hybrid of Option B & C)

## Slide 13: Roaming across SMDs of an ESS
SMD based roaming is the main mechanism to provide seamless roaming in 11bn
For deployments with non-contiguous Wi-Fi coverage for an ESS (e.g. two campus buildings), different SMDs can be defined for each contiguous coverage
FT (Fast BSS Transition) can be used for roaming across two non-contiguous SMDs of an ESS
We propose to mandate support for 11r/FT for UHR client STAs to achieve fast reassociation across non-contiguous coverage for an ESS.

## Slide 14: Summary (1)
There are several challenges with Roaming MLD architecture
  Additional buffering, data path coordination issues across non-collocated Roaming MLD and AP MLDs, roaming of Roaming MLD itself, scalability concern  additional delays, high infra and chipset complexity.
We propose to support association to an SMD and adopt seamless roaming within a Seamless Mobility Domain (SMD)
  An SMD consists of multiple AP MLDs across which seamless roaming is supported
  A single SMD can be configured to cover all AP MLDs of an ESS or an ESS can have multiple SMDs configured
  Each AP MLD maintains its own connectivity to DS and includes complete UMAC functionality
  A single PTK is generated for association to an SMD and used across all AP MLDs of that SMD

## Slide 15: Summary (2)
We propose following considerations for seamless roaming:
  Support only MLD level roaming, no link level roaming support
  Roaming context transfer can be done in two phases to achieve faster roaming
    Roaming preparation phase: Prepares one or more neighboring APs in advance for roaming by transferring near static contexts (e.g. STA capabilities, BA agreements, SCS + QoS Char., TWT, negotiated TTLM etc.).
    Roaming execution phase: Reserves resources and transfers dynamic context (e.g. SN,PN) to target AP MLD and deletes link to the source AP MLD to complete roaming.
    ML Reconfiguration framework can be used/extended to define signalling for roaming phases.
  Roaming operation can be initiated by the non-AP MLD or by the source AP MLD
  Support delivery of DL buffered data from source AP MLD even after the DS data path has been switched to a target AP MLD to avoid data loss
  Support the option of selected data forwarding to target AP MLD (e.g. for high QoS traffic) per negotiation between the client and source AP MLD
We propose to mandate support for 11r/FT for UHR client STAs to achieve fast roaming across non-contiguous SMDs of an ESS

## Slide 16: SP1
Do you agree to define a mechanism in 11bn that enables UHR non-AP MLDs to roam across non-collocated AP MLDs without requiring reassociation and renegotiation of unicast encryption keys?
  Each AP MLD maintains its own MAC-SAP connectivity to the DS
  Each AP MLD supports complete UMAC functionality. UMAC is not split into Upper UMAC and Lower UMAC residing on different entities.

## Slide 17: SP2
Do you agree to define a mechanism in 11bn that enables a UHR non-AP MLD to associate with a Seamless Mobility Domain (SMD) at initial association and support roaming across AP MLDs belonging to an SMD without requiring reassociation and renegotiation of unicast encryption keys?
  An SMD consists of one or more AP MLDs across which seamless roaming is supported. A single SMD can be configured to cover all AP MLDs of an ESS or multiple SMDs can be configured for an ESS.
  An AP MLD advertises information for configured SMD in Beacon and Probe responses of its affiliated APs
  Association procedure is enhanced to support association to an SMD
  A single PTK is generated for association to an SMD and used across all AP MLDs of that SMD

## Slide 18: SP3
Do you agree to define a roaming mechanism in 11bn that requires a UHR non-AP MLD to roam all links to a neighbouring target AP MLD.
  In a non-roaming state, a non-AP MLD only maintains links with a single AP MLD and does not have links split across multiple AP MLDs.
  Only during roaming transition, a non-AP MLD can have DL wireless connectivity through both the source AP MLD and a target AP MLD. The non-AP MLD always has UL wireless connectivity through a single AP MLD.

## Slide 19: SP4
Do you agree to define a roaming mechanism in 11bn that supports context transfer during roaming operation in two phases as defined below.
  Roaming preparation phase: Prepare one or more candidate AP MLDs for roaming in advance by transferring near static contexts to those AP MLDs. Details of near static context is TBD. For example, near static context could include STA capabilities, BA agreements, SCS with QoS Characteristics agreements, TWT agreements and/or negotiated TTLM.
  Roaming execution phase: Reserve resources on a single target AP MLD, transfer dynamic context to that target AP MLD and delete link with the source AP MLD to complete roaming. Details of dynamic context is TBD. For example, dynamic context could include SN and PN.

## Slide 20: SP5
Do you agree to define a roaming mechanism in 11bn that enables a non-AP MLD or its serving AP MLD to initiate the roaming operation?

## Slide 21: SP6
Do you agree to reuse/extend the 11be ML Reconfiguration framework to define signalling for seamless roaming in 11bn?

## Slide 22: SP7
Do you agree to define a roaming mechanism in 11bn that enables a non-AP MLD to continue to receive DL buffered MPDUs from the source AP MLD even after the DS data path has been switched to the target AP MLD?

## Slide 23: SP8
Do you agree to define a roaming mechanism in 11bn that supports the option of selected data forwarding from the source AP MLD to target AP MLD?
  Details of data forwarding that can be done during roaming are TBD. For example, MSDUs/A-MSDUs/MPDUs can be forwarded for specific TIDs/ACs (e.g. high-QoS TIDs).
  Details of data forwarding is negotiated between the non-AP MLD and source AP MLD.

## Slide 24: SP9
Do you agree to mandate support for 11r/FT (Fast BSS Transition) for UHR client STAs?

## Slide 25: References
[1] 11-23/0324 "Roaming Requirement”
[2] 11-22/1580 “A perspective on proposed Ultra-High Reliability (UHR) features for enterprise use cases”
[3] 11-22/1910 “Seamless Roaming for UHR”
[4] 11-23/0170 “Smooth Roaming”
[5] 11-23/1131 “Thoughts on seamless roaming”

## Slide 26: Backup

## Slide 27: Relationship across entities
Scenario 2 – No FT Mobility Domain is configured:
SSID/ESS is configured to consist of one or more SMDs. No FT Mobility Domain is configured.
Seamless roaming within SMD. No FT across SMDs.
Scenario 1 – FT Mobility Domain is configured:
SSID/ESS is configured to consist of one or more FT Mobility Domain (FT MDID). Each FT MD is configured to consist of one or more SMDs.
FT happens across SMDs of a given FT MD.
Notes: 2