## Slide 1: Seamless Roaming within a Mobility Domain
Date: 2023-11-27
Authors:

## Slide 2: Introduction
UHR PAR requires improved support for roaming. More reliable roaming mechanisms have been discussed in UHR to achieve seamless roaming [3][4].
Multiple architecture options for seamless roaming data path handling were presented in [1].
In this presentation, we expand on [1] and propose further details on roaming architecture, signaling and data path operation for seamless roaming.

## Slide 3: Recap (1)
In [1] four architecture options were captured for seamless roaming:
Option A - Mandatory 11k/v/r:
  Mandate support for existing 11k/v/r features. This can achieve best case roaming time of 5-10 msec, but most clients don't achieve that, and there can be brief data loss. Goal is to achieve better roaming performance in 11bn.
Option B - Elongated Client Connectivity (Control context transfer):
  AP MLD1 (source) and AP MLD2 (target) minimize the transferred context. Only control plane context is transferred without any data transfer. Client drains DL buffered data from the old AP MLD before it completely switches to the target AP MLD.
Option C - Hot Standby (Control context + Data transfer):
  AP MLD1 (source) and AP MLD2 (target) exchange all context one time including both control plane context and data (one or more of MSDUs/A-MSDUs/MPDUs). Infrastructure switches the DS data path to target AP MLD after context transfer.
Option D: Distributed MLO (Roaming MLD):
  UMAC MLO operation is distributed across lower UMACs on AP MLD1 (source) and AP MLD2 (target) and an Upper UMAC which provides single data path interface to DS across AP MLDs. The Upper UMAC provides Roaming MLD functionalities [4] [5] and could reside on one of the AP MLDs or on another network node (e.g. controller). Separate roaming of Upper UMAC would need to be supported as client roams, to minimize delays.

## Slide 4: Recap (2)
Summary of options:
 | Option A | Option B | Option C | Option D
Name | Mandatory 11k/v/r | Elongated client connectivity (Control context transfer) | Hot standby (Control context + data transfer) | Distributed MLO (Roaming MLD)
Frame loss upon roaming | Typical but brief losses | Rare DL & infrequent UL losses | Rare losses | No losses
Infrastructure upper layer complexity | N/A | N/A | N/A | High
AP complexity | Very low | Low | Moderate | High
Client complexity | Very low | Low-Moderate | Low | Moderate
Association / Security | Client associates to the “Mobility Domain” (e.g. an ESS), with a single unicast key |  |  | 

## Slide 5: Challenges with Distributed MLO Architecture (1)
Distributed MLO architecture (Option D) using a Roaming MLD for seamless roaming is ill advised because it leads to additional delays and high complexity for infrastructure and chipset [2].
Main concern - splitting data path functionality across Upper UMAC and Lower UMAC residing on different nodes/entities adds significant complexity and delays for continuous data path coordination across these nodes. These extra delays can lead to worse performance.
Case 1: If Roaming MLD with Upper UMAC is hosted on one of the AP MLDs
  Leads to additional delays from Roaming MLD to the non-collocated AP MLD
  Requires a mechanism to roam the Roaming MLD itself closer to client’s location for scalability and to minimize delays, which adds further complexity.

## Slide 6: Challenges with Distributed MLO Architecture (2)
Case 2: If Roaming MLD with Upper UMAC is hosted at a centralized node (e.g. controller)
  Leads to additional buffering of frames and adds delays from Roaming MLD to non-collocated AP MLDs.
  Typically, controller and AP MLDs sit far apart. Requires fast networking path between controller and all AP MLDs. Continuous data path coordination across controller and AP MLDs is challenging.
  Avoiding DL wireless duplication requires coordination between AP MLDs, adding additional delays.
  Scalability issues with Implementing reorder buffers. Requires massive throughput at controller with high client scale.
Due to these challenges, we strongly discourage adopting a Roaming MLD (Option D) architecture for seamless roaming in 11bn

## Slide 7: Roaming within a Seamless Mobility Domain (1)
Instead, we propose to adopt a roaming architecture based on Option B, Option C or hybrid of the two [1], which enables seamless roaming within a Seamless Mobility Domain (SMD)
An SMD is a logical control plane entity that covers multiple AP MLDs across which seamless roaming is supported. One SMD could cover all AP MLDs of an ESS or an ESS can have multiple SMDs configured.
Each SMD is uniquely identified in the network using a virtual SMD MAC Address.
An AP MLD is configured with the SMD that it belongs to. Affiliated APs of the AP MLD advertise SMD info in beacons & probe responses.

## Slide 8: Roaming within a Seamless Mobility Domain (2)
Each AP MLD maintains its own MAC SAP to DS and complete UMAC functionality resides on the AP MLD as in 11be.
  UMAC is not split into Upper & Lower UMAC on different entities
For seamless roaming:
  A client performs auth and associates with an SMD through an AP MLD and establishes setup links. SMD maintains control plane context for the client (association, security context, capabilities etc).
  SMD MAC Address is used in PTK generation to tie PTK to the SMD.
  Client then adds/deletes links with AP MLDs as it roams within that SMD.
  GTK for added links during roaming is provided to the STA as part of add link operation.
  AID space is per AP MLD. A new AID assigned to the non-AP MLD as part of Add Link operation.

## Slide 9: Roaming within a Seamless Mobility Domain (3)
Client roams all links to a neighbouring AP MLD
In a non-roaming state, a non-AP MLD has links setup with only a single AP MLD.
Only during roaming transition, a non-AP MLD can have link connectivity through multiple AP MLDs to achieve make-before-break roaming.
  Non-AP MLD has DL wireless connectivity through both source and target AP MLDs to drain DL buffered data from the source.
  Non-AP MLD always has UL wireless connectivity through a single AP MLD – first with source and then with target.

## Slide 10: Considerations for Seamless Roaming (1)
Roaming context transfer: context transfer can be done in two phases to achieve faster roaming time. Context transfer can be done over-the-DS.
  Roaming preparation phase:
    Prepares one or more neighboring APs for roaming by transferring near static contexts (e.g. STA capabilities, BA agreements, SCS + QoS Char., TWT, negotiated TTLM).
    No resources are reserved on neighboring APs.
    If near static contexts change during this phase, then Source AP transfers updated contexts to neighboring APs.
    Context may timeout on neighboring APs after certain ‘roaming preparation period’ indicated to the client.
    Roaming preparation can be initiated by the STA or the AP – e.g. AP may want to do load balancing based on BSS Load of neighboring APs.

## Slide 11: Considerations for Seamless Roaming (2)
Roaming execution phase:
  Started within the ‘roaming preparation period’ if specified.
  Client indicates the target AP MLD (should consider any AP recommendation if received) from the candidate target AP MLDs list using Add Link.
  Source AP attempts to reserve resources on the target AP MLD (client includes RSSI for target APs in Add Link).
    Client may indicate roaming is acceptable even if some or all resources can’t be reserved
  Source AP transfers dynamic context (e.g. SN, PN) to target AP MLD and sends Add Link Response (with group keys and AID).
  Link with source AP is deleted after draining of buffered DL data.
  Roaming execution can also be initiated by the AP by sending an Add Link Notification that recommends a target AP MLD.
ML Reconfiguration framework can be used/extended to define signalling for roaming phases.

## Slide 12: Considerations for Seamless Roaming (3)
Data path switching:
  DS data path is switched from source to target AP MLD right after the dynamic context (e.g. SN, PN) transfer to the target AP MLD and Add Link response is sent to the client.
  After Add Link response - client can exchange UL & DL data with the target AP MLD and UL switches to the target AP MLD.
  To avoid data loss, source AP MLD continues to try to drain buffered DL data (Option B in [1]) to client even after add link response. There are two DL wireless data path to the client from source and target AP MLDs during roaming transition.
Data forwarding:
  Option C in [1] described support for data forwarding to target AP during roaming. However, transferring all buffered data may be complex to implement - it is harder to take out and transfer MPDUs buffered deep in the hardware than transfer buffered MSDUs/A-MSDUs.
  AP may support the option of selected data forwarding (e.g. MSDUs/A-MSDUs for high-QoS TIDs) for fast roaming and to minimize data losses.
  Data forwarding done during roaming (e.g. MSDUs/A-MSDUs for specific TIDs/ACs or SCS streams) can be negotiated between source AP MLD and the non-AP MLD.
  Source AP MLD tries to drain rest of the DL buffered data to the non-AP MLD (hybrid of Option B & C)

## Slide 13: Roaming across SMDs of an ESS
SMD based roaming is the main mechanism to provide seamless roaming in 11bn
For deployments with non-contiguous Wi-Fi coverage for an ESS (e.g. two campus buildings), different SMDs can be defined for each contiguous coverage
FT (Fast BSS Transition) can be used for roaming across two non-contiguous SMDs of an ESS
We propose to mandate support for 11r/FT for UHR clients and APs to achieve fast reassociation across non-contiguous coverage for an ESS
  This also enables UHR clients to use 11r/FT with pre-UHR APs, providing better roaming performance

## Slide 14: Summary (1)
There are several challenges with Distributed MLO/Roaming MLD architecture.
  Additional buffering, data path coordination issues across Roaming MLD and AP MLDs, roaming of Roaming MLD itself, scalability concern  additional delays, high infra and chipset complexity.
We propose to adopt a roaming architecture which enables seamless roaming within a Seamless Mobility Domain (SMD) by association to the SMD and context transfer
  SMD is a logical control plane entity covering multiple AP MLDs across which seamless roaming is supported.
  Each AP MLD of an SMD has its own MAC SAP to DS and includes complete UMAC functionality
  A client performs initial auth and associates with an SMD through an AP MLD, and then adds links with target AP MLD when roaming.
In a non-roaming state, a non-AP MLD has links setup with only a single AP MLD.

## Slide 15: Summary (2)
We propose following considerations for seamless roaming:
  Roaming context transfer can be done in two phases to achieve faster roaming
  ML Reconfiguration framework can be used/extended to define signalling for roaming
  Roaming operation can be initiated by the non-AP MLD or by the source AP MLD
  To avoid data loss, support delivery of DL buffered data from source AP MLD even after the DS data path has been switched to the target AP MLD
  Support the option of selected data forwarding to target AP MLD (e.g. MSDUs/A-MSDUs for high QoS traffic) per negotiation between the client and source AP MLD
We propose to mandate 11r/FT for UHR clients and APs to achieve fast roaming across non-contiguous SMDs of an ESS, and improved roaming with pre-UHR APs

## Slide 16: SP1
Do you agree to define a mechanism in 11bn that enables a UHR non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) during and after the roaming operation?

## Slide 17: SP2
Do you agree to define a mechanism in 11bn that enables a UHR non-AP MLD to associate with a control plane entity (called Seamless Mobility Domain (SMD) here) covering multiple AP MLDs and the non-AP MLD remains associated with the SMD when it roams across AP MLDs of that SMD?
  The exact name of the control plan entity is TBD.

## Slide 18: SP3
Do you agree that in 11bn a non-AP MLD which is not in the process of roaming has setup links with only a single AP MLD?
  Each AP MLD maintains its own MAC-SAP connectivity to the DS and supports complete UMAC functionality as in 11be.

## Slide 19: SP4
Do you agree to define a roaming mechanism in 11bn that supports context transfer from source to target AP MLD during roaming operation in two phases as below?
  Roaming preparation phase: Transfer near static contexts to one or more candidate AP MLDs to prepare those AP MLDs in advance for roaming. Details of near static context is TBD.
  Roaming execution phase: Transfer dynamic context to a single target AP MLD such that the data exchange related context is preserved. Details of dynamic context is TBD.

## Slide 20: SP5
Do you agree to define a roaming mechanism in 11bn that enables a non-AP MLD or its serving AP MLD to initiate the roaming operation?

## Slide 21: SP6
Do you agree to define a roaming mechanism in 11bn that enables a non-AP MLD to continue to receive DL buffered MPDUs from the source AP MLD even after the DS data path has been switched to the target AP MLD?

## Slide 22: SP7
Do you agree to define a roaming mechanism in 11bn that supports the option of selected data forwarding from the source AP MLD to target AP MLD during the roaming procedure?
  Details of data forwarding that can be done during roaming are TBD. For example, MSDUs/A-MSDUs can be forwarded for high-QoS TIDs.
  Details of data forwarding is negotiated between the non-AP MLD and source AP MLD.

## Slide 23: SP8
Do you agree to mandate support for 11r/FT (Fast BSS Transition) for UHR clients and APs?

## Slide 24: References
[1] 11-23/0324 "Roaming Requirement”
[2] 11-22/1580 “A perspective on proposed Ultra-High Reliability (UHR) features for enterprise use cases”
[3] 11-22/1910 “Seamless Roaming for UHR”
[4] 11-23/0170 “Smooth Roaming”
[5] 11-23/1131 “Thoughts on seamless roaming”

## Slide 25: Backup

## Slide 26: Relationship across FT MD and SMD
Scenario:
SSID/ESS is configured to consist of one or more FT Mobility Domain (FT MD) identified by FT MD ID.
Each FT MD is configured to consist of one or more SMDs.
FT happens across SMDs of a given FT MD.
Seamless mobility happens across AP MLDs of a given SMD.