## Slide 1: MAP coordination for DFS operating channel

## Slide 2: Background
UHR PAR illustration
  improve the reliability and performance in the scenarios of overlapping BSSs
5GHz band operating rule(FCC,ETSI,CA,etc.)
  5GHz band divides into DFS(owner’s operating) channel and non-DFS channel.
  AP and STA can operate on the non-DFS channel immediately.
  AP shall perform Channel Availability Check(CAC) before operating on the target DFS channel, during which 5GHz signal is unavailable for connection.
  The Channel Availability Check process would take 1-10 minutes depending on the country.
  During CAC mode, only 2.4GHz AP is available for the Wi-Fi connection in 6GHz band unavailable country
Conclusion
  CAC mode on 5GHz bands cause a seriously performance issue.

## Slide 3: Popular solution on the high-end AP/STA products
The popular solution on the high-end AP products
  Integrate a dedicated Radio+RF chain for radar signal detection.
  Having 4*4 RF chains on 5GHz band,operates on 4*4 mode in normal mode, switches to 3+1 mode in CAC mode.
    Note: [3+1] mode: 3 RF chains operates on the original channel, while 1 RF chain swithes to the target DFS channel and stays in CAC mode.
Some high-end client or mobile AP/AP MLD may also integrate a scan radio
  The function is similar to the dedicated radio on some high-end APs.

## Slide 4: The problem on cost-down AP products
The status on cost-sensitive market
  2*2 two-link AP products still dominate the residential market
  To reduce the cost,no scan radio integrated.
  Stop providing Wi-Fi service on 5GHz bands for 1 mins or 10 mins when the AP switches to a DFS channel or enlarge the operating Bandwidth across the DFS channel

## Slide 5: Motivation
Ideas: may I “borrow” your scan radio for Channel Available Check?
  Leverage 11bn MAP scheme, allow low-cost AP(AP1) to trigger high-end AP(AP2) to scan the expected DFS channel via AP2’s scan radio
  Allow AP1 to trigger an associated high-end STA to detect radar signal on DFS channel via the scan radio
  Benifit: avoid the Wi-Fi service interruption issue on AP1 in CAC mode without increasing the cost.
  Consideration: a uniformed radio measurement signaling should be defined to cover by infrastructure network and MAP coordination network.

## Slide 6: The proposed procedure
AP1
AP2/STA
1. DFS channel scan request
2. use the scan radio to detect radar signal on the requested DFS channel for 1 or 10 mins
3. DFS channel scan report
4. switch to DFS channel immediately if no radar signal detected
The proposed procedure is similar to Beacon request/report as bellow:
0.Scan radio information exchanged

## Slide 7: Summary
Analyze the regulation rule of non-DFS and DFS channel on 5GHz band
Analyze the main solution on high-end AP/STA to avoid performance issue during CAC mode
Propose a “ scan radio sharing” solution to address the performance issue during CAC procedure on low-cost AP product

## Slide 8
THANK YOU 

## Slide 9: Reference
[1]802.11bn PAR
[2] ETSI EN 301 893 V2.1.1
[3] Revision of Part 15 of the Commission’s Rules to Permit Unlicensed National Information Infrastructure (U-NII) Devices in the 5 GHz Band