## Slide 1: The need for 802.11be non-AP MLD identification

## Slide 2: Introduction
The major features of IEEE P802.11bh (Randomized and Changing MAC addresses) is included in latest revision D2.0, with per-11be STAs as the baseline entities.
802.11be has defined a new entity, MLD, in which there’s one MLD MAC address and several link MAC addresses.
This submission briefly discusses:
  The supporting RCM and the identification issues on MLD
  Some recent additional market context for RCM
  A recommended standardization path for extending Randomized and Changing MAC addresses to support MLD
  The proposed timeline

## Slide 3: The statement of RCM on MLD
Both MLD MAC and Link MAC addresses can be randomized changed according to 11be latest draft.
One link MAC address may be the same as the MLD MAC address of an MLD.

## Slide 4: The identification issue and potential solution on MLD
Device ID and IRM schemes proposed by TGbh should be extended to cover different scenarios on MLD .
  To identify the frames from a certain non-AP MLD with single MAC address. e.g. (ML)probe, MAC address only be carried on MAC header.
  To identify the frames from a certain non-AP MLD with multiple MAC addresses. e.g., Authentication/Association, MAC addresses are carried on both MAC header and ML element.

## Slide 5: Updated Market Context for RCM
Wi-Fi industry focuses on 11be technology with the following aspects:
  Products: Some vendors have already launched several Wi-Fi 7 products.
  Wi-Fi Alliance: Wi-Fi CERTIFIED 7™, based on IEEE 802.11be technology, will be available before the end of Q1 2024. (link: https://www.wi-fi.org/discover-wi-fi/wi-fi-certified-7 )
Moreover...
  Few, if any, silicon vendors are interested in taping out a legacy chipset to implement 11bh solution only.
  With respect to the enhancement of device manageability, the identification issue on non-AP MLD with RCM is still expected to be a pain point for the Wi-Fi industry
Therefore
  We strongly recommend that the 802.11 group addresses the identification issue on non-AP MLD with RCM.

## Slide 6: Non-AP MLD with RCM Standardization Options and Recommendation
Option | Considerations
TG bh | Incompatible with the 802.11be baseline (according to the timeline)
TG me | Rev me does not include .11be, would have to wait for the Rev mf time frame to address it as part of a maintenance project
TG bi | Focus of .11bi is user privacy protection,e.g.,RCM in post-association., a related but separate topic, would disrupt .11bi scope and timeline.
TG be | Would expand the scope of .11be and likely extend the timeline; workload is already very high
Stand Alone New Project | With the .11bh work efforts wrapping up, a focused project as a follow on seems to make sense. Need for tight scope and timeline management
Recommendation is to develop a PAR and CSD for a standalone Task group for the purpose of standardizing Randomized and Changing MAC addresses for MLD

## Slide 7: A successful case:11az to 11bk
11az Timeline
2015-09
2019-03
........
2021-10
2021-11
........
2022-09
2022-10-04
11bk Timeline
2022-9
2022-11
PAR approved
WG letter ballot
SA letter ballot
802 EC Approval
last meeting
11bk PAR and CSD discussion
11bk PAR approve
and post to EC agenda
TGbk first meeting
2023-01
smoothly
switch

## Slide 8: The proposed Timeline between 11bh and 11bX
2021-02
2024-03
2024-07
2024-09
PAR approved
WG letter ballot
SA letter ballot
802 EC Approval
last meeting
11bh Timeline
2023-05
........
2023-11
11bX PAR and CSD discussion
11bX PAR approve
and post to EC agenda
11bX Timeline
smoothly
switch
2024-11
TGbX first meeting
11bX: Randomized and Changing MAC addresses for MLD (R4M)

## Slide 9
THANK YOU 

## Slide 10: reference
[1] 802.11 Timeline
[2] 11-22-771-70-TGaz Motion compendium
[3] 11-22-1070-00-00az-320-MHz-ranging.pptx

## Slide 11: SP
Do you support TGbh group should develop the PAR and CSD of the project “Randomized and Changing MAC addresses for MLD (R4M)”
Note: the project name can be modified.