## Slide 1: Generation elements
Date: 2023-12-15
Authors:

## Slide 2: Abstract
This submission proposes a generic mechanism whereby elements that are found to cause interoperability problems when extended (typically due to faulty implementation by legacy devices) can be extended in a way that avoids these interoperability problems

## Slide 3: Problem
Implementations continually find innovative ways to misinterpret the spec in a way that breaks forward-compatibility
  VHT STAs cannot cope when VHT APs advertise 160M support
  WPA2™ STAs cannot cope when APs advertise more than one AKM suite in the RSNE
  WPA3™ STAs cannot cope when APs advertise more than two AKM suites in the RSNE
  APs cannot cope when STAs advertise more than one octet in the RSNXE
  STAs cannot cope when APs advertise too many extended capabilities
  etc.
… or try to use new features and get it wrong
  STAs implement FT incorrectly and so fail to roam
  etc.

## Slide 4: Towards a solution
New PHY capabilities, and the corresponding (new) MAC capabilities, are already per-generation (HT/VHT/HE/EHT Capabilities element)
An “RSN override” mechanism has been proposed for the “number of AKM suites” problem(s)

## Slide 5: Solution
Introduce a Generation element that can encapsulate any “base” element
If the implementation sees that and knows about that generation, it uses the encapsulated element instead of the “base” element
Can stack Generation elements for a given “base” element; implementation uses the one for the latest generation it knows about
The Wi-Fi Alliance® already defines Wi-Fi generations, which gives a basis to build on

## Slide 6: Example (just an illustration!)
A Wi-Fi 7 or earlier device would just see the base RSNE, and use RSNE 1 (e.g. just one AKM)
A Wi-Fi 8 device would see the Generation element for Wi-Fi 8, and use RSNE 2 (e.g. two AKMs)
A Wi-Fi 9 device would not see a Generation element for Wi-Fi 9, but would see the one for Wi-Fi 8, and use RSNE 2
A Wi-Fi 10 or later device would see the Generation element for Wi-Fi 10, and use RSNE 3 (e.g. three AKMs)

## Slide 7: Additional considerations
Mechanism could be used for transition modes
  E.g. could have done WPA3 on top of WPA2, rather than as WPA3-TM
Mechanism could be used to override only part of an element
  Reduce cost of moral hazard (beacon bloat)
Early testing would help catch interop issues
  Avoid penalising nonbroken implementations
Mechanism would only be used where imperative
  Avoid penalising nonbroken implementations + reduce cost of moral hazard (beacon bloat)
Could be applied to non-infrastructure BSSes
  E.g. TDLS, Wi-Fi Direct®, Wi‑Fi Aware™
Could restrict a given Generation element to a specific generation
  As opposed to that and all subsequent generations (unless itself overridden)
Not necessarily exactly per-Wi-Fi-generation
  E.g. if need to fix the RSNE again for Wi-Fi 8 R2

## Slide 8: Implementation details
Can obviously have multiple Generation elements per generation
Many options for Generation element ID:
  <255 (about 20 available?)
  <255 with extra octet to specify generation
  255 with element ID extension (many available)
  255 with element ID extension and extra octet to specify generation
  vendor-specific element (e.g. WFA), probably with extra octet to specify generation
  The ones without the extra octet are a bit safer (against yet more misimplementation…)
If not vendor-specific, ANA should allocate
  Most requests likely to come from the Wi-Fi Alliance
Could allow >1 encapsulated element per Generation element
Element fragmentation would need slight tweaking
Wi-Fi Generation 7 | 246
Wi-Fi Generation 8 | 249
Wi-Fi Generation 9 | 251
Example

## Slide 9: Straw poll
Generation elements should be developed as a generic mechanism for solving forward-compatibility issues with legacy implementations
Y
N
A

## Slide 10: References
RSN overriding, 23/1857