## Slide 1: Generation elements
Date: 2024-01-11
Authors:

## Slide 2: Abstract
This submission proposes a generic mechanism whereby elements that are found to cause interoperability problems when extended (typically due to faulty implementation by legacy devices) can be extended in a way that avoids these interoperability problems

## Slide 3: Problem
Implementations continually find innovative ways to misinterpret the spec in a way that breaks forward-compatibility
  VHT STAs cannot cope when VHT APs advertise 160M support
  WPA2™ STAs cannot cope when APs advertise more than one AKM suite in the RSNE
  WPA3™ STAs cannot cope when APs advertise more than two AKM suites in the RSNE
  APs cannot cope when STAs advertise more than one octet in the RSNXE
  STAs cannot cope when APs advertise too many extended capabilities
  etc.
… or try to use new features and get it wrong
  STAs implement FT incorrectly and so fail to roam
  etc.

## Slide 4: Towards a solution
New PHY capabilities, and the corresponding (new) MAC capabilities, are already per-generation (HT/VHT/HE/EHT Capabilities element)
  But note this is new capabilities, not fixing forward-compatibility of existing capabilities
An “RSN override” mechanism has been proposed for the “number of AKM suites” problem(s)
  Note this has special considerations related to MitM/downgrade attacks
  The encapsulation proposed here could be used

## Slide 5: Solution
Introduce a Generation element that can encapsulate any “base” element
If the implementation sees that and knows about that generation, it uses the encapsulated element instead of the “base” element
Can stack Generation elements for a given “base” element; implementation uses the one for the latest generation it knows about
The Wi-Fi Alliance® already defines Wi-Fi generations, which gives a conceptual basis to build on
  But other bodies (e.g. 802.11, WBA) could use Generation elements too
  And the WFA might need Generation elements for an R2 too
  So not directly linked to the WFA’s generational numbering

## Slide 6: Example (just an illustration!)
A Wi-Fi 7 or earlier device would just see the base ExtCaps, and use ExtCaps 1 (e.g. 6 octets)
A Wi-Fi 8 device would see the Generation element for Wi-Fi 8, and use ExtCaps 2 (e.g. 8 octets)
A Wi-Fi 9 device would not see a Generation element for Wi-Fi 9, but would see the one for Wi-Fi 8, and use ExtCaps 2
A Wi-Fi 10 or later device would see the Generation element for Wi-Fi 10, and use ExtCaps 3 (e.g. 10 octets)

## Slide 7: Moral hazard
Pandering to broken implementations means there is no pressure to either implement the spec correctly or to fix broken implementations in the field
  Therefore Generation elements should only be used if absolutely necessary
Early testing would help catch interop issues
  Avoid penalising nonbroken implementations (e.g. current WPA3-capable STAs)
  This is basically a WFA problem
Generation elements would contribute to beacon bloat
  Again, Generation elements should only be used if absolutely necessary
  Could override only part of an element, to reduce the cost

## Slide 8: Additional considerations
Mechanism could be used for transition modes
  E.g. could have done WPA3 on top of WPA2, rather than as WPA3-TM
Could be applied to non-infrastructure BSSes/links
  E.g. TDLS, Wi-Fi Direct®, Wi‑Fi Aware™
Could restrict a given Generation element to a specific generation
  As opposed to that and all subsequent generations (unless itself overridden)

## Slide 9: Implementation details
Can obviously have multiple Generation elements per generation
Many options for Generation element ID:
  <255 (about 20 available?)
  <255 with extra octet to specify generation
  255 with element ID extension (many available)
  255 with element ID extension and extra octet to specify generation
  vendor-specific element (e.g. WFA), probably with extra octet to specify generation
  The ones without the extra octet are a bit safer (against yet more misimplementation…)
If not vendor-specific, ANA should allocate
  Requests likely to come from the Wi-Fi Alliance
Could allow >1 encapsulated element per Generation element
Element fragmentation would need slight tweaking
Wi-Fi Generation 7 | 246
Wi-Fi Generation 8 | 249
802.11bk Generation | 251
Example

## Slide 10: Overhead of Generation elements
Example: overriding Extended Capabilities element (element ID 127)
  1 octet ExtCap ID (127), 1 octet length, n octets extcaps
If Wi-Fi 8 Generation element ID is 249 and only ever encapsulate one
  1 octet Generation ID (249), 1 octet length, 1 octet ExtCap ID (127), <don’t need length>, n octets extcaps => 1 octet overhead
If Wi-Fi 8 Generation element ID is 249 and can encapsulate multiple
  1 octet Generation ID (249), 1 octet length, 1 octet ExtCap ID (127), 1 octet length, n octets extcaps => 2 octets overhead
If Generation element ID is 255+254 with extra octet and can encapsulate multiple
  1 octet Extension ID (255), 1 octet length, 1 octet Generation ID (254), 1 octet generation, 1 octet ExtCap ID (127), 1 octet length, n octets extcaps => 4 octets overhead

## Slide 11: Straw poll
Generation elements should be developed as a generic mechanism for solving forward-compatibility issues with legacy implementations
Y
N
A

## Slide 12: References
RSN overriding, 23/1857