## Slide 1: Resolving EPD/LPD inconsistency
Date: 2023-12-15
Authors:

## Slide 2: Abstract
High-level discussion of the concepts behind the terms EPD and LPD, in P802-REVc and P802.11REVme (and possibly 802.1AC), and a suggested direction toward consistency of these concepts.

## Slide 3: Background
Prior 802.11 contributions highlighted EPD/LPD inconsistency
  802. 11-20-0174-01-0arc (“EPD and LPD Terminology Misalignment in IEEE Std 802.1 and 802.11”)
  802.11-20-0245-02-000m (“Corrections to EPD and LPD Terminology”)
  802.11-21-0092-01-0arc (“LLC Theory and Protocol Discrimination”)
Since then:
  EPD and LPD have been stricken from 802.1Q (in 802.1Q-2022)
  EPD/LPD have been discussed in ballot of IEEE Std 802 revision (P802-REVc)
EPD and LPD are also used extensively in 802.11 and in 802.1AC
  802.1AC: mainly in Clauses 12. (Protocol discrimination and media), 13.2 (Wireless LAN convergence function), and B.1.5 (IEEE 802.11 parameter mapping)

## Slide 4: Status
Currently, P802-REVc describes (5.2.2) two methods “used by the LLC sublayer to determine the protocol identifier designating the higher layer protocol to which to deliver an LLC sublayer protocol data unit”:
  EPD: EtherType protocol discrimination (EPD), which uses, as the protocol identifier, the EtherType value made available to the LLC sublayer through the MSAP
  LPD: LLC protocol discrimination (LPD), which uses, as the protocol identifier the LLC address as specified in ISO/IEC 8802-2 or, using a particular form (described in 9.4) of the Subnetwork Access Protocol (SNAP) format, an EtherType
These definitions are confusing, leading to inconsistency with other standards (e.g. 802.11 and 802.1AC). Key points:
If its useful to distinguish these two “methods,” then they should be strictly non-overlapping alternative methods; however, they are not:
  A protocol carrying an EtherType identifier within SNAP is both EPD [per (a)] and LPD [per (b)].

## Slide 5: Example of Inconsistency
IEEE Std 802 says “LSAP addresses and EtherTypes may be encoded as protocol identifiers using Length/Type encoding, as exemplified in IEEE Std 802.3, which uses the value of a Length/Type field to distinguish between EPD and LPD.”
  In other words, Ethernet supports both EPD and LPD
    EPD when the Length/Type field is a Type
    LPD when the Length/Type field is a Length [but may be EPD as well as LPD?]
IEEE Std 802.11-REVme/d4.1 says “As specified in IEEE Std 802, EPD encoding always starts with a Length/Type field that is either a 2-octet length or a 2-octet EtherType”
  In other words, Ethernet uses only EPD, for any value of the Length/Type field

## Slide 6: Two key concepts
Two concepts are essential to the problem:
What is the protocol identifier? (an EtherType or an LSAP address)
  Both of these have unique registries within IEEE for globally-unique assignment
  Both of these are used to distinguish the “higher-layer” protocol that is being carried in the data, and are intended to (in the LLC) demultiplex the data payload to the appropriate higher-layer entity for further processing per its protocol definition
  Note: IEEE Std 802 also specifies a third type of protocol identifier: a private protocol identifier based on an OUI
How is the protocol identifier encoded?
  “802.3 style” using a “Length/Type” field
  “802.2 style”, with no “Length/Type” field
These two concepts are orthogonal. Either protocol encoding is enabled to carry any type of protocol identifier.
The definitions of EPD and LPD currently in P802-REVc do not make a distinction based on either (1) or (2).

## Slide 7: Proposed Direction
P802-REVc should identify the two key concepts and state that they are orthogonal.
If stated clearly, then the concept of EPD and LPD are unnecessary and should be deleted.
802.11 is already written based on the understanding that EPD and LPD are encoding types.
If P802-REVc specifies the two encoding types, then 802.11 could be revised so that EPD and LPD are replaced by those two encoding types
  This would be an easy edit.