## Slide 1: R-TWT protection in 11bn
Date: 2023-12-22
Authors:

## Slide 2: Background
MAP coordinated R-TWT SP protection has been discussed for a long time.
  In this contribution, we provide considerations and proposals on R-TWT SP protection in 11bn.

## Slide 3: Considerations on R-TWT SP protection 11bn
APs of OBSS R-TWT SPs may be not in an ESS. They are just neighboring.
Overlapped R-TWT SPs should be avoided between 2 APs that can hear from each other.
  If there have to be overlapped R-TWT SPs between the 2 APs, C-OFDMA and C-TDMA etc. can be candidate solutions. However, for APs not belonging to an ESS, there may be security issues. Further study is needed.
STAs in a BSS may have different OBSS R-TWT SPs to protect, subject to their locations.
STA12
STA11
AP1
AP2
STA21
AP3
STA31
STA32
STA22

## Slide 4: Proposals on R-TWT SP protection in 11bn
Based on the previous considerations, we propose in a BSS:
  A STA informs its associated AP the OBSS R-TWT SPs to protect. During each of the OBSS R-TWT SPs,
    The STA should not EDCA the channel to protect the OBSS R-TWT SP.
    The AP should not send to the STA to avoid transmission failure.
    The AP may send to another STA that doesn’t inform the OBSS R-TWT SP.
  The AP broadcasts the OBSS R-TWT SPs to protect. During each of the OBSS R-TWT SPs,
    The AP should not EDCA the channel to protect the OBSS R-TWT SP.
    STAs in the BSS should not send to the AP to avoid transmission failure.
  RCPI of the Beacon frame sent by the AP of each OBSS R-TWT SP to protect can be added.
    Spatial Reuse can be studied in further.
  New element to describe protected periods of the OBSS R-TWT SPs can be defined to save signaling overhead.
    Not all information in TWT element are needed.

## Slide 5: Conclusion
For OBSS R-TWT SPs protection, different locations of STAs should be taken into consideration.

## Slide 6: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0226-02-0uhr-coordination-of-r-twt-for-multi-ap-deployment.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-0250-00-0uhr-ap-coordination-with-r-twt.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-0291-00-0uhr-r-twt-multi-ap-coordination.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-1087-00-0uhr-announcement-for-r-twt-coordination.pptx
[5] https://mentor.ieee.org/802.11/dcn/23/11-23-0046-02-0uhr-multi-ap-coordination-for-low-latency-traffic-delivery-usage-scenarios-and-potential-features.pptx
[6] https://mentor.ieee.org/802.11/dcn/23/11-23-1916-00-00bn-r-twt-coordination-in-multi-bss.pptx
[7] https://mentor.ieee.org/802.11/dcn/23/11-23-1952-00-00bn-coordinated-r-twt-for-multi-ap-scenarios-follow-up.pptx
[8] https://mentor.ieee.org/802.11/dcn/23/11-23-2064-00-00bn-sta-assisted-multi-ap-coordination.pptx