## Slide 1: A-MPDU Coexistence Feedback
Date: 2024-01-04
Authors:

## Slide 2: Abstract
This submission proposes a mechanism to mitigate problems with coex during A-MPDU reception

## Slide 3: Problem
A STA might be unable to receive an MPDU in an A-MPDU because of coex issues
If the recipient STA does not ack MPDUs for this reason, the originating STA will typically assume a channel problem and reduce the rate for subsequent transmissions
This worsens the problem, since the consequent increased PPDU duration increases the likelihood of coex collision
In the worst case, the rate is reduced so much that even a single MPDU does not fit between consecutive coex events; as a result data flow stops and the link is dropped

## Slide 4: Solution
Extend the BlockAck frame(s) to carry information to help the originator distinguish between coex issues and channel issues
  Coex issues might include hidden node issues, if these can be identified
Specifically, return
  The number of bad A-MPDU subframe headers / bad MPDU FCSes received
    Can’t be a perfect count of missed MPDUs, since if A-MPDU subframe header is corrupted resync to next header is not guaranteed
    No counting when didn’t even try to receive, due to coex issues
  The cumulative away time during the PPDU

## Slide 5: Possible originator behaviour
If the originator had many MPDUs unacknowledged:
  If the recipient only reported a few bad MPDUs/subframes and a significant cumulative away time, the originator could surmise the recipient was just away due to coex issues for the unacked MPDUs, and use this as a hint not to change the rate
  If the recipient reported many bad MPDUs/subframes, the originator could surmise bad radio conditions, and use this as a hint to rate-adapt
  If the recipient only reported a few bad MPDUs/subframes and a zero or small cumulative away time, or there was no BA, the originator could surmise really bad radio conditions, and use this as a hint to rate-adapt

## Slide 6: Straw poll
BlockAcks should be extended to provide information on bad MPDUs/subframes and cumulative away time for previous PPDU, so that the originator can try to distinguish coex issues from channel issues
Y
N
A