## Slide 1: DPWiFi MATLAB Validation
Date: 2024-01-13
Authors:

## Slide 2
Abstract
During last November’s Doteleven plenary TWI proposed “Dynamic Polarization MIMO Multiplexing and Beamforming” as a candidate PHY for the nascent TGbn standard. TWI has since MATLAB-modelled “DPMXBF” (henceforth “DPWiFi”) for Fixed Wireless Access applications (salient test results presented herein) and conclusively simulation-validated its functionality and performance as posited in Honolulu.

## Slide 3: Proposed DPWiFi PHY
32 IEEE802.11be concurrent, cochannel RF streams
  32x32 MIMO Dynamic Polarization Multiplexing (“DP-32”)
  32x32 MIMO Tx/Rx DLOS/ nLOS/ NLOS Beamforming/Beamsteering
  AP MU-MIMO Tx Multi-beaming
  Client MU-MIMO Rx Interference Cancellation
  Client MU-MIMO Rx NLOS Multipath Recombination
  5-7 GHz UNII Operation
  4096 QAM 5/6
  320 MHz BW
  92.2 Gbps Peak Data Rate
  80 GbE P2P Throughput over a 28 km Free-Space Range
  27 GbE PMP Throughput across a 79 km2 Foliage-obstructed Area

## Slide 4
Proposed DPWiFi TRX Architecture
[HDP] DPWiFi Propagation Channel
[HDP-1] DPWiFi Rx PDMX
stevenlee131
Post-Honolulu enhancements

## Slide 5: DPWiFi for FWA
DPWiFi Fixed WiFi Access Requirements
  FWA propagation channel transfer function [HDP]: n-dimensional “Polarization Space”, n upper bound > 32 32 x 32 DPWiFi (“DPWiFi-32”) posits unrivaled 80 GbE P2P/ 27 GbE PMP Throughput for FWA
  [HDP] is non-singular, deterministic and scalar (i.e., hij = 1, i = j; hij = r, i ≠ j), r varying with [HDP] impairments
  FWA comprises DLOS, nLOS and NLOS links, all susceptible to propagation channel “depolarization” losses Channel Depolarization (“ChDp”, in o) = Rx DPA-incident DPWiFi polarization rotation from the Tx DPA-impressed baseline
    Direct Line of Sight TRXs hampered by atmospheric fog, rain, etc. depolarize by up to 5o
    near Line of Sight TRXs hindered by incompletely-obstructing foliage/ landscape/ structures depolarize by up to 15o
    Non Line of Sight (i.e., reflected/diffracted) TRX due to fully obstructing landscape/ structures/ vehicles depolarize by up to 45o
  Increasing ChDp severely impacts DPWiFi MIMO Demux, rapidly and fatally boosting S’i residual CCI DPWiFi must incorporate comprehensive ChDp compensation to support its otherwise incomparably compelling FWA solution
DPWiFi Fixed Wireless Access (2-Stage) Operation
  DPWiFi (Open Loop) Channel Sounding
    AP broadcasts “Training Packet (T)” to all associated STAs at 1mS intervals
    Each STA processes T, estimates ChDp, determines its actual [HDP], computes [HDP-1] and reconfigures its Rx PDMux to match
  FWA Traffic DPWiFi TRX Normal Data traffic DPWiFi TRX, but with each STA fully compensating for its particular channel impairments

## Slide 6: DPWiFi TRX Validation Plan
Note: See corresponding Validation Test results following

## Slide 7
DPWiFi TRX MATLAB Model
Data Source Generates
1x Training Packet/
1x Data Packet
SPC/Modulators Synthesize
1x Training Stream/
32x Symbol Streams
Tx DPAs Walsh-Polarize
1x Training Stream/
32x Symbol Streams
DPWiFi Channel MIMO-Multiplexes
1x Training Stream/
32x Symbol Streams
Rx DPAs De-correlate
32x M-M Training Streams/
32x M-M Symbol Streams
Rx DPDMux Estimates Channel DPI/
Recovers 32x Symbol Streams
Demodulators/PSC Recover 1x Data Packet
Data Sink Accepts 1x Data Packet

## Slide 8
DPWiFi TRX Model Detail

## Slide 9: DPWiFi TRX Validation
TWI is currently executing the full DPWiFi TRX Validation Plan of Slide 6
However, the key “Will DPWiFi work for FWA?” question has already been settled:
  Validation Plan items 1.15 and 2.15 comprise the most extreme DPWiFi-for-FWA corner case
    I.e., if 320 MHz MCS13 DPWiFi-32 operation under prescribed test conditions functions/performs to spec, then ALL OTHER BW/MCS/MIMO order DPWiFi combinations will ALSO perform to spec
    Ergo, following find
DPWiFi Validation: DPWiFi-32 320MHz MCS13 vs Channel Depolarization

## Slide 10: DPWiFi-32 320 MHz MCS13 TRX Validation- Data
DPWiFi Validation Data
1.1 DPWiFi-32 320MHz MCS13
ChDp = 0.0o

## Slide 11: DPWiFi-32 320 MHz MCS13 TRX Validation- Data
DPWiFi Validation Data
1.2 DPWiFi-32 320MHz MCS13
ChDp = 1.0o

## Slide 12: DPWiFi-32 320 MHz MCS13 TRX Validation- Data
DPWiFi Validation Data
1.3 DPWiFi-32 320MHz MCS13
ChDp = 1.1o

## Slide 13: DPWiFi-32 320 MHz MCS13 TRX Validation-Data
DPWiFi Validation Data
1.4 DPWiFi-32 320MHz MCS13
ChDp = 5.0o

## Slide 14: DPWiFi-32 320 MHz MCS13 TRX Validation-Data
DPWiFi Validation Data
1.5 DPWiFi-32 320MHz MCS13
ChDp = 15.0o

## Slide 15: DPWiFi-32 320 MHz MCS13 TRX Validation-Data
DPWiFi Validation Data
1.5 DPWiFi-32 320MHz MCS13
ChDp = 15.0o

## Slide 16: DPWiFi-32 320 MHz MCS13 TRX Validation-Data
DPWiFi Validation Data
1.6 DPWiFi-32 320MHz MCS13
ChDp = 45.0o

## Slide 17: DPWiFi-32 320 MHz MCS13 TRX Validation- A & C
DPWiFi Validation Analysis
DPWiFi Validation Conclusions

## Slide 18
DPWiFi MATLAB Validation Summary