## Slide 1: AMP Station operation states
Date: 2024-01-11
Authors:

## Slide 2: Abstract
The operation energy states of an AMP station is presented and discussed

## Slide 3: Example of AMP STA operation energy states
The energy source generates supply of energy, and the AMP STA uses it to accumulate energy.
The AMP STA cannot perform RX+TX until its energy becomes high (pp. 1, 2, 3).
Once the AMP STA goes to high energy, it is ready for RX+TX (p. 4)
RX+TX is consuming energy, and the AMP STA is at low energy level when RX+TX is completed (p.5)
Even at low energy, the AMP STA can perform some functions. For example, take measurements, store information, and receive (p. 6). As long as this is possible, the AMP STA is in the ACTIVE Low state
The AMP STA must accumulate energy for the next RX+TX (pp. 6, 7, 8, 9)
In the absence of energy supply, the station goes into no energy state due to exhaustion of energy (p.11)

## Slide 4: Summary
Depending on the accumulated energy, the AMP STA can be in three states:
  NO ENERGY - no action other than energy accumulation
  ACTIVE High energy – any activity
  ACTIVE Low energy – memory retention, sensing, receiving, and other low energy functions
AMP-STA may need time for the energy supply to be ready for RX+TX (Active high energy state)
AMP-STA may or may not be able to support the ACTIVE Low energy state after the RX+TX phase. This may be implementation dependent: either the STA may not support this state at all, or it may be circumstance dependent. For example, the RX+TX phase fully exhausts the accumulated energy.