## Slide 1: Discussion on Target Objectives for IMMW
Date: 2024-01-14
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St 550, San Diego CA 92131 |  | sanggook.kim@lge.com

## Slide 2: Introduction
In the last November meeting, many contributions discussed high level design ways and technical scope for IMMW [1-5]
  All of them have almost identical views
    Leverage Sub-7 PHY design and 11be MLO architecture
  Details are slightly different
    Target objectives and detailed PHY features
In this contribution, we discuss target objectives for IMMW
  Peak data rate
  Latency
  Additional objectives
    Average throughput
    Power consumption

## Slide 3: Peak Data Rate (1/2)
Some contributions sought for peak data rate enhancement by supporting wider bandwidths and/or multiple streams
  [2] recommended bandwidths from 320 MHz to 2560 MHz
  [4] suggested that SU-MIMO be included
On the contrary, other contributions considered restricting the scope and didn’t focus on peak data rate for complexity reduction [1][3][5]
Our view is that IMMW should be developed to support higher data rate which can cover practical use cases in conjunction with sub-7 GHz
  In [6], 10 Gbps for non-AP STA with 2 spatial streams was proposed as one of the UHR objectives
  Examples of data rate [Mbps] for IMMW based on 11ac and 11be PHY designs assuming 4x / 8x upclocking
 | 80 MHz in 11ac |  | 320 / 640 MHz in mmWave |  | 80 MHz in 11be |  | 320 / 640 MHz in mmWave | 
 | 1 SS | 2 SS | 1 SS | 2 SS | 1 SS | 2 SS | 1 SS | 2 SS
16 QAM 3/4 | 175.5 | 351.0 | 702.0 / 1404.0 | 1404.0 / 2808.0 | 216.2 | 432.4 | 864.8 / 1729.6 | 1729.6 / 3459.2
64 QAM 5/6 | 292.5 | 585.0 | 1170.0 / 2340.0 | 2340.0 / 4680.0 | 360.3 | 720.6 | 1441.2 / 2882.4 | 2882.4 / 5764.8

## Slide 4: Peak Data Rate (2/2)
To achieve much higher data rate, we can consider several approaches such as wider bandwidth, more spatial streams and higher modulation
  For example, more or less 10 Gbps data rate can be achieved with 2 SS and 64 QAM 5/6 in 1280 MHz bandwidth
    E.g., 1280 MHz bandwidth can be constructed by applying 16x / 8x / 4x upclocking to 80 / 160 / 320 MHz bandwidth, respectively
  For another example, 2x data rate can be achieved with 4096 QAM 5/6 compared to using 64 QAM 5/6
  Since IMMW is not a standalone Wi-Fi, we need to be careful to determine these PHY features from the complexity and cost viewpoint
    Mandatory sets and whether to define optional configurations need more discussion
Another consideration is there are pros and cons in 11ac and 11be based PHY designs and thus we need further discussion on which one is better
  11ac based PHY design is better in terms of immunity against CFO and phase noise
  Considering future extension, reusing 11ax / 11be PHY may have some benefits
    Various MU transmissions including MIMO and OFDMA may be possible
    Much wider bandwidth and higher modulation may be applicable

## Slide 5: Latency (1/3)
In [7], 1 ms / sub-ms latency was considered to support AR / VR / XR, etc.
  Considering the dense environment in sub-7 GHz, this target may be quite harsh
The mmWave band may be beneficial to achieve latency reduction
  Beamformed transmission and large pathloss nature may enable interference-free transmission
  Whenever latency sensitive traffic arrives, it may be possible to immediately transmit it if a certain channel in the mmWave band is available
Our view is to consider latency reduction as one of the main objectives
  The exact target needs to be discussed
    E.g., worst latency enhancement comparing with using only sub-7 GHz
  There are also several issues to address
    Channel access delay and transmission delay should be coped with
    In addition, transmission recovery methods should be come up with when beamforming is outdated

## Slide 6: Latency (2/3)
To minimize the channel access delay, an efficient channel access method in the mmWave band should be studied
  Existing features such as MLO, TWT/rTWT with modification may enable smooth channel access
  How to apply contention based channel access should be discussed
  Most of the control and managements frames can be exchanged in sub-7 GHz
For readiness of a transmission and a reduction in the transmission delay, we need to simplify and expedite the beamforming training
  It is imperative to perform beamforming in mmWave unlike sub-7 GHz
  Sub-7 GHz may be of assistance to overhead reduction for beamforming training
    Beamforming training can be managed
    Sector candidates can be shortlisted
  Beamforming reciprocity can be exploited as much as possible
    Only transmit or receive sector sweep may be necessary

## Slide 7: Latency (3/3)
When the current mmWave transmission is no longer reliable because of blockage or outdated beamforming, we need an alternative method for transmission recovery and low latency
  How to determine whether the current transmission is reliable or not may be necessary
  Simple beam tracking methods can be considered
  Link transition approach based on MLO can be also defined

## Slide 8: Additional Objectives (1/2)
Average throughput
  Huge amounts of frequency resource and the properties of mmWave band are helpful to average throughput enhancement
  We can consider average throughput enhancement as one of the objectives and the exact target needs to be discussed
    E.g., average throughput enhancement comparing with using only sub-7 GHz
  Similar to the case for latency reduction, collaborative operation between sub-7 GHz and mmWave bands may be one of the most important factors
  Also, supporting high peak data rate may be helpful to average throughput enhancement
  In addition, beamforming accuracy and robustness may be essential
    Beamforming training procedure can be different from that of the latency reduction case
  We can also consider supporting multiple users based on MLO
    Although we may not consider MU transmission in one mmWave link, different links (e.g., sub-7 GHz band(s) + mmWave band(s)) can support different users at the same time
    Using multiple mmWave links may need additional array antennas and implementation while beamforming training may be simple compared to that for the MU case in one link

## Slide 9: Additional Objectives (2/2)
Power consumption
  For handheld devices such as smartphone, tablet, laptop, etc., power consumption issues should be carefully handled
  We can consider power saving as one of the objectives and the exact target needs to be discussed
    E.g., increased rate of power consumption comparing with using only sub-7 GHz
  The most power consuming procedure in the mmWave band may be the beamforming training
    We need a simplified beamforming training method similar to the case for latency reduction while it should guarantee robust performance
  We also need to deal with how to perform power efficient channel access
    E.g., channel access can be managed in sub-7 GHz and STAs can be awake during the assigned period

## Slide 10: Conclusion
We have considered the following topics to discuss the objectives of IMMW
  Peak data rate
  Latency
  Additional objectives
    Average throughput
    Power consumption
We need to be careful to determine main objectives of IMMW for a successful standardization
  We have claimed that it would be better to focus on the support of practical use cases from the perspective of the peak data rate
  We have also recommended to consider latency reduction, average throughput enhancement and power saving as main objectives for IMMW

## Slide 11: References
[1] 11-23-1819-01-immw-integrated-mmwave-design-considerations
[2] 11-23-1878-01-immw-high-level-design-considerations-of-immw
[3] 11-23-1905-00-immw-high-level-thoughts-on-immw
[4] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave
[5] 11-23-2004-00-immw-technical-scope-proposal
[6] 11-22-0046-01-0wng-next-generation-after-802-11be
[7] 11-22-0685-00-0wng-discussion-on-next-generation-wi-fi