## Slide 1: Considerations on Multi-AP Operation - Follow Up
Date: 2024-01-12
Authors:

## Slide 2: Abstract
In PAR of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enhancement, reduce latency, and reduce power consumption for AP, compared to Extremely High Throughput (EHT) MAC/PHY operation.
Multi-AP operation (aka. Multi-AP coordination/transmission) has been discussed as one of the key candidate features to meet the requirement of UHR capability.
In this contribution, we share some considerations on multi-AP operation, including the support of selecting multi-AP transmission schemes and the support of scheduling the multi-AP transmission.

## Slide 3: Recap: Multi-AP Operation [1~8]
Multi-AP operation may include several phases/procedures between overlapping basic service sets (OBSSs).
Multi-AP operation procedures may be performed as long-term or short-term operations:
  Long-term operation: e.g., one or more beacon interval level
  Short-term operation: e.g., one or more transmission opportunity (TXOP) level
The multi-AP transmission may be carried in a multi-AP data transmission phase, preceded by one or more multi-AP coordination phases, including a multi-AP selection phase.
Some multi-AP operation procedures may repeat optionally for follow-up or new transmissions.

## Slide 4: Multi-AP Transmission Scheme Selection
The multi-AP selection phase may include frame exchanges to allow a sharing AP (AP1) to determine whether a candidate shared AP (AP2) may participate in a multi-AP transmission.
However, the existing procedure relies on the sharing AP determining a multi-AP transmission scheme without consideration of whether the selected scheme can be adequately performed by the shared AP.
Solution
  The sharing AP and/or the shared AP may support more than one multi-AP transmission schemes.
  The shared AP (AP2) provides the sharing AP (AP1) a preferred multi-AP transmission scheme.
  The sharing AP may consider the preferred multi-AP transmission scheme when selecting a multi-AP transmission scheme by the sharing AP.
  The sharing AP announces to the shared AP the multi-AP transmission scheme.

## Slide 5: Multi-AP Transmission Scheduling
After a sharing AP (AP1) selects a shared AP (AP2) for a multi-AP transmission, the shared AP may become unavailable before the beginning of the multi-AP data transmission phase. (e.g., AP power saving)
Solution 1: Shared AP Unavailability Window
  The shared AP (AP2) signals to the sharing AP (AP1) an unavailability window, during which the shared AP is unavailable to participate in a multi-AP transmission.
  The sharing AP schedules the multi-AP transmission to avoid the unavailability window of the shared AP.
Solution 2: Multi-AP Transmission Window
  The sharing AP (AP1) signals to the shared AP (AP2) a multi-AP transmission window.
  The shared AP responds the sharing AP a decision of participating or not in the multi-AP transmission window.

## Slide 6: Summary
In this contribution, we shared some thoughts on multi-AP operation. We proposed the method of selecting multi-AP transmission schemes and methods of scheduling the multi-AP transmission.

## Slide 7: Q&A Discussion (Sept. 2023)
C: The sharing AP will give the shared AP some notification. For confirmation frame, it could simplify the case. We don’t need to have confirmation frame. It can help AP2 know it is selected. Multi-AP trigger fame serves the same function.
A: Yes, it could be merged with the multi-AP trigger frame. This is an example shows the selection phase. There may be other examples.

## Slide 8: References
IEEE 802.11-18/1982r1, Consideration on multi-AP coordination for EHT
IEEE 802.11-19/0448r1, Multi-AP transmission procedure
IEEE 802.11-19/1102r0, A unified transmission procedure for multi-AP coordination
IEEE 802.11-19/1129r2, Consideration-on multi-AP coordination
IEEE 802.11-19/1143r3, Efficient operation for multi-AP coordination
IEEE 802.11-19/1895r2, Setup for multi-AP coordination
IEEE 802.11-20/0596r1, AP candidate set follow-up
IEEE 802.11-20/0617r3, Multi-AP operation basic definition
IEEE 802.11-22/1512r0, Multi-AP coordination for UHR
IEEE 802.11-22/1515r0, A candidate feature multi-AP
IEEE 802.11-22/1530r1, Multi-AP coordination for next-generation Wi-Fi
IEEE 802.11-22/1899r0, Multi-AP operation for low-latency traffic delivery follow-up
IEEE 802.11-23/0226r2, Coordination of R-TWT for multi-AP deployment
IEEE 802.11-23/0293r0, Follow-up on TWT-based multi-AP coordination
IEEE 802.11-23/0297r0, R-TWT for multi-AP
IEEE 802.11-23/0860r0, Further thoughts on coordinated-TWT
IEEE 802.11-23/1449r1, UHR SG September 2023 Meeting Minutes