## Slide 1: Multi-AP Coordination for STA (Re)Association
Date: 2024-01-12
Authors:

## Slide 2: Abstract
In PAR of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enhancement, reduce latency, and reduce power consumption for AP, compared to Extremely High Throughput (EHT) MAC/PHY operation.
Multi-AP operation (aka. Multi-AP coordination/transmission) has been discussed as one of the key candidate features to meet the requirement of UHR capability.
In this contribution, we propose a method of multi-AP coordination for STA association transfer operation, including the support of scheduled AP power save mode.

## Slide 3: Background
Existing EHT AP supports some features for power saving.
  Link disablement: AP MLD temporarily disables the link of an affiliated EHT AP;
  Battery-powered mobile AP may also turn off due to power outage.
    For example, mobile AP (MLD), NSTR mobile AP MLD, etc.
  As a result, the number of STAs served by AP may be reduced. Some STAs need to (re)associate with a new AP.
Some features of AP power save mode has been discussed in UHR SG and TGbn [22/0015].
  Scheduled and dynamic power save for APs, listen state [23/0010, 23/1965]
  Unscheduled AP MLD power save [23/0225, 23/1922]
  As discussed, AP power save feature may introduce potential issues, such as STA may experience loss of connectivity, high roaming delay, or loss of synchronization [23/1835].
To support the AP power save mode, it would be beneficial to improve roaming. Smooth roaming, aka seamless roaming which discussed for UHR [22/1910, 23/0170, 23/0231], may be considered leveraging multi-AP operations [23/0295].

## Slide 4: STA (Re)association with Scheduled AP Power Save Mode
AP1 and AP 2 are in different BSSs forming a multi-AP group via a wireless backhaul.
Assuming AP1 is a mobile AP, AP1 is scheduled to transit to a doze state of power save mode or power off. As such, AP1 will become unavailable for serving associated STA1 and STA2 once entering to the doze state.
AP1 may broadcast a beacon frame notifying its unavailability. As STA1 and STA2 receive a beacon frame from AP2 before or after receiving the beacon frame from AP1, STA 1 and STA2 need to initiate (re)association procedures to associate with AP2, respectively.
As a result, delay may be significantly increased by the number of STAs transmitting reassociate request frames to AP2 and receiving reassociate response frames from AP2.

## Slide 5: Multi-AP Coordination for STA (Re)association with Scheduled AP Power Save Mode
AP1 and AP2 may broadcast beacon frames exchanging capability information of supporting STA association transfer capability.
Before transitioning into a scheduled doze state of power save mode or power off, AP1 may send to AP2 a frame requesting (re)association of STA1 and STA2 with AP2.
After receiving the request sent by AP1, AP2 may send to STA1 and STA2 a notification frame informing association transfer of STA1 and STA2 from AP1 to AP2.
Detailed signaling and procedure are TBD.

## Slide 6: Summary
In this contribution, we shared some thoughts of multi-AP coordination for STA transfer operation, including the support of scheduled AP power save mode.

## Slide 7: References
23/0480, UHR proposed PAR, Laurent Cariou (Intel)
22/0015, AP MLD power management, Liwen Chu (NXP)
23/0010, Considerations for enabling AP power save, Alfred Asterjadhi (Qualcomm)
23/1965, Dynamic power save follow up, Alfred Asterjadhi (Qualcomm)
23/0225, Considering Unscheduled AP Power Save, Guogang Huang (Huawei)
23/1922, Multi Link SM Power Save Mode, Jason Yuchen Guo (Huawei)
22/1910, Seamless Roaming for UHR, Duncan Ho (Qualcomm)
23/0170, Smooth roaming discussion, Liwen Chu (NXP)
23/0231, Thoughts on Seamless Roaming Under the Non-collocated AP MLD Architecture, Guogang Huang (Huawei)
23/0279, Considerations on Seamless Roaming, Insun Jang (LG Electronics)
23/0295, Discussion on Multi-AP Coordination, Xiaofei WANG (InterDigital)