## Slide 1: Efficient Coordinated Spatial Reuse Follow Up
Date: 2024-01-15
Authors:

## Slide 2: Abstract
In [1], we proposed an efficient C-SR protocol that doesn’t require the Sharing AP or Shared AP to collect RSSI reports from STAs or other APs.
In this contribution, we generalize the initial idea for broader use cases.

## Slide 3: General Procedure for C-SR
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
Interference Measurement
Phase
Interference measurement phase
  The sharing/shared APs measure interference or pathloss to each other’s target STA.
Transmission phase
  Initiated by the sharing AP. The sharing AP controls the transmit power and MCS of the shared APs.
Transmission Phase

## Slide 4: Interference Measurement Phase
An interference measurement phase can be one of the following.
  Beacon RSSI measurement report [3]
  Multi-AP channel sounding [4]
  Coordinated measurement procedure [2]
Regardless of the interference measurement phase, a sharing AP obtains an estimate of cross interference of all APs and STAs participating in the C-SR transmission phase. It uses these estimates to determine the transmit powers of the shared APs.

## Slide 5: Efficient C-SR transmission method (1/3)
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
DL Data Frame
BA
BA
MCS,ARIL
MAP
TF
NDPA*
NDPA*
NDP
NDP
measure X2
measure X1
TP=f(X2,ARIL)
Interference Measurement
Phase
Transmission Phase
The MAP TF implicitly indicate TP for the shared AP by indicating acceptable interference level (ARIL) of its target STA (STA1).
The MAP TF also implicitly indicate the MCS of the shared AP by indicating an estimated interference level of the shared AP target STA (STA2).
  Note: the sharing AP is required to know the Shared AP target STAs.

## Slide 6: Example
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
DL Data Frame
BA
BA
ARIL=-80 dBm
MAP
TF
NDPA*
NDPA*
NDP
NDP
X2 = -70 dBm
TP=ARIL+20-X2= 10 dBm
20 dBm
AP2 – STA1 Pathloss =90 dB
MCS, ARIL
IL = -80 dBm
The example shows how the sharing AP can control the interference of the shared AP without directly indicating the transmit power.
The transmit power of the PPDU (NDP) where X2 was measured needs to be known by AP2. How to signal this is TBD.

## Slide 7: Efficient C-SR transmission method (2/3)
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
DL Data Frame
BA
BA
ARIL
TF*
TB PPDU
measure X2
TP=f(X2,ARIL)
UL TB PPDU transmission
Transmission Phase
In some cases, the Interference Measurement Phase may not be necessary [5]. For example, if a triggered UL transmission is followed by a DL transmission by the sharing AP.
The MAP TF implicitly indicate TP for the shared AP by indicating acceptable interference level (ARIL) of its target STA (STA1).
  Note: the sharing AP doesn’t need to know the Shared AP target STAs.

## Slide 8: Efficient C-SR transmission method (3/3)
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
MAP
TF
DL Data Frame
DL Data Frame
BA
ARIL 1 (or TP1)
ARIL 2 (or TP2)
TF*
TB PPDU
measure X21
measure X22
min(f(X21,ARIL1),f(X22,ARIL2)) or TP1
AP3
(shared AP)
DL Data Frame
measure X31
measure X32
BA
TB PPDU
STA2
(Associated with AP1)
The MAP TF may also indicate explicit transmit powers of shared APs if the sharing AP has recent data of beacon RSSI report from STA 1 and STA 2.
Otherwise, the MAP TF implicitly indicates transmit powers using ARIL of its target STAs.
min(f(X31,ARIL1),f(X32,ARIL2)) or TP2
UL TB PPDU transmission
Transmission Phase

## Slide 9: Conclusion
In this contribution, we gave an update on efficient CSR protocol.
The proposed CSR protocol enables the sharing AP to initiate CSR efficiently without existing RSSI measurements from target STAs.
The efficiency of the protocol relies on implicit indication transmit power for the shared APs using acceptable receive interference parameter.

## Slide 10: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0908-00-0uhr-efficient-coordinated-spatial-reuse.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-0668-02-0uhr-coordinated-measurement.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-1832-00-00bn-multi-ap-coordinated-spatial-reuse.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-0854-00-0uhr-obtaining-obss-channel-information-for-multi-ap-operation.pptx
[5] https://mentor.ieee.org/802.11/dcn/20/11-20-0576-00-00be-coordinated-spatial-reuse-protocol.pptx