## Slide 1: Vendor Specific PHY Signaling
Jan 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Motivation for Standardized PHY-level Vendor Specific Signaling Recap from [1]
Goals:
  Signal the presence of proprietary PHY-layer features in PPDUs to devices in the transmitter’s eco-system
  Avoid confusing devices outside their eco-system by conforming to the 802.11 standard
Stakes are raised with U-SIG
  This needs to support many generations of 802.11 MAC/PHY amendments and many vendors/eco-systems
  Any misuse of reserved fields or VS-redefinition of standardized fields runs the risk that the misuse/redefinition will be exposed in future amendments
The MAC has rich and mature mechanisms for safe feature experimentation, prototyping and deployment
  Vendor Specific (sub)elements, and (Public) Action frames
  Some of these proprietary features didn’t work out, and did not burden the 802.11 standard
  Some of these proprietary features created high value and were returned to 802.11 and have been proposed/accepted as standardized features
    i.e., vendor specific extensions support a rich and healthy 802.11 eco-system
Let’s create a safe environment for PHY experimentation, prototyping and deployment too

## Slide 3: Comment 1 on [1]: Use of BSS Color, STA-ID and Upper Layer Enablement Signaling Suffice
Comment 1: Enabling VS PHY features after VS upper layer negotiation, then distinguishing VS PPDUs/user processing via BSS Color and STA-ID, is a sufficient solution.
Follow-up:
  BSS Color is often disabled with little effort paid towards ensuring local uniqueness. MAPC is likely to exacerbate this issue. Perfect BSS Color isolation is never guaranteed; indeed, co-hosted BSSs should use the same BSS Color.
  STA-ID is set to AID. APs are motivated to use low AIDs to minimize the TIM element length in beacons, so AID collisions (and thence STA-ID collisions) are indirectly desirable (and routine).
  Corollaries:
    Nearby APs with the same BSS Color cannot reliably distinguish non-triggered UL PPDUs by BSS Color and STA-ID
      Problems if they use different VS specific extensions or if some use “validate” VS extensions and the others don’t
    Virtualization is non-robust:
      Co-hosted APs not using MBSSID cannot reliably distinguish non-triggered UL PPDUs by BSS Color and STA-ID
      A device, that is a client of both an infrastructure AP and a P2P AP where the APs use the same BSS Color and select the same STA-ID for the client device, cannot distinguish the transmitter of a DL PPDU.
      Problems if one transmitter uses VS extensions and the other doesn’t (or the device supports more than one VS eco-system)
  These problems might be low probability, but that doesn’t help a specific device while it is experiencing them

## Slide 4: Comment 2 on [1]: This doesn’t address Per-User or TB-PPDU Vendor Specific Signaling
Comment 2: This doesn’t address Per-User Vendor Specific Signaling
Follow-up:
  Agreed: then see updated design in next slides

## Slide 5: Proposal: High-level Requirements for UHR TB PPDU
No identify confusion
  Use upper layer signaling to indicate the Vendor ID
No easy SIG field to use: needs something after user separation
  Which is limiting but apparently unavoidable
Option A:
  A new SIG field after the training for the Data field akin to the VHTSIGB field
Option B:
  Bits 11-15 of Service field
Service field already exists and suffices
Recommendation:
  Option B, unless and until 802.11 unreserves too many bits of the Service field
  To allow implementers enable VS development while remaining in compliance with 802.11, SFD should define that the 11bn amendment permit vendor specific upper layer Signaling between AP and non-AP to unreserve bits 11-15 of the Service field in a UHR TB PPDU sent by the non-AP STA to its AP.

## Slide 6: Proposal: High-level Requirements for UHR MU PPDU
Support one or both of the following:
  VS Common Signaling
  VS Per-User Signaling
Always Present:
  Presence / absence of VS Common Signaling
  Presence / absence of VS Per-User Signaling
VS SIG support (if defined)
  Presence / absence of VS SIG field (etc)
Needed if at least one of VS Common Signaling / VS Per-User Signaling is present
  Vendor ID
LSTF
LLTF
LSIG
RLSIG
USIG
VS SIG
UHR STF
UHR LTF
Data
PE
VS Common Signaling includes:
  Validate (or not)
  VS Common Content
VS Per User Signaling includes:
  Bitmap of users with VS per-user content
    Define N as the number of bits in the bitmap equal to 1
  Bitwidth of per-user content, B
  N*B bits of Per-User Content
UHR SIG
VS Signaling
VS Signaling
A, B
C, D
E
either
0 or 4 usec / 0, 4 or 8 usec

## Slide 7: Summary
It seems unavoidable that vendors will seek to incorporate vendor specific PHY features
  But no current mechanism is guaranteed safe and compliant
We propose a way to future proof the U-SIG field (etc) even when there are vendors that seek to incorporate vendor specific features
  Trivial change for TB PPDU
  Modest change for MU PPDU
    Supports both VS Common Content and VS Per User Content
    The overhead is ~2 bits in the U-SIG field for disinterested vendors
    Various Signaling options are available (see backup):
      4-8 usec VS SIG field after USIG is most powerful for VS Common Content
      UHRSIG (padding, overlength User fields) is most natural for VS Per-User Content
    Plenty of VS bits are available
… for guaranteed, long-term PHY safety and reliable interop even in the presence of VS PHY features

## Slide 8: References
[1] 23/1099, “Vendor Specific SIG field”, Brian Hart (Cisco Systems)

## Slide 9: Strawpoll
Do you agree to add the following text to the 11bn SFD:
  11bn shall define a mechanism for VS Signaling in UHR MU and TB PPDUs.
  The mechanism for VS Signaling in UHR TB PPDUs shall use the Service field.
  The mechanism for VS Signaling in UHR MU PPDUs shall support both Common and Per-User Signaling.
Y / N / A

## Slide 10: Backup

## Slide 11: Optional Feature: VS SIG for early VS Common Signaling
VS-SIG field: traditional SIG design with BCC, 1SS and 20 MHz-duplication:
  Option A: Don’t define a VS-SIG; use UHR-SIG only
  Option B: VS-SIG field with MCS0, 1 OFDM symbol, or
  Option C: VS-SIG field with a small selection of low MCSs and numbers of OFDM symbols
Two parts of U-SIG | Bit | Field | Number of bits | Description
U-SIG-1 | B20 / B20-B21 | VS SIG Info | 1 / 2 | 0: No VS SIG field 1: VS SIG field using MCS0 and 1 OFDM symbol / 0: No VS SIG field 1: VS SIG field using MCS0 and 1 OFDM symbol 2: VS SIG field using MCS1 and 1 OFDM symbol 3: VS SIG field using MCS0 and 2 OFDM symbols
 | B20B21/22-… | Disregard | … | Set to all 1s and treat as Disregard.

## Slide 12: … wherein 26 / 52 bit examples of the potential VS SIG binary fields are:
Hart et al (Cisco Systems)
Bitwidth | Description
9 | Vendor ID
1 | VS Validate
6 | Vendor Specific Content
4 | CRC
6 | Tail
Bitwidth |  | Description
16 | 24 | Vendor ID
1 | 1 | VS Validate
25 | 17 | Vendor Specific Content
4 |  | CRC
6 |  | Tail
26 bits available
(MCS0 in 1 OFDM symbol)
52 bits available (MCS1 in + 1 OFDM symbol or MCS0 in 2 OFDM symbols)
Vendor ID:
      9-bit and 16-bit Vendor IDs are a finite resource and must be limited to genuine silicon vendors - might be assigned judiciously by 802.11 ANA and acclaimed by a WG vote
      24-bit Vendor ID = OUI; allocated in the usual way (no need to support OI)
VS Validate: 0 (continue receiving PPDU whether or not Vendor ID is known), 1 (continue receiving PPDU if Vendor ID known; otherwise just assert CCA busy required for the rest of the PPDU)
Vendor Specific Content = not specified by 802.11

## Slide 13: Signaling in UHR-SIG of MU PPDU
Hart et al (Cisco Systems)
UHR-SIG can carry Common (if present and no VS-SIG) and Per-User Signaling (if present)
Various options are available (for future study):
  Option A: Both VS Common Content and VS Per-User Content in Padding (cleanest)
  Option B: VS Common Content in Common field; VS Per User Content in Padding
  Option C: VS Common Content in Common field; VS Per User Content appended to User fields
  Etc

## Slide 14: Extensions to Receive Procedure for UHR MU PPDU
VS SIG Processing (if defined):
  A UHR STA that receives a UHR PPDU identifies the presence and duration of the VS SIG field
  If the VS-SIG field is present:
    If the VS SIG CRC is bad:
      The STA may stop processing the PPDU or continue to process the PPDU after the VS-SIG field (with unchanged CCA requirements either way)
    Else:
      The STA processes the contents of the VS-SIG field.
VS Signaling Processing
  A UHR STA that receives a UHR PPDU identifies the presence of VS Common signaling and VS Per User Processing
  If neither are present:
    The STA processes the PPDU without VS signaling
  Else:
    The STA extracts the Vendor ID and VS Validate field.
    If the STA understands the Vendor ID
      The STA extracts the VS Common signaling and VS Per User Signaling for the STA and processes the PPDU using the vendor extensions
    Elseif the VS Validate field equals 0
      The STA processes the PPDU without the vendor extensions
    Else (unknown Vendor ID and VS Validate field equals 1)
      The STA stops processing the PPDU (with unchanged CCA requirements)

## Slide 15: Hypothetical MU PPDU Examples where Vendor Specific Signaling is needed for (UL/DL, VS Validate = 0/1):
UL MU PPDU indicates VS Validate = 0 and:
  TX reports it is currently moving at high speed; or not
  TX reports it has extra-low low phase noise / amplitude wander / EVM transmitter; or not
  …
UL MU PPDU indicates VS Validate = 1 and:
  Sends a VS constellation/code rate/FEC
  …
DL MU PPDU* indicates VS Validate = 0 and:
  Sends standardized constellations/code rates/FECs to users outside the ecosystem and VS constellations/code rates/FECs to individual users (or groups of users) within the ecosystem
  …
DL MU PPDU* indicates VS Validate = 1 and:
  Uses an extra-short GI for the Data field
  …
*For when BSS Color and STA-ID are not locally unique; or when the RX HW is virtualized and the RX is in communication with other APs/GOs, etc