## Slide 1: Seamless Roaming Consideration
Date: 2024-01-13
Authors:

## Slide 2: Abstract
This presentation shares our experiences of seamless handover implementation.

## Slide 3: Our Experiences
We have implemented WLAN seamless handover system from 20 years ago.
We would like to share our experiences.
Our system
  L2: IEEE 802.11 WLAN
  L3: Mobile IP

## Slide 4: Mobile IP
Home
Agent
AP1
Correspondent
Node
AP2
Internet
Mobile
Node
Dst: Home Address
Src: Correspondent Node
Home Address
Dst: Home Address
Src: Correspondent Node
Dst: Care of Address
Src: Home Agent
Encapsulate
Care of Address
Dst: Correspondent Node
Src: Home Address
Register Care of Address
Switching AP disrupts communication

## Slide 5: Single Radio Seamless Handover
Mobile Node
Radio
Virtual
Interface
Virtual
Interface
AP1
AP2
APs must be operated on the same channel
Mobile Node (MN) communicates through AP1.
MN finds AP2 and associates with it. (keep using AP1 link)
In certain condition, MN decides to use AP2 link. (implementation dependent)
MN registers its Care of Address to Home Agent.
MN transmits packets to AP2 while MN can receive packets from both AP1 and AP2. This means MN can receive delayed packets from AP1. (No packet losses)
In certain condition, MN decides to disconnect from AP1. (implementation dependent)

## Slide 6: Multiple Radio Seamless Handover
Mobile Node
Radio
Virtual
Interface
Virtual
Interface
AP1
AP2
Same channel
Radio
Virtual
Interface
Virtual
Interface
AP3
AP4
Different channel
Same channel
Multiple radio to support multiple channels.

## Slide 7: Roaming Consideration
Our system have achieved seamless handover on the existing IEEE 802.11 with Mobile IP.
Obviously Mobile IP is a L3 protocol and it does not fit to IEEE 802.11 roaming.
Considering about roaming in a DS,
  TX from non-AP MLD is simple. Just use preferred link.
  RX on non-AP MLD needs notification to DS where the non-AP MLD locates.
    Non-AP MLD can notify its location by transmitting a broadcast frame to DS. (e.g Gratuitous ARP/NDP)
  Seamless roaming can be realized by existing IEEE 802.11.
    Just a non-AP MLD implementation issue.
  Do we need new standards for seamless roaming?

## Slide 8: Reference
H. Morioka, H. Mano, M. Ohmori, M. Ohta, M. Hirabaru, M. Hasegawa, M. Inoue, "Seamless Handover with Wireless LAN, Mobile IP, MISP and PDMA", The 9th International Symposium on Wireless Personal Multimedia Communications, 2006