## Slide 1: Improved Transmit MIMO Beamforming with UEQM
Date: 2024-01-13
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Qijia Liu | Broadcom |  |  | 

## Slide 2: Introduction
Unequal modulation (UEQM), meaning one encoder and different QAM per spatial stream was previously proposed in 11n but not adopted in practice.
In here we review the performance gain of UEQM using the current MCS set (which has widely expanded since 11n)
Simulation assumptions:
  SVD based Tx beamforming
  MIMO Configs: 2x2, 4x2, 4x4
  80MHz
  DNLOS, BLOS
  Including RF impairments
  Gain numbers based on RvR simulation, which uses genie rate selection per channel realization at each SNR point
Why should we expect gains? better QAM matching to the different SNR per stream with SVD based BF especially with higher condition numbers

## Slide 3: Condition Numbers (1)
As seen in the
Simulation
4x4 –
strongest/weakest

## Slide 4: Condition Numbers (2)
As seen in a measurement
campaign in an enterprise
environment with 4x4 ULA half
lambda spacing 36x4 locations

## Slide 8: Summary of Gains and Conclusions
() – median gain
All QAM Combinations | 2x2 Nss-2 | 4x2 Nss-2 | 4x4 Nss-4
80MHz DNLOS | 0.8 - 2.6dB (2dB) | 0.2 - 2dB (0.9dB) | 2.2 - 5dB (3.6dB) Peak goodput gain: 3%
80MHz BLOS | 1.8 - 3dB (2.5dB) | 0.3 - 1.8dB (0.7dB) | 4.6 - 7dB (5.6dB) Peak goodput gain: 7%
Highest gain in square configs 2x2 , 4x4 (higher in 4x4)
 Recommend adopting UEQM in 11bn

## Slide 9: SP #1
Do you agree to support unequal modulation (UEQM) (meaning one encoder and different QAM per spatial stream) for MIMO beamforming in 11bn?