## Slide 1: Robust secondary channel access
Date: 2024-01-04
Authors:
Name | Affiliations | Address | Phone | Email
Yanchun Li | Huawei | Huawei Industrial Base, Bantian, Longgang District, Shenzhen 518129 China |  | liyanchun@huawei.com
Yunbo Li |  |  |  | 
Hassan Omar |  |  |  | 
Notes: November 2012

## Slide 2: Introduction
A number of UHR/11bn contributions have discussed non-primary channel access (NPCA), aka. Secondary channel access (SCA).
This contribution discusses usage scenario of secondary channel access and potential issues. The finding is that coordination among APs and STAs can better address these issues. The proposed solution can utilized idle secondary channel without compromising complexity or cause interference.
March 2024

## Slide 3: Recap secondary channel access
Due to limited BW capability at non-AP STA, or limited power budget, OBSS AP can reduce its transmitting BW to better serve its STA.
The idle secondary channel (S40) can be used by AP1 to improve channel utilization.
March 2024
OBSS AP2’s P40 Transmissions
AP1’s P80
AP1’ S40
AP1’s P80

## Slide 4: Issue in Secondary channel access
Secondary channel access has to be carefully designed. Otherwise, it will make trouble.
OBSS AP2’s P40 Transmissions
AP1’s P80
AP1’ S40
AP1’s P80
AP1
AP2
STA1
(hidden from AP2)
P40 Tx
S40 sensing
P40 Tx
X

## Slide 5: Issues in seconary channel access
When lack of coordination, transmission success probability of a secondary channel access will be low.
March 2024
AP1
AP2
STA1
(hidden from AP2)
P40 Tx
S40 Tx
P40 sensing
X
missed

## Slide 6: Issues in secondary channel access
S40 |  |  |  |  |  | 
P40 |  |  |  |  |  | 
S40-2 |  |  |  |  |  | 
S40-1 |  |  |  |  |  | 
S40-0 |  |  |  |  |  | 
P40 |  |  |  |  |  | 
S40 |  |  |  |  |  | 
P40 |  |  |  |  |  | 
OBSS
Local BSS Tx
Local BSS Rx
  Sync Issue 2: AP on the SCH2 while STA is on SCH1,
  when more than one SCHs for Back-off
Sync Issue 3: ED is not sufficient when PCH of OBSS is on this SCH
Sync Issue 4: Multiple APs and non-AP STAs may content on SCH. Need a simple channel access rule on SCH
Duration Rule/ Maximum number of TXOPs
Sync Issue 1: AP on the SCH while STA is still on PCH
PCH to SCH channel switch time
  Sync Issue 5: If Basic NAV on PCH is short, STA may prefer to stay on PCH for the sake of power saving.
Basic NAV on PCH
Subtype of control frame
PCH=primary channel
SCH=secondary channel
March 2024

## Slide 7: Proposed scheme
Propose that AP1 use explicit frames to notify all STAs. So, the process is in more coordinated way. AP, as initiator, performs concurrent PD on secondary channels to better avoid interference on secondary channel, while STA can be simple and do single primary/secondary channel sensing.
OBSS AP2’s P40 Transmissions
AP1’s P80
AP1’ S40
AP1’s P80
AP2 queries AP1
AP1 respond and indicate to switch to S40. It can prevent local hidden STA to contend on primary channel, also notify STA to go to secondary channel for SCA.
P40 sensing
S40 sensing and Rx
P40 sensing
AP1
STA1
March 2024

## Slide 8: Proposed scheme
To simplify the implementation, AP1’s transmission on secondary channel and primary channel starts simultaneously.
OBSS AP2’s P40 Transmissions
AP1’s P80
AP1’ S40
AP1’s P80
AP2 transmit PPDU to querie AP1
AP1
AP1 transmits PPDU to indicate switching to S40 and also announce NAV on secondary channel.
March 2024

## Slide 9: Conclusions
This presentation proposed an UHR secondary channel access process to improve channel utilization. It increases the robustness of access on secondary channel and resolves hidden node issue.
March 2024

## Slide 10: Reference
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0797-01-0uhr-non-primary-channel-access.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-1288-00-0uhr-non-primary-channel-utilization-follow-up.pptx
March 2024

## Slide 11: Straw Poll 1
Do you agree that 11bn provides a secondary channel access mode to increase channel access efficiency?
  Yes
  No
  Abstain
March 2024

## Slide 12: Straw Poll 2
Do you agree that 11bn provides a robust secondary channel access mode which allows AP to indicate secondary channel access to avoid hidden node issue?
  Yes
  No
  Abstain
March 2024