## Slide 1: Hybrid PPDU and Distribution Bandwidth for DRU
Date: 2024-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
A hybrid PPDU where DRUs and RRUs are used at the same time in a PPDU transmission was discussed [1-5]
We share our view on the hybrid PPDU and also discuss how to support 20 MHz operating STAs in the hybrid PPDU
Meanwhile, in [1][2][5], 160 MHz distribution bandwidth was proposed for DRU
We address a PHY processing issue at both transmitter and receiver sides when 160 MHz distribution bandwidth is applied to a PPDU transmission
We also propose some details on 160 MHz distribution bandwidth

## Slide 3: Hybrid PPDU – Recap & Issue
Most of the contributions [2-5] proposed 160 MHz and 320 MHz hybrid PPDUs and had a similar view on them
  Either DRUs or RRUs are used in 80 MHz
  Distribution bandwidth is 80 MHz for DRU when puncturing is not applied
    Some of the contributions also considered 160 MHz distribution bandwidth in 320 MHz hybrid PPDU [2][5]
  If there is punctured 20 MHz in 80 MHz, 20 MHz and 40 MHz distribution bandwidths are applied to non-punctured 20 MHz and 40 MHz, respectively
There are still some issues to consider as follows
  80 MHz hybrid PPDU & Mandatory support for DRU
  Support for small RRUs in hybrid PPDUs for 20 MHz operating STAs

## Slide 4: Hybrid PPDU – 80 MHz Hybrid PPDU
In addition to 160 MHz and 320 MHz hybrid PPDUs, we also propose an 80 MHz hybrid PPDU
  Either DRUs or RRUs are used in 40 MHz
  Distribution bandwidth is 40 MHz for DRU when puncturing is not applied
  If there is punctured 20 MHz, 20 MHz distribution bandwidth can be applied to non-punctured 20 MHz
The reasons behind our proposal are as follows
  80 MHz is important and widely used for a PPDU transmission
    Note that 80 MHz is the maximum mandatory bandwidth for non-AP STAs
  If the 80 MHz hybrid PPDU is not supported, we cannot support DRU incapable STAs or cannot benefit from DRU since DRU and RRU are not applicable to an 80 MHz transmission simultaneously

## Slide 5: Hybrid PPDU – Mandatory DRU Support
We can consider an alternative to the 80 MHz hybrid PPDU
  If support for DRU is mandatory, we can resolve the issues mentioned in the previous slide
    Since there is no DRU incapable STA, we can always benefit from DRUs for a PPDU transmission
  We propose the followings specifically
    STAs shall support DRUs defined in 20 MHz distribution bandwidth
    STAs except for 20 MHz operating STAs shall support DRUs defined in 40 MHz and 80 MHz distribution bandwidths
Consequently, we suggest either support for the 80 MHz hybrid PPDU or mandatory support for DRU

## Slide 6: Hybrid PPDU – How to Support 20 MHz Operating STAs
We propose to support small RRUs (e.g., 26 / 52 / 106 RRUs) in the hybrid PPDU described in slide 3 for 20 MHz operating STAs
  When there is a punctured 20 MHz channel, 20 MHz distribution bandwidth is possible for DRUs
    20 MHz operating STAs capable of DRU can be supported by DRUs or small RRUs
    20 MHz operating STAs incapable of DRU can be supported by small RRUs
  When there is no punctured 20 MHz channel, 20 MHz distribution bandwidth is not possible for DRUs
    20 MHz operating STAs can be supported by small RRUs regardless of their capability
The reason behind our proposal is as follows
  If large RRUs are only supported in the hybrid PPDU, there is no supporting 20 MHz operating STAs when there is no punctured 20 MHz channel or 20 MHz operating STAs are incapable of DRU
  Note that in a wider bandwidth TB PPDU, 20 MHz operating STAs do not support 242 RRU

## Slide 7: 160 MHz Distribution Bandwidth – Recap
In [1][2], we proposed to support up to 160 MHz distribution bandwidth
  We expect that 160 MHz may be widely used in 11bn
    Even though 11be mandates the support of up to 80 MHz for non-AP STAs, 160 MHz has been included in the certification program since Wi-Fi 5 (R2)
    160 MHz may become more common along with hardware improvement and thus this support can be mandatory for non-AP STAs in 11bn
  In 160 MHz, various kinds of large DRUs are available with a better transmit power gain resulting in higher throughput
DRU Size |  | 26 | 52 | 106 | 242 | 484 | 996
Gain (dB) | 160 MHz | 11.14 | 11.14 | 11.14 | 8.13 | 5.12 | 2.69
 | 80 MHz | 11.14 | 11.14 | 8.13 | 5.12 | 2.69 | N/A

## Slide 8: 160 MHz Distribution Bandwidth – Issue
The current PHY processing is based on 80 MHz and it may be complex to handle 160 MHz distribution bandwidth
  We may need to make 160 MHz processing possible
At the transmitter side, 160 MHz PHY processing may be possible by just bypassing the segment parser
  Basically, the segment parser distributes data bits to each 80 MHz subchannel meaning that RUs larger than 996 RU needs the segment parser to reuse the current implementation
  However, the maximum size for DRU in 160 MHz may be 996, and thus, the segment parser is not required
11bn approved that DRU is applied to TB PPDU meaning that the receiver is AP, and thus, there may be no problem with 160 MHz processing at the receiver as well
  AP schedules TB PPDU and knows 160 MHz channels where DRUs are used
  Hence, in these 160 MHz channels, AP can perform 160 MHz processing without any complicated problem

## Slide 9: 160 MHz Distribution Bandwidth – Proposal
We propose the followings
  11bn supports 160 MHz distribution bandwidth for DRU
  The maximum size of DRU is 996 in 160 MHz distribution bandwidth
  160 MHz distribution bandwidth is supported in a 160 MHz TB PPDU and a certain 160 MHz channel in a 320 MHz TB PPDU as well
    Even in the 320 MHz hybrid PPDU, 160 MHz distribution bandwidth can be supported in a certain 160 MHz channel
  Transmitter and receiver may perform 160 MHz PHY processing in the 160 MHz channel where 160 MHz distribution bandwidth is applied
    One example to perform 160 MHz PHY processing is to bypass the segment parser / deparser

## Slide 10: Conclusion
We have shown our view on 80 MHz hybrid PPDU
  We have proposed to either support the 80 MHz hybrid PPDU or mandate the support for DRUs
  We have also proposed to support small RRUs in the hybrid PPDU for 20 MHz operating STAs
In addition, we have discussed 160 MHz distribution bandwidth
  We have addressed a PHY processing issue for a PPDU using DRUs distributed in 160 MHz
  We have also proposed some details regarding 160 MHz distribution bandwidth

## Slide 11: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  11bn supports 160 MHz and 320 MHz hybrid PPDUs
    Either DRUs or RRUs are used in 80 MHz
    Distribution bandwidth is 80 MHz for DRU when puncturing is not applied
      Support for 160 MHz distribution bandwidth in the 320 MHz hybrid PPDU is TBD
    If there is a punctured 20 MHz channel in 80 MHz where DRUs are used, 20 MHz and 40 MHz distribution bandwidths are applied to non-punctured 20 MHz and 40 MHz, respectively
Y/N/A: //

## Slide 12: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  11bn supports an 80 MHz hybrid PPDU
    Either DRUs or RRUs are used in 40 MHz
    Distribution bandwidth is 40 MHz for DRU when puncturing is not applied
    If there is a punctured 20 MHz channel in 40 MHz where DRUs are used, 20 MHz distribution bandwidth is applied to non-punctured 20 MHz
Y/N/A: //

## Slide 13: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  STAs shall support DRUs defined in 20 MHz distribution bandwidth
  STAs except for 20 MHz operating STAs shall support DRUs defined in 40 MHz and 80 MHz distribution bandwidths
Y/N/A: //

## Slide 14: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  Small RRUs (regular RUs) are supported for 20 MHz operating STAs in a hybrid PPDU
    The RRUs mean existing RUs which are defined in 11ax and 11be
    Exact set of supported small RRUs are TBD
Y/N/A: //

## Slide 15: Straw Poll #5
Do you agree to add the following text to the TGbn SFD?
  11bn supports 160 MHz distribution bandwidth for DRU
Y/N/A: //

## Slide 16: Straw Poll #6
Do you agree to add the following text to the TGbn SFD?
  The maximum size of DRU is 996 in 160 MHz distribution bandwidth
Y/N/A: //

## Slide 17: Straw Poll #7
Do you agree to add the following text to the TGbn SFD?
  160 MHz distribution bandwidth is supported in a 160 MHz TB PPDU and a certain 160 MHz channel in a 320 MHz TB PPDU
Y/N/A: //

## Slide 18: Straw Poll #8
Do you agree to add the following text to the TGbn SFD?
  Transmitter and receiver may perform 160 MHz PHY processing in the 160 MHz channel where DRUs are used and 160 MHz distribution bandwidth is applied
    160 MHz PHY processing means constellation mapper, LDPC tone mapper / BCC interleaver, etc., are performed in a 160 MHz channel without segment parser / deparser
Y/N/A: //

## Slide 19: References
[1] 11-23-1919-01-00bn-dru-proposal
[2] 11-24-0014-00-00bn-further-thoughts-on-dru
[3] 11-23-1988-02-00bn-considerations-on-dru-design-and-application
[4] 11-23-2020-00-00bn-high-level-perspective-on-distributed-tone-ru-for-11bn
[5] 11-23-2200-00-00bn-distribution-bandwidth-of-dru