## Slide 1: Hierarchical Modulation for 802.11
Date: 2024-01-XX
Authors:

## Slide 2: Introduction
UHR PAR seeks to
  Improve reliability of WLAN connectivity
  Reduce latencies
  Increase manageability
  Increase throughput including at different SNR levels
  Reduce device level power consumption
Hierarchical Modulation can address several of the above
  Improve Reliability
  Reduce Latency
  Increase Throughput in interference scenarios

## Slide 3: What we propose
We propose a slight modification in the current QAM mapping. We call it,
  Hierarchical Modulation (HM)
The scheme is agnostic to the existing and proposed 802.11 features such as
  SU-MIMO, MU-MIMO, OFDMA (rRUs, dRUs) etc.
Note: HM is not a technic to improve absolute throughput – but to improve reliability especially under interference

## Slide 4: Hierarchical Modulation : Overview of the Idea An Example of Transmitter Block Diagram
Yellow block combines the 2 data streams and presents to the Mapper
symbol stream
Prepend service field
Append tail bits
Append pad bits
HP-data stream
Scrambler
Conv/LDPC Encoder
Interleaver
Group bits into symbols
Assembly HP & LP data steams
Modulator
/Mapper
Prepend service field
Append tail bits
Append pad bits
Scrambler
Conv/LDPC Encoder
Interleaver
Group bits into symbols
LP-data stream
I
Q
bit processing unit in today’s 802.11 a/g/n/ac/ax/be Transmitter

## Slide 5: Hierarchical Modulation: Features
Bits from two different data streams (PPDUs) are modulated into a single symbol stream.
  High priority (HP) stream
  Low priority (LP) stream
Receivers with “good” reception conditions can receive both data streams, while those with poor reception conditions may only receive the HP stream.
  Typically, the HP stream is of lower bit-rate, but has higher robustness than the LP one.
HP and LP streams can be used for two completely different services.

## Slide 6: Hierarchical Modulation: How it works? (1/2)
Consider a 64QAM modulation as shown in the figure below [1].
  The upper 2 bits are same for a given quadrant.
    Like QPSK modulation
  The lower 4 bits changes within any given quadrant
    Like 16QAM modulation
000100
010100
100100
00
11
01
10
HP - QPSK

## Slide 7: Hierarchical Modulation: How it works? (2/2)
Let’s say we have two data streams which go onto a Symbol (PHY) stream
  Map the 2 bits from data stream-1 to the “MSBs” of the IQ symbol
    QPSK modulation
  Use the 4 bits from data stresm-2 to the “LSBs” of the IQ symbol
    16QAM modulation
  We can have different FEC mechanism for each of these streams.
  To demodulate at the receiver, calculate the LLRs for the 2-MSBs as if it is a QPSK modulation
  Calculate the LLRs of the 4-LSBs as if it is a 64- or 16QAM modulation
    (Option 1) 64QAM demodulation and discard 2-LSBs
    (Option 2) 16QAM demodulation using the two-stage detection (See page 7)
  Run 2 FEC decoders (LDPC and/or Viterbi) and recover the 2 streams.
If the SNR is appropriate, both the streams will be decodable.
  In a noisy environment, the LP stream (16QAM) need not be decodable.
  SNR requirements for decoding this 16QAM signal will be same as that for 64QAM signal.
  In this case only the HP stream will be decodable.

## Slide 8: Transmissions in the presence of interference
If one of the above partitions, e.g., QPSK/16QAM (2nd row) is chosen, the HP stream will have approximately 12dB SNR margin than the LP stream.
HP/LP | Final selected Constellation size | Approx. SNR margin between HP and LP (for same code rate)
QPSK/QPSK | 16QAM | 6dB
QPSK/16QAM | 64QAM | 12dB
16QAM/64QAM | 1024QAM | 18dB
64QAM/64QAM | 4K-QAM | 18dB

## Slide 9: An Example Set of System Parameters
Let’s consider 20MHz, 802.11be, SISO configuration.
  234 data carriers
Let each subcarrier is modulated with 64QAM.
  Let the HP stream is QPSK modulated (within the 64QAM) with code-rate 1/2 (MCS1)
  Let the LP stream is 16QAM modulated (within the 64QAM) with code-rate 3/4 (MCS4)
Therefore
  HP data rate: (1,000,000/16) * 234 * 2 * ½ = 14.625Mbps
  LP data rate: (1,000,000/16) * 234 * 4 * ¾ = 43.875Mbps
  Combined data rate: 14.625 + 43.875 = 58.5 Mbps
Note that the HP stream is more protected than the LP stream at the cost of reduced data rate compared to EHT-MCS 5 (i.e., 64QAM with code rate 2/3)

## Slide 10: Receiver Design Considerations
May use Linear detection (MMSE, ZF) or non-linear detection (ML/near ML)
Consider 64 QAM modulation with QPSK for HP stream
  At the receiver, calculate the LLRs for the 2-MSBs as if it is a QPSK modulation
  Calculate the LLRs of the 4-LSBs as if it is a 64QAM modulation
  Run 2 FEC decoders (LDPC and/or Viterbi) and recover the 2 streams.
for HP stream
  The LP data (The variation among the points in the cloud) has the same effect of white noise
  The HP receivers may operate at a higher noise level, due to LP stream, thus penalizing the HP stream performance.[2]
  This penalty depends on the constellation ratio between HP and LP
  Generally not excessive.

## Slide 11: General Observations on HM
In 802.11 PHY we presently have
  Spatial division multiplexing
    Among Single Users (SU-MIMO)
      Multiple data streams to a single user.
    Among Multiple Users (MU-MIMO)
      Independent data streams to multiple-users
  Frequency division multiplexing
    among single user (OFDM)
      Multiple sub-carriers to a single user.
    Among Multiple Users (OFDMA)
      Independent Resource Units to multiple users.
We propose Modulation Multiplexing
  Among same user (SU – SISO/MIMO)
    HP and LP streams to the same user.
  Among multiple Users
    HP stream to user-1 and LP stream to User 2.

## Slide 12: Applications

## Slide 13: Transmissions in the presence of interference
Let’s say the 2nd Row is chosen
  Send the “Must Reach” PPDUs in HP stream
  HP stream will have about 12dB SNR margin than the LP stream.
  Even if the interference is 12dB above the receiver noise level, HP stream will be reliably received.
Can also be used to gauge the approximate level of interference.
HP/LP | Final selected Constellation size | Approx. SNR margin between HP and LP (for same code rate)
QPSK/QPSK | 16QAM | 6dB
QPSK/16QAM | 64QAM | 12dB

## Slide 14: Multi-User Transmission
Sharing modulation across users
  Example
    Consider STA1 is near and STA2 is far from an AP.
    Let the receive SNR from AP to STA1 is sufficient to support 64QAM transmissions with LDPC ¾ coding.
    Let the receive SNR from AP to STA2 is low
      Only QPSK with convolutional ½ coding is the suitable transmission.
    Let the STA2 is sensitive to transmission delays.
In this example, data stream-1 can be modulated with (16QAM, LDPC ¾ coding) which is addressed to STA1 while data stream-2 can be modulated to (QPSK, Conv. ½ coding). It can be addressed to STA2.
Note: Conventional MU-MIMO may not be effective in this case due to the low SNR at STA2.
AP1
STA1
STA2
SNR= ~20dB
SNR= -~5dB

## Slide 15: More applications
mm-Wave Transmission
  Will experience substantial received-power fading for movements over short distances.
    Human induced fades can range from 18 to 36dB!
    Can last on the order of 10s to 100s of milli-seconds.
    HP/LP architecture can provide more reliability and/or effective throughput.
Latency Sensitive Transmission
  Both time-critical latency sensitive (LS) traffic and ordinary traffic can be scheduled simultaneously using HP/LP architecture.
Unequal Error Protection (UEP)
  Alternative way of enabling UEP is to use the hierarchical modulation

## Slide 16: Summary
We introduced hierarchical modulation and its applications for the improvement of 802.11 systems.
  Transmissions in the presence of interference
  Multi-user transmission
  mm-Wave transmission
  Latency sensitive transmission
  Alternate mechanism for Unequal Error Protection

## Slide 17: Reference
[1] A Brief Introduction: DVB-T Hierarchical Modulation, March 2000
[2] A Hierarchical Modulation for Upgrading Digital Broadcast Systems: IEEE TRANSACTIONS ON BROADCASTING, VOL. 51, NO. 2, JUNE 2005