## Slide 1: NAV Rules in C-TDMA
Authors:
Date: 2024-03-05
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Duncan Ho |  |  |  | 
Giovanni Chisci |  |  |  | 
Sherief Helwa |  |  |  | 

## Slide 2: Introduction
Background
  Previous contributions related to C-TDMA (see [1-10]) have:
    Discussed how EHT’s TXS framework can be extended for C-TDMA
  Some contributions have discussed NAV protection (see [1, 3, 4, 8-10])
In the January 2024 meeting, there were extensive discussions about NAV protection in C-TDMA
Based on the constructive feedback received, this contribution proposes a mechanisms to reduce over suppression in C-TDMA

## Slide 3: C-TDMA Frame Exchange Sequence
High-level Protocol:
  The sharing AP announces the C-TDMA schedule to the shared AP
    via a Schedule Announcement frame
  The sharing AP triggers TXOP sharing with the shared AP
    via a TXOP Allocation frame
  The sharing AP reclaims unused TXOP (if any) from the shared AP
    via a TXOP Return frame
CTR => Control Response

## Slide 4: C-TDMA Frame Exchange Sequence
The Schedule Announcement frame:
  Identifies the shared AP(s) and may identify in-BSS STA(s)
  Identifies the traffic priority for which the shared TXOP is to be used
  Helps shared AP(s) make scheduling decisions
    Unlike TGbe’s TXS framework (where an associated STA uses shared TXOP for p2p), a shared AP needs to identify suitable client(s) to serve during the shared TXOP
      Based on the shared duration and estimated start time of sharing
      Based on the allowed traffic priority
  Helps the shared AP(s) manage in-BSS transmission
    Based on estimated time at which the shared TXOP will be given
      i.e., manage in-BSS STAs hidden to sharing AP’s BSS (details in a later slide)
The TXOP Allocation frame:
  Extension of baseline TXS frame to provide information regarding:
    Exact duration of the shared TXOP
    The traffic priority for sharing
Residual TXOP return (if any) from a shared AP to the sharing AP

## Slide 5: NAV in C-TDMA
The Duration field in the Schedule Announcement frame from AP1 (sharing AP) provides protection until the start of the in-BSS frame that follows the immediate response frame from AP2 (shared AP)
The response from AP2 to the Schedule Announcement frame sets the intra-BSS NAV for its STAs until the start of the in-BSS frame from AP1
The Duration field in the TXOP Allocation frame from AP1 provides protection until the start of the subsequent frame after the immediate response frame from AP2
CTR => Control Response

## Slide 6: Additional Considerations
For successful TXOP sharing, the shared AP must be available to receive the TXOP Allocation frame from the sharing AP
  During sharing AP’s in-BSS transmissions, the medium around the shared AP may get busy if its associated STA(s) hidden to the sharing AP’s BSS access the medium
    The shared AP can’t respond to the sharing AP’s poll to receive the TXOP
      This will lead to wasted sharing opportunity
For successful TXOP return, the sharing AP must be available to receive the TXOP Return frame
  During shared AP’s in-BSS transmissions, the medium around the sharing AP may get busy if its associated STA(s) hidden to the shared AP’s BSS access the medium
    The sharing AP may lose the TXOP

## Slide 7: Employ Baseline Mechanisms
General idea: The APs take proactive steps to protect themselves and successfully receive TXOP sharing or TXOP return
Employ one or more baseline mechanisms in the standards:
  Scheduled UL access via MU EDCA from associated STAs of shared and sharing APs
    MU EDCA Parameter Set element
  RTS enablement for UL access from STAs of shared and sharing APs
    HE Operations element

## Slide 8: Summary
In this contribution, we propose NAV rules for participating APs in C-TDMA to prevent over suppression
We highlighted the use of baseline mechanisms to alleviate hidden node issues in C-TDMA
  Protecting the shared AP during in-BSS transmissions of the sharing AP
  Protecting the sharing AP during in-BSS transmissions of the shared AP

## Slide 9: References
[1] Abhishek Patil and et al. (Qualcomm), “C-TDMA Frame Sequence,” 23/1895r1, Jan 2024.
[2] Yanjun Sun and et al. (Qualcomm), “Considerations on Coordinated TDMA (C-TDMA),” 23/0041r0, Jan 2023.
[3] Dibakar Das and et al. (Intel), “C-TDMA procedure in UHR,” 23/0261r0, Apr 2023.
[4] Yanjun Sun and et al. (Qualcomm), “Follow-up on Coordinated TDMA (C-TDMA),” 23/0739r1, Jul 2023.
[5] Si-Chan Noh and et al. (Newracom), “Considerations on Return TXOP between multiple APs,” 23/1327r0, Aug 2023.
[6] Liwen Chu and etc al. (NXP), “Extended TXOP sharing,” 23/249r1, May 2023.
[7] George Cherian and et al. (Qualcomm), “Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be,” 19/1582r2, Nov 2019.
[8] Dibakar Das and et al. (Intel), “C-TDMA Follow-up,” 23/93r2, Mar. 2024.
[9] Geonhwan Kim and et al. (LG Electronics), “TXOP Protection in C-TDMA,” 24/227r1, Apr. 2024.
[10] Si-Chan Noh and et al. (Newracom), “NAV protection for C-TDMA,” 24/375r0, Feb. 2024.